## Slide 1
EDP – TGbi –Agenda - January 2022
Date: 2022-01-13
Authors:
Name | Affiliations | Address | Phone | Email
Carol Ansley | Cox Communications |  | +1-404-229-1672 | carol@ansley.com

## Slide 2
Abstract
This presentation summarizes 802.11 TGbi’s scope and activities to date. It also covers the expected future timeline.

## Slide 3: TGbi – Enhanced Data Privacy
TGbi is developing a new amendment specifying modifications to the IEEE Std 802.11 medium access control (MAC) specification to develop new mechanisms that address and improve user privacy.
  Devices incorporating IEEE Std 802.11, such as Wi-Fi devices, are ubiquitous and being compliant with IEEE Std 802.11 may not always sufficiently protect users from user tracking and user profiling attacks.
  Work has been done in this area in IEEE Std 802.11aq-2018, but the 802.11 Working Group agreed that it was appropriate for a fresh look at these issues.
  TGbh is working on short-term remediation of MAC address randomization, while TGbi has a wider scope to examine general privacy issues and improvements to the standard.

## Slide 4: TGbi – Enhanced Data Privacy
  Example Use Cases
  Several submissions have identified potential privacy exposures related to post-association MAC addresses.
  The current 802.11 standard requires a station to use the same MAC address continuously during a single association which implies that a person monitoring the air can determine whether or not a certain device has remained associated and thus infer the location of that device’s user.
  A related use case pointed out that in a Smart Home, many IoT devices do not change their MAC address at all, currently. In addition, an IoT device’s function may be inferred by monitoring its traffic. If all of the traffic from a camera, for example, uses the same MAC address, it is not hard to determine when the camera is actively transmitting video and when it is not.

## Slide 5: TGbi – Enhanced Data Privacy
  Next Steps
  The Task Group has completed its call for use cases and issues.
  In the upcoming Interim session, TGbi will motion to close consideration of new use cases and issues, then turn to the development of requirements related to the issues and use cases that have been identified.
  TGbi welcomes participation and submissions from anyone interested in the topic of improving data privacy.

## Slide 6: Timeline
TG use case start: March 2021
Use case completion: January 2022
Features identified: July 2022
LB initial: March 2023
LB re-circ: September 2023
Ballot Pool: May 2024
MDR: May 2024
SA ballot: July 2024
SA re-circ: January 2025
802.11/EC approval: July 2025
RevCom/SASB approval: September 2025

## Slide 7: Organizing Plan
Continuing call for submissions
Submissions can include use cases and/or issue identification
Develop a Use Case/Requirement Document based on submissions
Develop a Draft based on approved features
COMPLETE January 2022

## Slide 8
Amendment Title
Standard for Information technology--Telecommunications and information exchange between systems Local and metropolitan area networks--Specific requirements Part 11: Wireless LAN Medium Access Control (MAC) and Physical Layer (PHY) Specifications-- Amendment: Enhanced service with user privacy protection