## Slide 1: TG bh Identifiable Random MAC Address Discussion - Protection against Spoofing
Date: 2022-01
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
This is a presentation and discussion on “Identifiable Random MAC Address”, IRMA and spoof STA and spoof AP.

## Slide 3: Identifiable Random MAC
  Basic idea:
  First time association:
  STA associates to AP with a random MAC address (IRMA) and indicates support for IRM
  AP requests and receives a private key (IRMK). This IRMK is stored.
  Subsequent associations:
  STA associates with a new IRMA, indicates “Known” and includes an IRM KDF (where IRM KDF is a function of the IRMA and IRMK).
  AP searches through stored IRMKs to find IRMK that produces the same IRM KDF.
  AP then requests a new IRMK. (This step prevents any spoof STA)
  STA sends new IRMK.

## Slide 4: Terms
  Identifiable Random MAC (IRM) : a scheme where a non-AP STA uses identifiable random medium access control (MAC) addresses (IRMA) to prevent third parties from tracking the non-AP STA while still allowing trusted parties to identify the non-AP STA.
Identifiable Random MAC Address (IRMA) – a random MAC address used by a STA using IRM
Identifiable Random MAC Key (IRMK) – a Key used to resolve an IRMA
IRM KDF – function of IRMA and IRMK :
where IRM KDF = HDKF-Expand (IRMK, IRMA, 9)
Note: This is new. The IRMK is reduced from 128 bits to 72. This is sufficient as is shown in following slides.

## Slide 5: IRM element
STA can use “private” address
IRM element sent in Association Request
AP then knows if STA IRMK already known (stored) or not
I have been wondering if setting say bits 1 and 3 could be used to say “Known” AND “frequent caller”. Or such? This could assist in Spoof AP

## Slide 6: Brief Overview of IRM scheme
First time Association to a particular AP
STA produces a random 48-bit MAC address from 46 random bits, plus the “01” local admin.
  Same as any RMA,
  Termed “IRMA”.
  The STA chooses a new random MAC every association, so the TA, the IRMA, changes every time.
STA sends Association Request with an IRM Element with indication set to “Unknown”
  The IRM OKM field is omitted from IRM element
Once associated, AP sends IRMK Request Action frame and STA responds with the IRMK Response frame that includes a random 72 bit key, IRMK. The IRMK is then the identity for the STA and is stored by the AP

## Slide 7
Re-Associations to the same AP
STA produces a random 48-bit MAC address from 46 random bits, plus the “01” local admin. - IRMA
STA then calculates a 72-bit OKM, the IRM OKM, using the 72-bit private key, IRMK, that is stored at that AP.
  IRM OKM = HDKF-Expand {IRMK, IRMA,9}.
STA sends Association Request with an IRM Element that includes the IRM OKM, and an indication to the AP that the STA is “Known” i.e., the AP has the private key IRMK.
  Also can include the IRMK Check field (enables AP to down select keys by a factor of 256)
As STA is “Known”, AP can search through its store of IRMKs to find the one that, together with the IRMA (i.e. the TA from the STA), produces the same IRM OKM value that is in the IRM element. Thus, the STA is identified.
Once associated, AP sends IRMK Request Action frame and STA responds with a new IRMK. The IRMK is then the new identity for the STA and is stored by the AP.
  Changing IRMK renders any attack by a spoof STA or third party trying to determine the IRMK, completely moot. See later.

## Slide 8: IRMK Check field
STA can add an IRMK Check field to the IRM element that allows AP to down-select IRMKs if it has many IRMKs stored.
AP can request the IRMK Check to down select IRMKs if not included in IRM Element
IRMK Offset takes a value N, from 0 to 56 (Note: IRMK is 72 bits)
The Check field contains the 8 bits representing the EX-OR of the 8 bits of the IRMK, bN to bN+7 with the following 8 bits (bN+8 to bN+15)
i.e. For n = 0 to 7 Bits in Check field are bn = EX-OR (bN+n, bN+n+8) where bN is Nth bit in IRMK
Acts as a “Hint” to the AP so AP can quickly find a stored IRMK.
Reduces the list of IRMKs by 1/256
e.g., correct key in a list of 1000 IRMKs found with just 2 calculations
Note that 256 combinations of the 16 bits satisfy the 8 bit Check field.
Reduces the integrity of key from 72 bits to 64 bits

## Slide 9: Spoof STA attack
Scenario:
  Rogue STA copies the association of the ‘real” STA
    IRMA and IRM OKM
  Rogue associates to AP (worse case, it knows the password)
    Indicates “Known”
What happens:
  AP does not find the IRMK that complies and will request an IRMK (with reason “No IRMK found”)
Why?
  When the ‘real’ STA associated with that IRMK, it was recognized by AP and then a new IRMK was issued.
Result:
  Rogue STA cannot masquerade as the real STA.

## Slide 10: Third Party snooping
Scenario:
  Third party captures the IRMA and IRM OKM
  Third party brute strength calculates IRMK, (unlikely but let’s assume)
      72 bit IRMK, 263 = 9.22 x 1018 1 day = 8.64 x 1016 tera OKMs (see note)
      hence, about 100 days at 1 terahash/sec
    Rogue STA tries to associate using an IRMA and a correct IRM OKM
What happens:
  AP does not find the IRMK and might request an IRMK (with reason “No IRMK found”)
Why?
  When the ‘real’ STA associated with that IRMK, it was recognized by AP and then a new IRMK was issued.
Result:
  Rogue STA cannot masquerade as the real STA even if it found the correct IRMK from a previous association.
Note: 263 assumes the IRMK Check was included

## Slide 11: AP Spoof
Scenario (assume AP has all the correct credentials)
  Rogue AP spoofs an AP that is attractive to the “real” STA
  STA decides to associate
STA indicates “Known” or “Unknown”
  What happens:
    AP accepts association and sends IRMK request
    STA sends a new IRMK
  Result:
    AP has an IRMK for that STA.
  Discussion
    No different than STA associating not using IRM
    Only if rogue AP spoofs a “known” AP, if STA goes back to the “known” AP, it will not be recognized and STA will receive request for new IRMK.
    STA has not disclosed any device or user information, but presumably spoof AP could interrogate it.
    This is only a “problem” if STA associates i.e., AP has all the right credentials.
    BUT……

## Slide 12: Method to prevent/reduce Spoof AP attack
IF this Spoof AP were considered a real threat, then an IRMK Check could be added to the AP IRMK Request frame
Once associated as “Known” AP sends IRMK Request
  It is assumed that the AP has recognized the IRMK for the STA
  If “IRMK Check” field is added, then STA can check that the AP has the correct IRMK.
  Obviously the spoof AP cannot do this so it has to revert to sending New IRMK Request, with a reason “No IRMK found”.
  Up to STA whether to provide new IRMK or not
    Based on time since last visit? Type of AP/network? Never?
    If suspicious disassociate?
    Does it matter? IRMK has no information.

## Slide 13: Spoof AP discussion
This spoof AP case is only a problem if the STA actually associates.
  Not easy to do such an AP unless open or advertised Password.
If the STA does not associate the IRMK is unchanged
  Spoof AP has learn nothing about the STA.
Worse case is that the IRMK is wrong when STA goes back to the ‘Real’ AP.
  Assumes spoof AP has same address as ‘real’. Unlikely, tends to be based on SSID.
  STA would receive a New IRMK request worse case.
Is the problem enough to add the IRMK Check to every IRMK Request? At the moment I don’t think so, but could be done easily if others felt that AP Spoof is a real problem.

## Slide 14: Summary and Conclusion
Spoof STA is not a problem.
Is a Spoof AP a real life threat?
  Spoof AP is only a problem if STA associates. ( STA might associate with or without IRM, and decision to associate has nothing to do with IRM)
  IRMK is only a temporary ID.
  Spoof AP is not doing this to find out the IRMK, it is doing it to interrogate the STA.
  Spoof APs are not easy to set up.
  Would STA see it just as an “attractive AP”? If so, not lose the IRMK.
Conclusion
  Adding IRMK Check to the IRMK Request restricts spoof AP to having to request a new IRMK with a reason.
  Personally in two minds whether to add this. Adding Check does provide a firm indication that the correct IRMK has been found and causes spoof AP to ask for a New IRMK. Which is always suspicious.
  Easy to add. IRMK Request is only 2 octets at the moment and would only become 4.

## Slide 15
  Interested to hear opinions on the Spoof AP case
  Is it real?
  As IRMK changes all the time, and is a ID only for the next association, does it matter?
  Associating to the spoof AP has nothing to do with IRM, but if AP admits it does not have the IRMK, it does provide some level of protection.
  Adding the Check does provide a positive acknowledgment that the AP knows the STA. Which may be a good thing in itself. (I did consider this from the onset so maybe I start to lean back that way).
  Only consideration is what to do if the IRM Check is not right (assuming a real AP could that happen)?
  A spoof AP would automatically avoid Check and send the New IRMK Request. Back to so what?
Have prepared two version of the IRM text:
  With IRMK Check in IRMK Request
  Without IRMK Check in IRMK Request