## Slide 1: Initial Privacy Enhancement Requirements
Date: 2022-03
Authors:

## Slide 2: Abstract
Proposal: We propose consider 11bi as two sets of features
  Client Privacy Enhancements (CPE) preventing identification & tracking of the Client
  BSS Privacy Enhancements (BPE) preventing identification & tracking of the whole BSS (AP+Clients). Extends CPE
We propose 5 CPE & 5 BPE Features addressing issues 1) to 7) from [1]:
  CPE: SAE Password ID and PMKID obfuscation, Client fingerprinting resistance, Client OTA MAC Address randomization, Client’s Private DS MAC Addresses, SA/DA hidden OTA
  BPE: SSID obfuscation, AP fingerprinting resistance, BSSID (AP’s OTA MAC Address) randomization, AP’s Private DS MAC Addresses, SA/DA hidden OTA
We propose requirements covering the 5 CPE & 5 BPE Features, for [2]
Our approach is that the all 11bi features are optional and other organizations can decide when they are mandatory.

## Slide 3: Terminology (for this presentation)
Abbreviation Meaning
Client non-AP STA or (non-AP MLD with affiliated STAs)
AP AP or (AP MLD with affiliated APs)
PE Privacy Enhancements = Features specified by 11bi
CPE Client Privacy Enhancements
BPE BSS Privacy Enhancements
CPE Client (AP) CPE-capable Client (AP)
BPE Client (AP) BPE-capable Client (AP)
Legacy Client (AP) non-11bi Client (AP)
OTA MAC Address MAC Address used in TA and RA
DS MAC Address MAC Address used to route messages in the DS

## Slide 4: Two set of PE Features
Client PE (CPE) features
  Prevents id and tracking of individual CPE Clients when used with CPE AP.
  (Mostly) coordinated/managed by CPE Client.
  Can a BSS with Client PE features also support seamless legacy connections? Hope “yes”
BSS PE (BPE) features
  “AP Privacy” Use cases. Builds on & extends CPE features
  Prevents id & tracking of entire BSS (BPE AP + associated BPE Clients).
  Coordinated/managed by BPE AP
  Can a BSS with BSS PE features also support seamless legacy connections? Unclear
    Legacy Clients will permit tracking BSS

## Slide 5: CPE and BPE Feature Summary
Client PE (CPE)
BSS PE (BPE)
Feature ID | Client PE (CPE) Features | Issue
CPE-A | SAE password ID & PMKID obfuscation | I1, I5
CPE-B | Client Fingerprinting resistance Minimal IE in Probe Request. (Re)Assoc Request/Response encrypted | I2
CPE-C | Client OTA MAC Address (TA/RA) randomization Simultaneously change AID, SN & PN (both directions) | I3
CPE-D | Private Client DS MAC Addresses | I3
CPE-E | SA/DA Obfuscation | I4
Feature ID | BSS PE (BPE) Feature | Issue
BPE-A | SSID, SAE password ID & PMK obfuscation | I6
BPE-B | AP Fingerprinting resistance Minimal IE in Beacon and Probe Response. (Re)Assoc Response encrypted | I2, I6
BPE-C | BSSID (TA/RA) Randomization Simultaneously change AID, SN & PN (both directions) | I6, I7
BPE-D | Private AP DS MAC Address | I6
BPE-E | SA/DA hidden OTA | I6
TGbi Proposed Issues [1]
I1: Protecting Password Identifiers
I2: Avoid Element Fingerprint
I3: STA MAC address persistence within an ESS
I4: Tracking SA & DA OTA
I5: Protecting authentication identifiers and key identifiers
I6: Mobile AP Privacy
I7: Protecting behavioral fingerprinting while associated
I8: PHY/RF related privacy

## Slide 6: Client PE Feature Requirements

## Slide 7: Feature CPE-A (1/2): SAE password ID obfuscation
See Issue 1) Protecting Password Identifiers
  SAE Password ID is transmitted by the Client in the clear
  Risk: Eavesdropper observes SAE Password ID and uses that value to either uniquely identify the Client or identify the Client as belonging to the set of Client using that SAE Password ID (alternatively, using the identical SAE password credential).
  Goal of countermeasure: prevent adversaries from using SAE password ID to determine if two Clients are using the identical SAE password credentials.
Requirement:
CPE-A-1: 11bi shall define a mechanism to prevent an eavesdropper distinguishing whether authentication exchanges between CPE Clients and CPE APs use identical SAE credentials or distinct SAE credentials

## Slide 8: Feature CPE-A (1/2): PMKID Obfuscation
See Issue 5) Protecting authentication identifiers and key identifiers
  Background: Following full association, , PMKID is transmitted by the Client in the clear prior every time the Client reassociates (until the Client performs another association) to identify the PMK.
  Risk: Eavesdropper observes PMKID and uses that value to track the Client as it reassociates to other APs.
  Goal of countermeasure: prevent adversaries from using PMKID to determine if reassociations between CPE Clients and CPE APs are using identical PMK.
Requirement:
CPE-A-2: 11bi shall define a mechanism to prevent an eavesdropper distinguishing whether reassociation exchanges between CPE Clients and CPE APs use identical PMK or distinct PMK.

## Slide 9: Feature CPE-B: Client Fingerprinting
See Issue 2) Avoid Element Fingerprint
  Background: Elements are transmitted unprotected in Probe Request/Response.
  Risk: Eavesdropper observes Elements in Probe Request/Response to develop an “Element Fingerprint” which can be used to identify or track a Client.
  Goal of countermeasure: Prior to Authentication only essential Elements are transmitted in Probe Request/Response. After Authentication, the transmission of remaining Elements in (Re)Association Request/Response is protected.
Requirements:
CPE-B-1: 11bi shall define a minimal set of Elements for transmission by a CPE Client in a probe request prior to authentication.
CPE-B-2: 11bi shall define a mechanism for a CPE Client and CPE AP to establish keys from an Authentication exchange which can then be used to protect the (Re)Association Request/Response.
CPE-B-3: 11bi shall define a mechanism for a CPE Client and CPE AP to protect the (Re)Association Request/Response.

## Slide 10: Feature CPE-C: Client OTA MAC Address Randomization (1/2)
See Issue 3) STA MAC address persistence within an ESS
  Background: Client OTA MAC Addresses cannot be randomized in the middle of an association or on reassociation.
    Note: 11aq covers other cases where Client can change its OTA MAC Address
  Risk: Eavesdropper can use the Client’s OTA MAC Address to determine that the Client remains associated to an AP. Eavesdropper can use the Client’s OTA MAC Address to determine when the Client reassociates to another AP.
  Goal of countermeasure: allow randomization of the Client’s OTA MAC Address while remaining associated to an AP, or when reassociating to another AP.
Requirements:
CPE-C-1: 11bi shall define a mechanism for a CPE Client to change its own OTA MAC Address when reassociating from a CPE AP to another CPE AP
CPE-C-2: 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in the middle of an Association (Associate STA State 4) without any loss of connection
CPE-C-3: 11bi shall define a mechanism for a CPE AP to initiate seamlessly changing the OTA MAC Addresses of all associated CPE in the BSS Client’s (those CPE Clients in Associate STA State 4) simultaneously without any loss of connection

## Slide 11: Feature CPE-C: Client OTA MAC Address Randomization (2/2)
Related to Issue 3) STA MAC address persistence within an ESS
  Background: SN, PN increase monotonically during an association and transmitted in the clear. AID is transmitted in the clear.
  Risk: If a Client’s OTA MAC Address changes randomly while SN and PN continue increasing monotonically, then eavesdroppers can track Client by observing SN and PN. Similarly, if a Client’s OTA MAC Address changes randomly while AID does not change then eavesdroppers can track Client by observing AID.
  Goal of countermeasure: SN, PN, AID change when Client’s OTA MAC Address changes.
    For future study: should PN change to 0, or change to a random value? If PN change to a random value, also should PN be initialized to a random value on (Re)Association to make it difficult to distinguish mid-association change of MAC Address to change of MAC address due to (Re)Association.
Requirements:
CPE-C-4: 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted SN to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.
CPE-C-5: 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted PN to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.
CPE-C-6: 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection.

## Slide 12: Feature CPE-D: Client’s Private DS MAC Address
See Issue 3) STA MAC address persistence within an ESS
  Background: It is desirable to persist the DS MAC Address for the duration of the association to avoid impacting upper layers. Client DS MAC Address is currently the OTA MAC Address – which no longer is fit for purpose if the Client’s OTA MAC address changes while the Client is associated. Another MAC Address is required.
  Risk: If Client’s DS MAC Address is transmitted in the clear, then the Eavesdropper can use the Client’s DS MAC Address to identify or track the Client.
  Goal of countermeasure: provide a way to keep the Client’s DS MAC Address private.
Requirements:
CPE-D-1: 11bi shall define a mechanism for a CPE Client and CPE AP to establish the CPE Client’s DS MAC Address without the CPE Client’s DS MAC Address being transmitted in the clear.

## Slide 13: Feature CPE-E: SA/DA Obfuscation
See Issue 4) Tracking SA and DA OTA
  Background: SA and DA are currently sent in the clear OTA .
  Risk: This reveals MAC addresses of other Devices used in the DS, identifying OUI of Wired Devices and allowing tracking of CPE Clients.
  Goal of countermeasure: Hide SA/DA.
Requirements:
CPE-E-1: 11bi shall define a mechanism for CPE Clients and CPE APs to transmit and receive the Client’s DS MAC Address in SA and DA in protected form on both the downlink and uplink.
CPE-E-2: 11bi shall define a mechanism for CPE Clients and CPE APs to transmit and receive other DS MAC Addresses in SA and DA in protected form on both the downlink and uplink.

## Slide 14: CPE Requirements Summary (1/2)
Req ID | Requirement | Issue | Status | Information
CPE-A: SAE Password ID and PMKID obfuscation |  | I1, I5 |  | 
CPE-A-1 | 11bi shall define a mechanism to prevent an eavesdropper distinguishing whether authentication exchanges between CPE Clients and CPE AP use identical SAE credentials or distinct SAE credentials (where a CPE AP supports multiple SAE credentials). |  | Proposed | Proposed
CPE-A-2 | 11bi shall define a mechanism to prevent an eavesdropper distinguishing whether reassociation exchanges between CPE Clients and CPE APs use identical PMK or distinct PMK |  | Proposed | Proposed
CPE-B: Client Fingerprinting resistance |  | I2 |  | 
CPE-B-1 | 11bi shall define a minimal set of Elements for transmission by a CPE Client in a probe request prior to authentication. |  | Proposed | Proposed
CPE-B-2 | 11bi shall define a mechanism for a CPE Client and CPE AP to establish keys from an Authentication exchange which can then be used to protect the (Re)Association Request/Response. |  | Proposed | Proposed
CPE-B-3 | 11bi shall define a mechanism for a CPE Client and CPE AP to protect the (Re)Association Request/Response. |  | Proposed | Proposed
CPE-C: Client OTA MAC Address randomization |  | I3 |  | 
CPE-C-1 | 11bi shall define a mechanism for a CPE Client to change its own OTA MAC Address when reassociating from a CPE AP to another CPE AP |  | Proposed | Proposed
CPE-C-2 | 11bi shall define a mechanism for a CPE Client to initiate changing its own OTA MAC Address used with a CPE AP in Associate STA State 4 without any loss of connection. |  | Proposed | Proposed
CPE-C-3 | 11bi shall define a mechanism for a CPE AP to initiate changing the OTA MAC Addresses of all associated CPE Client’s in the BSS (those CPE Clients in Associate STA State 4) simultaneously without any loss of connection |  | Proposed | Proposed
CPE-C-4 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted SN to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection. |  | Proposed | Proposed
CPE-C-5 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted PN to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection. |  | Proposed | Proposed
CPE-C-6 | 11bi shall define a mechanism for a CPE Client and CPE AP to change the CPE Client’s AID to an uncorrelated new value in Associate STA State 4, without any loss of connection. |  |  | 

## Slide 15: CPE Requirements Summary (2/2)
Req ID | Requirement | Issue | Status | Information
CPE-D: Private DS MAC Addresses |  | I3 |  | 
CPE-D-1 | 11bi shall define a mechanism for a CPE Client and CPE AP to establish the CPE Client’s DS MAC Address without the CPE Client’s DS MAC Address being transmitted in the clear. |  | Proposed | Proposed
CPE-E: SA/DA Obfuscation |  | I4 |  | 
CPE-E-1 | 11bi shall define a mechanism for CPE Clients and CPE APs to transmit and receive the CPE Client’s DS MAC Address in SA and DA in protected form on both the downlink and uplink. |  | Proposed | Proposed
CPE-E-2 | 11bi shall define a mechanism for CPE Clients and CPE APs to transmit and receive other DS MAC Addresses in SA and DA in protected form on both the downlink and uplink. |  |  | 

## Slide 16: BSS PE Feature Requirements

## Slide 17: Feature BPE-A (1/3): SSID obfuscation
See Issue 6) Mobile AP Privacy
  Background: SSID is transmitted in the clear by the AP, and used by the Client for discovery.
  Risk: Eavesdropper observes SSID and uses that value to identify the ESS of the AP.
  Goal of countermeasure: allow easy discovery of an ESS’s BPE APs by BPE Clients configured for the ESS, which mitigating easy identification or tracking by an adversary.
Requirement:
BPE-A-1: 11bi shall define a mechanism for a BPE Client to determine which of the BPE Client’s configured networks a BPE AP belongs to (if any), while providing some mitigation against an eavesdropper easily identifying the ESS of the BPE AP.

## Slide 18: Feature BPE-A (2/3): SAE password ID obfuscation
See Issue 6) Mobile AP Privacy
  SAE Password ID is transmitted by the Client in the clear
  Risk: Eavesdropper observes SAE Password ID and uses that value to either uniquely identify the AP or identify the AP as belonging to the set of AP using that SAE Password ID (alternatively, using the identical SAE password credential).
  Goal of countermeasure: prevent adversaries from using SAE password ID to determine if two APs are using the identical SAE password credentials.
Requirement:
The following existing requirement also addresses this feature
  CPE-A-1: 11bi shall define a mechanism to prevent an eavesdropper distinguishing whether authentication exchanges between CPE Clients and CPE APs use identical SAE credentials or distinct SAE credentials

## Slide 19: Feature BPE-A (3/3): PMKID Obfuscation
See Issue 6) Mobile AP Privacy
  Background: Following full association, , PMKID is transmitted by the Client in the clear prior every time the Client reassociates (until the Client performs another association) to identify the PMK.
  Risk: Eavesdropper observes PMKID and uses that value to track the Client when it reassociates to the AP.
  Goal of countermeasure: prevent adversaries from using PMKID to determine if reassociations between CPE Clients and CPE APs are using identical PMK.
Requirement:
The following existing requirement also addresses this feature
  CPE-A-2: 11bi shall define a mechanism to prevent an eavesdropper distinguishing whether reassociation exchanges between CPE Clients and CPE APs use identical PMK or distinct PMK.

## Slide 20: Feature BPE-B: AP Fingerprinting
See Issue 2) Avoid Element Fingerprint & Issue 6) Mobile AP privacy
  Background: Elements are transmitted unprotected by the AP in Beacon frames and Probe Response frames.
  Risk: Eavesdropper observes Elements in Beacon frames and Probe Response frames to develop an “Element Fingerprint” which can be used to identify or track an AP.
  Goal of countermeasure: Prior to Authentication only essential Elements are transmitted in Beacon frames and Probe Response. After Authentication, the transmission of remaining Elements in (Re)Association Responses is protected.
Requirements:
BPE-B-1: 11bi shall define a minimal set of Elements for transmission by a BPE AP in a Beacon frame and Probe Response frame prior to authentication.
The following existing requirements also address this feature:
  CPE-B-2: 11bi shall define a mechanism for a CPE Client and CPE AP to establish keys from an Authentication exchange which can then be used to protect the (Re)Association Request/Response.
  CPE-B-3: 11bi shall define a mechanism for a BPE Client and BPE AP to protect the (Re)Association Request/Response.

## Slide 21: Feature BPE-C: BSSID (AP OTA MAC Address) Randomization (1/2)
See Issue 6) Mobile AP privacy
  Background: BSSID (AP’s OTA MAC Address) is static. Associated Clients’ OTA MAC Addresses might change infrequently.
  Risk: Eavesdropper can use the BSSID to track the BSS (both the AP and the Client’s associated to the AP). Eavesdropper can also use OTAMAC address of associated Clients to track the BSS.
  Goal of countermeasure: allow randomization of the AP’s OTA MAC Address with and without associated Clients. Allow AP to initialize randomization of the associated Clients’ OTA MAC Addresses
Requirements:
BPE-C-1: A BPE AP may change its BSSID while there are no Clients associated.
BPE-C-2: 11bi shall define a mechanism for a BPE AP to facilitate changing its BSSID while there are Clients associated, without disrupting the connectivity from the Clients.
The following existing requirement also addresses this feature
  CPE-C-3: 11bi shall define a mechanism for a CPE AP to initiate seamlessly changing the OTA MAC Addresses of all associated CPE in the BSS Client’s (those CPE Clients in Associate STA State 4) simultaneously without any loss of connection

## Slide 22: Feature BPE-C: BSSID Randomization (2/2)
Related to Issue 6) Mobile AP Privacy
  Background: SN, PN increase monotonically during an association and transmitted in the clear. AID is transmitted in the clear.
  Risk: If a AP’s OTA MAC Address changes randomly while SN and PN continue increasing monotonically, then eavesdroppers can track AP by observing SN and PN.
  Goal of countermeasure: SN, PN change when AP’s OTA MAC Address changes.
    For future study: should PN reset to 0, or reset to a random value? See also requirements CPE-C-4 and CPE-C-5.
Requirements:
The following existing requirements also address this feature
  CPE-C-4: 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted SN to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.
  CPE-C-5: 11bi shall define a mechanism for a CPE Client and CPE AP to change the transmitted PN to an uncorrelated new value on downlink and uplink to new values in Associate STA State 4, without any loss of connection.

## Slide 23: Feature BPE-D: AP’s Private DS MAC Address
See Issue 6) Mobile AP privacy
  Background: It is desirable to have a persistent AP DS MAC Address to avoid impacting upper layers.
  Risk: If AP’s DS MAC Address is transmitted in the clear, then the eavesdropper can use the AP’s DS MAC Address to identify or track the BSS.
  Goal of countermeasure: provide a way to keep the BPE AP’s DS MAC Address private.
Requirements:
CPE-D-1: 11bi shall define a mechanism for a BPE Client and BPE AP to establish the BPE AP’s DS MAC Address without the CPE AP’s DS MAC Address being transmitted in the clear.

## Slide 24: Feature BPE-E: SA/DA Obfuscation
See Issue 4) Tracking SA and DA OTA
  Background: SA and DA are currently sent in the clear OTA .
  Risk: This reveals MAC addresses of the AP and other devices in the ESS, allowing the BSS to be identified or tracked.
  Goal of countermeasure: Hide SA/DA.
Requirements:
The following existing requirements also address this feature
  CPE-E-1: 11bi shall define a mechanism for CPE Clients and CPE APs to transmit and receive the Client’s DS MAC Address in SA and DA in protected form on both the downlink and uplink.
  CPE-E-2: 11bi shall define a mechanism for CPE Clients and CPE APs to transmit and receive other DS MAC Addresses in SA and DA in protected form on both the downlink and uplink.

## Slide 25: BPE Requirements Summary
Req ID | Requirement | Issue | Status | Information
SSID, SAE Password ID & PMK obfuscation Also addressed by Requirements CPE-A-1 and CPE-A-2 |  | I6 |  | 
BPE-A-1 | 11bi shall define a mechanism for a BPE Client to determine which of the BPE Client’s configured networks a BPE AP belongs to (if any), while providing some mitigation against an eavesdropper easily identifying the ESS of the BPE AP. |  | Proposed | Proposed
AP Fingerprinting resistance Also addressed by Requirements CPE-B-2, CPE-B-3 |  | I2, I6 |  | 
BPE-B-1 | 11bi shall define a mechanism for the BPE AP to refrain from transmitting Beacon frames containing elements except TBD element(s). |  | Proposed | Proposed
BSSID randomization. Also addressed by Requirements CPE-C-3, CPE-C-4, CPE-C-5 |  | I6/I7 |  | 
BPE-C-1 | BPE AP may change its BSSID while there are no Clients associated. |  | Proposed | Proposed
BPE-C-2 | 11bi shall define a mechanism for a BPE AP to facilitate changing its BSSID while there are Clients associated, without disrupting the connectivity from the Clients. |  | Proposed | Proposed
AP Private DS MAC Address Also addressed by Requirements BPE-E-1, BPE-E-2 |  | I6 |  | 
BPE-D-1 | 11bi shall define a mechanism for a BPE Client and BPE AP to establish the BPE AP’s DS MAC Address without the CPE AP’s DS MAC Address being transmitted in the clear. This will likely be the same mechanism as used in Req CPE-D-1 |  | Proposed | Proposed
SA/DA Obfuscation: Also addressed by Requirements CPE-E-1, CPE-E-2 |  | I6 |  | 

## Slide 26: Conclusion
We presented a proposal to look at 11bi features in two sets:
  Client Privacy Enhancements (CPE) features and
  BSS Privacy Enhancements (BPE) features
For each of CPE and BPE we outlined 5 features addressing issues 1) to 7).
For the 5 CPE features and 5 BPE features we presented high level requirements
There is overlap between the features and requirements in this document, and those proposed by other contributors.

## Slide 27: References
[1] 11-21-641r7 Proposed Issues
[2] 11-21-1848r2 Requirements Document
[3] 11-21-0109r1 Proposed 11bi Requirements