## Slide 1: TG bh Identifiable Random MAC Address with ID
Date: 2022-01
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Intro
This is a presentation on “Identifiable Random MAC Address”, IRMA combined with the ID Query scheme
Note also that the IRMK is now 72 bits and is changed on every association
  counters spoof STA attack
  Reduces complexity
  Reduces storage

## Slide 3: 802.11 Definitions
  Identifiable Random MAC (IRM) : a scheme where a non-AP STA uses identifiable random medium access control (MAC) addresses (IRMA) to prevent third parties from tracking the non-AP STA while still allowing trusted parties to identify the non-AP STA.
Identifiable Random MAC Address (IRMA) – a random MAC address used by a STA using IRM
Identifiable Random MAC Key (IRMK) – a Key used to resolve an IRMA

## Slide 4: CAPABILITY BIT
An IRM/ID Capability field is used in the STA and AP
The AP looks for the IRM/ID Capability AND the IRM OKM in IRM/ID element
AP can use the IRM/ID Capability bit to indicate to STAs that there may be a reason to be identified, i.e., “I provide a service”

## Slide 5: IRM/ID element
STA can use “private” address
IRM/ID element sent in Association Request
AP then knows if STA IRMK already known (stored) or not, and an ID may also be stored
The IRM OKM field is not present if the IRM Indicator field is set to “Private”, “Private/ID”, “Unknown” or “Unknown/ID".

## Slide 6: IRM/ID Indicator
The IRM OKM field is not present if the IRM Indicator field is set to “Private”, “Private/ID”, “Unknown” or “Unknown/ID".

## Slide 7: Basic Steps for IRM
STA and AP indicates IRM/ID support in Extended Capability Field
First Time Association
STA generates 48 bit IRMA
  Generates a random 46 bit number
  Appends I/G = 0, U/L = 1 (Compatible with 12.2.10)
STA sends the IRM/ID element in Association Request
  IRM Indicator set to “Unknown” or “Unknown/ID
  IRM OKM field is omitted.
After Association, AP requests the IRMK, and STA sends it.
If “Unknown/ID”, AP sends ID Query Request and STA responds with ID Query Response

## Slide 8: STA Re-Associates
Re-Associations
STA generates 48 bit IRMA
STA calculates IRM OKM using the IRMA and the IRMK previously used for that AP
STA sends the IRM/ID element in Association Request
  IRM/ID Indicator set to “Known” or “Known/ID” and IRM OKM is included
  IRMK Check field may be included (Down-selects IRMK list by factor of 256)
AP uses IRMA and stored IRMKs to calculate IRM OKM and identifies the STA IRMK.
AP then requests new IRMK from STA
  This prevents any spoof STA or third party attack
AP and STA update their lists
If “Known/ID” then AP Looks up associated ID that is already stored for that STA.
Note: STA can send an unsolicited ID Query Response.

## Slide 9: IRMK and IRM OKM function
IRMK (Identifiable Random MAC Key)
STA generates the IRMK
  Random 72-bit number .
STA shares IRMK with AP when first associated
STA provides IRM OKM in “IRM element”
The IRMK is used to resolve the identity of the STA
  verifies that the OKM included in the IRM element matches the output of the local OKM computation
  IRM OKM= HKDF-Expand (IRMK, IRMA, 9)
  This produces a 9 octet, 72 bit, output key
Since the AP has the IRMK stored locally and has access to the IRMA (the TA address) and the IRM OKM in the association packet, it can perform this computation and verify the IRMK
NOTE: Only the HKDF-Expand is used because the IRMK is already a “good” pseudorandom key. i.e. the HKDF-Extract is not required.
NOTE: 72 bit key is considered secure enough for this application. Only real need is to prevent duplicates.

## Slide 10: IRM OKM
Proposed to use a single step HMAC-based HKDF (RFC 5869)
IRM OKM = HKDF-Expand (IRMK, IRMA, 9)
The ‘usual’ first step HKDF-Extract, is not required as the IRMK is already a pseudorandom key.
The output keying material (OKM) is a 72 bit key.
IRMK is also 72 bits.
  Only real criteria is that chance of duplicates is low.
  Finding the key does not achieve anything as it is changed every association.
IRM OKM is included in the IRM element only when STA is ‘known’.

## Slide 11: IRMK Check field
IRMK Offset takes a value N, from 0 to 56 (Note: IRMK is 72 bits)
The Check field contains the 8 bits representing the EX-OR of the 8 bits of the IRMK, bN to bN+7 with the following 8 bits (bN+8 to bN+15)
i.e. For n = 0 to 7
Bits in Check field are bn = EX-OR (bN+n, bN+n+8) where bN is Nth bit in IRMK
As an example, IRKM Offset = 42
Check field b0 is EX_OR of bits 42 and 60, and b7 is EX-OR of bits 49 and 67
Acts as a “Hint” to the AP so AP can quickly find a stored IRMK.
Reduces the list of IRMKs by 1/256
e.g. correct key in a list of 1000 IRMKs found in just 2 calculations
Note that 256 combinations of the 16 bits satisfy the 8 bit Check field.
Reduces the integrity of key from 72 bits to 64 bits (see slide 12)

## Slide 12: Action Frames to get IRMK/ID
STA sends “Unknown” or “Unknown/ID” if first time association
AP sends IRMK Request, STA sends IRMK Response with IRMK
AP sends ID Query Request, STA sends ID Query Response
STA sends “Known” or “Known/ID” if STA has previously associated with the AP
AP sends IRMK Request, STA sends IRMK Response with a new IRMK
AP notes the associated ID already established
AP can request New IRMK (with reasons)
STA can send new ID query response
AP can request “IRMK Check” (If many IRMKs stored for example, and Check not present in the IRM element).

## Slide 13: IRMK Check Request/Response
If AP has many IRMKs and STA did not include the IRMK Check field in IRM element, then AP can request it.
Notes:
STA could always includes Check in IRM element
STA could include Check only if it knows the AP is a busy one.
  IF STA recognizes AP as a “busy AP” then STA should include IRMK Check.
IRMK Check reduces the possibilities from 271 to 263
Note: 263 = 9.25 x 1018
Approx 100 days if performing 1 tera hashes per second
Originally proposed 128 it key but realized this was way over the top for what we need. As the STA chooses a new key (IRMK) at every association, brute force determination of the key is of no use. Still nice to have some security and protection against duplicates, and effectively using 64 bits (72 - 8 for the check) is considered completely adequate.
Also reduces the storage to just 9 octets per STA.

## Slide 14: AP requests new IRMK
AP can request a new IRMK (provides reason)
REASON
AP might delete stored IRMKs
  Old
  Capacity
If STA associates as “Known” and IRMK not found, then AP can request a new IRMA (might be seen as a spoof AP)

## Slide 15: Pre-Association
STA can send IRM/ID ANQP-element
AP can use the IRM OKM and the IRMA (TA) to find the IRMK
(Can only be used if AP already has the IRMK)
AP can get the IRMK to identify the STA then can look up the associated ID.

## Slide 16: IRM/ID is very Secure
Every time STA associates, the address IRMA AND IRM OKM values change.
  Impossible to know if same STA associating.
Even if Third party brute strength all keys, IRMK (72 bits, or 68 bits if using IRMK Check), to find the IRMK, as IRMK changes each association, there is no point!!!
Spoof STA copying the IRMA and IRM OKM from an association is not recognized by AP as the IRMK changed after “real” STA associated using these copied fields.
IMPOSSIBLE to know the STA for third parties listening as IRMA and IRM OKM change every time (as does the IRMK)
ID Query can be linked to the IRMK. Does not need to be repeated if associating as ‘known’

## Slide 17: STA details and Storage
IRM enables the AP to identify the STA,
  i.e. STA “123”
  AP stores 9 octets for the IRMK for each STA.
  Changes each association
ID enables the AP to identify the service for the STA
  IRMK changes each association but the ID is constant

## Slide 18
QUESTIONS??

## Slide 19: Straw Poll
Do you agree that an Identifiable Random MAC/ID Query scheme, along the lines as described in <this document>, should be included in the TGbh Amendment?