## Slide 1: Parameters for sub-7 GHz Sensing NDPA
Date: 2022-01-20
Authors:
Name | Affiliation | Address | Phone | Email
Junghoon Suh | Huawei |  |  | junghoon.suh@huawei.com
Mengshi Hu |  |  |  | 
Rui Du |  |  |  | 
Yan Xin |  |  |  | 

## Slide 2: Background
The capability for the Sensing parameters are negotiated during the Sensing Session Set-up phase [1]
It was discussed what sensing parameters need to be negotiated during the Sensing Measurement Set-up phase [2,3]
We try to summarize what parameters are needed for the Sensing NDPA

## Slide 3: Sensing NDPA format
It is not determined how the Sensing NDPA format may be designed yet, however, there have been two directions in Sensing NDPA design [4,5]
  Using the same subtype in the Frame Control field as in the baseline 802.11 NDPA
  Using the different subtype in the Frame Control field from the baseline 802.11 NDPA
Regardless of whichever direction to choose for the Sensing NDPA, there could be Common Info field and STA Info field

## Slide 4: Common Info field
The name of this field is TBD, which can be called a Special STA Info field, NDPA Variant field, Extended Sounding Dialog Token field, etc.
Presence of Common Info field
  Depending on the proposal, this can be TBD bits
  Special STA Info field case: 11bits for dummy AID are needed
Measurement Set-up ID: TBD bits
  In case we need to indicate the different Measurement Set-up ID for each STA listed in the STA Info field, the Measurement Set-up ID can go into the STA Info field
Measurement Instance ID: Sounding Dialog Token Number may play a role of this ID
  6 bits enough (?)
  In case it is necessary to carry more than 6 bits for this ID, this needs to be carried in the Common Info field as well
  In case we need to indicate the different Measurement Instance ID for each STA listed in the STA Info field, the Measurement Instance ID can go into the STA Info field
NDPA Version ID (For future Extension)
  1 byte will be enough
Disambiguation bit: 1 bit every two byte after the first 2 bytes in case of Special STA Info field, for other cases 1 bit every two byte
Reserved subfield for future extension

## Slide 5: STA Info field
AID11: (11bits)
Bandwidth: (9 bits) Indicates the sub-channels CSI FB is required
Number of TX Streams: (4 bits)
Number of RX Streams: (4 bits)
CSI FB Type: (1 or 2 bits) depending on how many options we need for “CSI_ESTIMATE”
  This can be set during the Measurement Set-up
Ng: (2 bits – 8, 16, 32, 64 tones)
Disambiguation: 1 bit per every two bytes after the first two bytes (No need this if we use the different subtype)
Scale Factor: (1 bit – 3 or 6 bits)
CSI FB Bit Size: (2 bits – 6, 8, 10, 12 bits)
TX Power: (2 bits) Impact on the Sensing Range
Number of Taps for TCIR: (6 bits) (TBD)  This can go to the Measurement Set-up frame
Threshold for CSI FB: (4 bits)
Measurement Set-up ID (MSI): (TBD bits) It is needed when the different MSI is needed per STA Info field
Measurement Instance ID (MII): (TBD bits) It is needed when the different MII is needed per STA Info field
Reserved subfield for future extension: TBD bits
Total: 60 to 70 bits are needed

## Slide 6: Summary
We have a Common field and STA Info fields in Sensing NDPA
We may need more than 4 bytes for a STA Info field based on the necessary parameters in Sensing NDPA

## Slide 7: References
[1] 11-20-1851-01-00bf-overview-of-wi-fi-sensing-protocol
[2] 11-21-0365-02-00bf-wi-fi-sensing-parameters
[3] 11-21-2029-01-00bf-definitions-of-some-sensing-operational-parameters
[4] 11-21-1896-02-00bf-ndpa-for-sensing
[5] 11-21-1751-01-00bf-condideration-for-ndpa-in-11bf

## Slide 8: SP 1
Do you agree to have a Common Info field and the STA Info field(s) in the Sensing NDPA?
  The name of the Common Info field is TBD (e.g. alternative name can be Special STA Info field)
  It is TBD how to indicate the presence of Common Info field to distinguish from the incumbent NDPA frames

## Slide 9: SP 2
Do you agree to transmit the Measurement Set-up ID in the Common Info field of a Sensing NDPA?
  Size of Measurement Set-up ID is TBD

## Slide 10: SP 3
Do you agree to carry the following parameters in the STA Info field of the Sensing NDPA?
  Feedback Bandwidth (9 bits)
  Number of TX Streams (3 bits)
  Number of RX Streams (3 bits)

## Slide 11: SP 4
Do you agree to carry the following parameters in the STA Info field of Sensing NDPA?
  Ng: (TBD bits)
  Scale Factor: (TBD bits)
  CSI FB Bit Size: (TBD bits)

## Slide 12: SP 5
Which option do you prefer in transmitting the TX Power (TX Power of the Responder) parameter ?
  Option 1: STA Info field in the Sounding NDPA regardless of TB or non-TB Sounding
  Option 2: Common Info field in the Sounding NDPA for non-TB Sounding and Trigger Frame following the NDP for TB Sounding