## Slide 1: Opaque Device Identifier
Date: 2022-01-20
Authors:

## Slide 2: Abstract
A scheme to have a network-generated device ID is proposed

## Slide 3: Basic Idea
Identifier is assigned by network to STA
  Network owns ID space, decides on format of ID
  Different networks can use different IDs as they wish
To the STA, it’s just a blob
STA obtains a blob on first association
STA includes blob in 4way HS
4way HS updates and produces a new blob that the STA uses on a subsequent association
STA can “opt out” by just throwing away the blob and getting a new one on the next association if it wants to stop being tracked
Requirement: all APs in ESS share a symmetric key

## Slide 4: Converting a Device ID to a Blob
Instance from the network name space is treated as an opaque string– could be a name, a number, anything that is significant to the network
Different networks can use different name spaces
Opaque string is padded, a single octet defines the length of the pad followed by length-1 octets of zero
  Therefore minimum pad is 1 octet, the length indicator
Padded opaque string prepended with a random tweak
  Size of tweak influences security of blob– an 8 octet tweak would secure blobs roughly to a birthday bound of 232
Tweaked padded opaque string is SIV encrypted (deterministic AEAD mode, no IV)

## Slide 5: Generation of Blob
Slide 5
AES-SIV
key
device identifier:
blahfubar
4000blahfubar
padded:
tweaked:
71a08cf14000blahfubar
blob:
891b52f0725635f3abc8a6b13159df5afbf0a

## Slide 6: Handling of the Blob
STA includes blob in message 2 of 4way HS
  First association there is no blob, if missing AP allocates a name out of the name space for the STA
AP decrypts blob, validates tweak, discards padding and tweak
  Failure to decrypt could result in a deassociation if the group desires or it could just be treated as a missing blob
  Failure to validate tweak should result in deassociation
AP makes note that STA MAC is now associated with the identifier
AP re-encrypts identifier with new padding and tweak, stores latest tweak used to encrypt the identifier
AP inserts new blob in message 3 of 4way HS
STA retains new blob for subsequent association to allow tracking and throws it away if it wants to opt out of tracking
AES-SIV decryption and encryption is very fast

## Slide 7: Properties of Scheme
A passive attacker cannot determine a device identity
A passive attacker cannot connect device identities across associations
Identifiers can be arbitrarily padded to foil passive traffic analysis
Identities are secure under a reasonable birthday bound (which will depend on the size of the tweak and the how the pad size varies)
An attacker cannot substitute identifiers to connect distinct associations
An AP needs to only manage a single symmetric secret, used to protect all identities used in the ESS, and 8 octets per allocated device ID
All APs in the ESS can share the same symmetric key (in an out-of-band fashion)
Minimal overhead—e.g. 16 octet tag + 8 octet tweak + 1 octet pad length + padding = 25 octets plus padding
Uses symmetric cryptography for speed and DOS resistance
Each identifier is unique to the ESS it was obtained from, a given ESS will have no knowledge of the identifiers used in other ESSs
Identifiers cannot be tracked across networks

## Slide 8: Use Cases Addressed
Post-association access control
  User identified, access control determined at sign-up/first association
  Blob presented on all subsequent association, connection gets the treatment
  Attempts to access network without a blob can be denied if desired
Post-association home automation
  First association is done at home when opener installed
  Garage door won’t open unless appropriate blob is received
Grocery store frequent shopper notification
  Keep reusing the blob at the store, tie visits to each other
Customer support and troubleshooting
  Require some way to present a blob that could be read back
  891b5-2f072-5635f-3abc8-a6b13-159df-5afbf-0a
  On second thought that might be a lot to read back
Captive portal
  Blob is assigned when guest first goes through captive portal (using OWE, not open)
  Subsequent associations present blob, guest identified, captive portal avoided
Maybe more!

## Slide 9: References
11-21/0488
11-21/0541