## Slide 1: TG bh MAC Address Designation (MAAD MAC)
Date: 2022-02
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Outline
AP shows support for MAAD in Extended Capabilities
  STA does not indicate support. Third party observer does not know MAAD is in use.
STA associates
STA sends MAAD request
  MAD Request Action fame
AP sends MAAD response which is a 48 bit MAC address
  Locally administered
  AP stores the allocated MAAD MAC for that STA
  STA stores the MAAD MAC for that AP
STA comes back and uses the MAAD MAC Address
AP instantly recognizes the STA.
  AP can identify the STA pre-association
STA Associates using the MAAD MAC
STA sends MAAD request and gets a new MAAD response with a new MAC Address
Etc. etc.

## Slide 3: ADVANTAGES
Simple – very simple
  One action frame exchange (short)
  Easily implemented.
  No crypto requirements (post association)
MAAD Address changes every time so no STA spoof
  Also 3rd party cannot tell scheme in use (STA does not indicate support)
AP allocates MAAD MAC Address
  No duplications
  STA can use same MAAD MAC across ESS
AP recognizes STA pre-association
  MAAD MAC in association request and probes.
No calculations required other than AP generating a 48 bit address
  Simple for STA and AP
Meets all the criteria for Use Cases