## Slide 1: TG bh MAC Address Designation (MAAD MAC)
Date: 2022-02
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Outline
AP shows support for MAAD in Extended Capabilities
  STA does not indicate support. Third party observer does not know MAAD is in use.
STA associates
At any time while associated, STA sends MAAD request
  MAD Request Action fame – does not form part of association.
AP sends MAAD response which is a 48 bit MAC address
  Locally administered
  AP stores the allocated MAAD MAC for that STA
  STA stores the allocated MAAD MAC for that AP
When STA comes back it uses the MAAD MAC Address (or not)
AP instantly recognizes the STA from TA.
  AP can identify the STA pre-association – e.g. directed probe
STA Associates using the allocated MAAD MAC as TA
At any time, STA sends MAAD request and gets a new MAAD response with a new MAC Address
  Note that The request/response DOES NOT FORM PART OF ASSOCIATION.
Etc. etc.

## Slide 3: MAAD Action frames
Octets: 1 1
Figure – 9-ccc – MAAD Request Action field format
Category | MAAD Action | MAAD MAC
Category | MAAD Action
Octets: 1 1 6
Figure – 9-ddd – MAAD Response Action field format

## Slide 4: ADVANTAGES
Simple – very simple - Easily implemented.
  No crypto requirements,
  Action frame exchange can take place at any time whilst associated - does not form part of the association
MAAD Address changes every time (if STA so wishes) so no STA spoof possible
  Also 3rd party cannot tell scheme in use (STA does not indicate support)
STA initiates (is in control) BUT AP allocates
  No duplications, easy opt-in opt-out for STA.
  STA can use same MAAD MAC across ESS.
AP can recognize STA pre-association
  MAAD MAC as TA in association requests and probes.
  AP can note from a directed probe that a known STA is within range (e.g. Home Use Case).
No calculations required other than AP generating a 48 bit address
  Simple for STA and AP, easily implemented
Meets all the criteria for Use Cases