## Slide 1: 5/6 GHz coexistence update for IEEE 802.11 TGbe and/or IEEE 802.11 WG for possible presentation in March 2022
24 January 2022
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: Traditional good coexistence in the 5 GHz band was threatened by plans of the cellular industry to use it too
Good coexistence in 5GHz has been enabled within the Wi-Fi industry …
… but this model was threatened by the emergence of new stakeholders
Wi-Fi has traditionally been the main user of the unlicenced 5 GHz band globally
Coexistence between different Wi-Fi systems has been enabled by:
  Standards negotiated within the IEEE 802.11 WG
  Certifications specified by the Wi-Fi Alliance
The process of discussion within the Wi-Fi industry has resulted in (mostly) good coexistence
A few years ago, the cellular industry decided they would also like to make use of the 5 GHz band
  eg 3GPP, MulteFire Alliance, LTE-U Forum, etc
  This was their right … the 5 GHz band was designed for use by all!
However, this required coexistence mechanisms to be agreed by a wider group of stakeholders
  Industries: Wi-Fi & cellular
  Regulators: including in US & Europe

## Slide 3: Difficult negotiations over a period of years resulted in an acceptable compromise for 5 GHz coexistence
The compromise
All systems use an EDCA-like LBT, with exponential backoff, mechanism for access
All systems transmit for a maximum period of time once they gain access
Listening occur using either:
  PD/ED at -82/-62 dBm, as practiced since 1997 by Wi-Fi
  ED-only @ -72 dBm, to avoid need for PD in cellular systems
The negotiation of 5 GHz sharing was heated, over many years …
… but eventually led to an acceptable compromise
LTE-U/Wi-Fi sharing resulted in heated discussions in WFA, FCC & LTE-Forum … and eventually there was a compromise but LTE-U become irrelevant in the market
LAA/Wi-Fi sharing also resulted in heated discussions in 3GPP, IEEE 802 & ETSI BRAN … but ended with a more lasting compromise
The was not much enthusiasm for more heated discussions wrt NR-U/Wi-Fi sharing … and so it piggybacked on the LAA/Wi-Fi driven compromise
The compromise
All systems use an EDCA-like LBT, with exponential backoff, mechanism for access
All systems transmit for a maximum period of time once they gain access
Listening occur using either:
  PD/ED at -82/-62 dBm, as practiced since 1997 by Wi-Fi
  ED-only @ -72 dBm, to avoid need for PD in cellular systems
While not ideal, the compromise was acceptable to all

## Slide 4: The 5 GHz compromise is a regulatory requirement in Europe but is likely to be respected globally
  The eventual coexistence compromise was implemented in:
    IEEE 802.11 standards, with no change required from past practice
    3GPP specs, particularly for LAA and NR-U
  It also become a requirement in EN 301 893, which is the 5 GHz Harmonised Standard for Europe
    The inclusion of the compromise by ETSI BRAN in EN 301 893 was part of the reason it was accepted by 3GPP as an acceptable solution
    EN 301 893 has some regulatory force in Europe, which gave all stakeholders confidence the compromise would be upheld, at least in Europe (and therefore globally given the desire for a single global SKU)
  The various versions of EN 301 893 (including some drafts, via Notified Bodies) have enabled products to be placed on the market in Europe:
    Wi-Fi: 802.11a/n/ac/ax (all are available on market in Europe today)
    3GPP: LAA & NR-U (not clear if any products are on market in Europe today)

## Slide 5: The refined 5 GHz compromise in Europe forces 802.11be to use a different coex option from the past
  In 2021, negotiations for the next version of EN 301 893 become blocked
    Some cellular stakeholders believed the agreement for a compromise should not apply beyond IEEE 802.11ac
    Allegations were made that some Wi-Fi systems did not implement Preamble Detection correctly to threaten the imposition of complex testing
    It all become very complicated … and the regulators in ETSI BRAN started to get impatient
  To avoid outcomes not in the best interests of the Wi-Fi industry, a refined compromise for EN 301 893 (5 GHz) was agreed by all
    Access mechanisms used by 802.11a/n/ac/ax complaint systems were effectively grandfathered (including 802.11ax coloring)
    All other systems would need to use ED-only based listening @ -72 dBm (scaled with tx power)
    Only simplified tests would be required

## Slide 6: The refined 5 GHz compromise in Europe works well for IEEE 802.11ax but maybe not IEEE 802.11be
  The refined EN 301 893 compromise was a great outcome for IEEE 802.11a/n/ac/ax based systems …
    They could operate as specified by the IEEE 802.11 standard
    Simple testing meant lower certification costs and less risk
    Reasonable coexistence was likely with LAA/NR-U systems using ED-only @ -72 dBm, based on simulations undertaken some years ago in 3GPP
  … but not necessarily a great outcome for IEEE 802.11be based systems, or Wi-Fi generally, in terms of good coexistence
    The obvious options for 802.11be to operate within the ED-only @ -72 dBm constraint are all unattractive
    Other options to mitigate the constraints on 802.11be in 5 GHz are uncertain or unlikely

## Slide 7: The obvious options for 802.11be to operate with ED-only @ -72 dBm constraint are all unattractive
Previous status quo | Operating within the new ED-only @ -72 dBm constraint |  | 
802.11be uses PD/ED @ -82/-62 dBm, with NAV | 1) 802.11be uses PD/ED @ -82/-72 dBm, with NAV | 2) 802.11be uses PD/ED @ -72/-72 dBm, with NAV | 3) 802.11be uses ED-only @ -72 dBm, without NAV
Similar access as 802.11ax, with efficient use of spectrum from use of NAV | Defers more often than 802.11ax, which uses EDT @ -62 dBm | Uncertain sharing with 802.11ax; never tested or simulated | Similar access as 802.11ax* but less efficient use of spectrum by Wi-Fi due to no NAV
Similar access as LAA/NR-U* | Defers more often than NR-U/LAA, due to use of PD & NAV | Defers more often than LAA/NR-U, due to use of NAV | Similar access as LAA/NR-U*
Aligned with 802.11 standard | Aligned with 802.11 standard (additional ED regulatory restriction) | Not aligned with 802.11 standard TGbe work required? | Not aligned with 802.11 standard TGbe work required?
* Assumes PD/ED @ -82/-72 dBm and ED-only @ -72 dBm have similar access, albeit with some exceptions (based on 3GPP simulations)
Forces 802.11be to have the same inefficiencies as LAA/NR-U by removing NAV based sharing, which is more sophisticated than ED based sharing
Preliminary studies (11-21-0705-00, 11-21-0851-00, 11-21-1179-00) presented to the Coex SC show disadvantage to 802.11be … at least some of the time

## Slide 8: Other options to mitigate the constraints on 802.11be in 5 GHz are uncertain or unlikely
  Don’t operate 802.11be in 5 GHz (at least in Europe)
    There is still 500 MHz of 6 GHz spectrum in Europe in which it can operate
    Does 802.11be need to operate in 5 GHz?
      If not, the problem goes away; a WFA question?
  Persuade ETSI BRAN to allow 802.11be to operate in the same way as 802.11a/n/ac/ax
    Probably not possible in the current environment
  Suggest that ETSI BRAN change EDT to -62 dBm
    Provides maximum simplicity and flexibility for Wi-Fi
    Will probably result in poor coexistence with other technologies ignoring Wi-Fi, as demonstrated by multiple simulations in 3GPP/ETSI BRAN/Coex SC
      Note: there is such a proposal from some ETSI BRAN members
      This claim is contentious and further study is encouraged; a Coex SC question!
    Are other technologies likely to compete with Wi-Fi in 5 GHz?
      If not, the problem goes away; a WFA question?
Possible actions?

## Slide 9: There are a variety of potential questions and tasks for TGbe & the Wi-Fi Alliance
  The Coex SC will continue evaluating the coexistence of 802.11be constrained by ED-only @ -72 dBm with other Wi-Fi & other systems …
    Based on material like 11-21-0705-00, 11-21-0851-00 & 11-21-1179-00 …
    ... and hopefully real deployments
  … and could propose a Liaison Statement to the Wi-Fi Alliance in March 2022 asking the WFA’s opinion on market related issues that impact the need for 802.11be to coexist with other technologies in 5 GHz
  … but there are also some potential tasks for TGbe related to specifying 802.11be operation under the constrained 5 GHz rules in Europe

## Slide 10: There are a variety of potential questions for the Wi-Fi Alliance in relation to 5 GHz operations
Possible questions for Wi-Fi Alliance in relation to 5 GHz operation
  Assuming 802.11be operations are disadvantaged in 5 GHz in Europe compared to 802.11ax, is it acceptable for 802.11be operations to focus on 2.4/6 GHz in Europe, using 802.11ax in 5 GHz?
    In at least short term; in the longer term, it might be possible to change EN 301 893 to allow 802.11be to operate like 802.11ax
  Noting that the rules in EN 301 893 (5 GHz) were driven by a concern other technologies would not coexist well with Wi-Fi, is it believed other technologies will be used frequently in 5 GHz (including DFS channels)?
    A “no” answer might encourage the specification of more liberal constraints in EN 301 893 …
    … but, of course, more liberal constraints might change the answer to “yes”
  …

## Slide 11: There are a variety of possible tasks for TGbe with respect to 5 GHz operation
Possible tasks for TGbe in relation to 5 GHz operation
  Assuming 802.11be operations are desirable in 5 GHz in Europe, should the 802.11be standard specify operations with
    PD/ED @ -72/-72 dBm, with use of NAV
    ED-only @ -72 dBm, without use of NAV
    PD/ED @ -82/-72 dBm, with NAV, ie no change from today?
  …

## Slide 12: There is a possible related task for TGbe with respect to 6 GHz operation
  In EN 303 687, the EDT is -72 dBm for both 802.11ax & 802.11be
  This is different to traditional 802.11 operations, which generally uses an PD/ED @ -82/-62 dBm
  The TGbe need to decide how to handle this difference for 802.11ax/be in 6 GHz in Europe
    Use PD/ED @ -82/-72 dBm (which may disadvantage Wi-Fi compared to NR-U)
    Allow PD/ED @ -72/-72 dBm (like NR-U, except for use of NAV)
    Something else?
  The decision could be:
    Reflected in the standard
    Handled outside the standard?