## Slide 1: Interaction between R-TWT and SCS (CC36 resolution for CID 4121)
Date: 2021-05-18
Authors:
Name | Company | Address | Phone | Email
Liangxiao Xin | Sony Corporation |  |  | Liangxiao.Xin@sony.com
Mohamed Abouelseoud |  |  |  | Mohamed.Abouelseoud@sony.com
Li-Hsiang Sun |  |  |  | Li-Hsiang.Sun@sony.com

## Slide 2: Related CID
CID | Commenter | Clause Number(C) | Comment | Proposed Change | 
4121 | Akira Kishida | 35.6.2.1 | Priority in latency sensitive traffic or TID should be clarified when operating on restricted service periods. In other words, some prioritization between TIDs in restricted service periods should be clarified. | As in comment. | 

## Slide 3: Introduction
Current tools for improving latency performance in TGbe
  SCS procedure: differentiate latency sensitive traffic stream under a QoS characteristics from other regular traffic or other latency sensitive traffic stream under different QoS characteristics in a same TID  traffic is tied to SCSID
  R-TWT procedure: channel reservation for latency sensitive traffic  traffic is tied to SCSID
The above two tools play different roles, and they should interact to achieve the best latency performance.
  R-TWT can use QoS characteristics of SCS traffic stream(s) for scheduling.
  SCS traffic stream might need R-TWT to provide channel resource reservation service.
However, the interaction between R-TWT and SCS is not well defined.
  The current draft does not define how to use SCS information for R-TWT scheduling
  The current draft does not define if SCS information is required before/during the R-TWT setup
  R-TWT setup is currently tied to TID not SCSID
We discuss adding parameters to facilitate the SCS and R-TWT interoperation

## Slide 4: Goal and difficulty
If a R-TWT is to be scheduled based on the QoS characteristics of a SCS traffic stream, It should prioritize the SCS traffic stream of concern during the R-TWT SPs instead of all the traffic in the same TID of a STA.
  For example, STA has two SCS traffic streams, e.g., SCS1 and SCS2 of TID=6, with different QoS characteristics. SCS1 traffic stream requires R-TWT for channel reservation and SCS2 traffic stream does not. During a R-TWT SP for SCS1 traffic stream, STA should prioritize SCS1 traffic stream only.
One concern when R-TWT procedure is prioritizing SCSID in a specific TID in the operation of BA
  The assignment of new MPDUs SN should prioritize the SCSID of concern. All previously assigned SN should be transmitted without interruption.

## Slide 5: Proposal 1
A SCS traffic stream should indicate whether it requires R-TWT scheduling for it during the SCS setup procedure
Proposal: Add R-TWT Request field in QoS Characteristics element to indicate whether SCS traffic stream requires R-TWT scheduling
  When the “R-TWT Request” is set to 1 in a SCS request frame, STA requires AP to schedule R-TWT for the SCS traffic stream. STA/AP may add the TWT element to the SCS request/response frames for RTWT setup or have separate RTWT setup after establishing SCS.
Element ID
Length
Element ID Extension
Control Info
Min SI
Max SI
Minimum Data Rate
Delay Bound
Maximum MSDU Size
Service Start Time
Mean Data Rate
Burst Size
MSDU Lifetime
MSDU Delivery Ratio
MSDU Count Exponent
Medium Time
R-TWT Request
QoS Characteristics element

## Slide 6: Proposal 2
R-TWT setup procedure contains SCS traffic information to indicate which SCS traffic streams are prioritized during the R-TWT SPs.
Proposal: Add one (or more) SCSID field in the Broadcast TWT parameter set field
R-TWT SPs are scheduled based on the QoS characteristics of the SCS traffic stream.
  R-TWT SP interval should be between min service interval and max service interval of SCS
  R-TWT SP duration should be greater or equal to medium time of SCS
  If the SCSID is UL or P2P, AP can use the R-TWT for scheduling TF or MU RTS TX
Request Type | … | Broadcast TWT Info | SCS ID
Broadcast TWT parameter set field

## Slide 7: SP1
Do you support to add R-TWT request field in QoS Characteristic element to indicate whether SCS traffic stream requires R-TWT scheduling?
  Note: this SP aims to trigger resolution of CID 4121

## Slide 8: SP2
Do you support to add one or more SCSID fields in the Broadcast TWT parameter set field to indicate the SCS traffic streams that are prioritized during the R-TWT SPs?
  Note: this SP aims to trigger resolution of CID 4121