## Slide 1: TGbc: Resolution to CID 2074 Date: 2022-01-19
Authors:
Name | Affiliations | Address | Phone | email
A. De la Oliva | InterDigital, UC3M | Avda. De la Universidad 30, Leganes, Madrid, Spain | +34 91 6248803 | aoliva@it.uc3m.es
Xiaofei Wang | Interdigital |  |  | 

## Slide 2: Motivation
There has been several discussions within IEEE 802.11bc about mobility and how to handle STAs moving while receiving EBCS traffic
An EBCS traffic stream is identified by a Content ID which is local to the AP but unique and shared across APs sharing the same AP certificate.
In order to consume an EBCS traffic stream in current specification, from a different AP, an EBCs Info frame needs to be received from target AP.
  This may take some time
  How do we reduce this time?
Please note that listening for EBCS Info frame may potentially mean that you interrupt the reception of an EBCS traffic stream
  E.g., the AP you are waiting the EBCS Info frame from is in a different band or channel than the one you are receiving the EBCS traffic stream from

## Slide 3: Current solutions used for reducing HO delay
A promising solution, that may be reused for reducing the HO in bc, is the Reduced Neighbor Report.
It includes, in a very compact way, information on when the next beacon of neighbor APs is expected and the channel/band the AP transmits.

## Slide 4: Propose enhancement
Add to the Reduced Neighbor Report element information on the TBTTs to next EBCS Info frame
Some more changes are needed to accommodate this field (length fields etc..)
 | Neighbor AP TBTT Offset | Neighbor AP EBCS Next Info frame TBTT Offset | BSSID (optional) | Short SSID (optional)
Octets | 1 | 0 or 2 | 0 or 6 | 0 or 4

## Slide 5: Conclusion
Roaming while receiving an EBCS traffic stream may break the current reception due to delays listening to EBCS Info frame
This delay can be shortened if time to next EBCS Info frame is advertised, e.g., using the Reduced Neighbor Report
  This has also the advantage of indicating the APs with same EBCS certificate than the one sending the Reduced Neighbor Report element
If the group is intersted we can prepare a contribution with the required changes