## Slide 1: TX and RX Timestamping Implementations
Date: March 9, 2022
Author:
Notes: This presentation is making the assumption that a sensing measurement timestamp is necessary. Contribution 3 of the memo was the “Should vs Shall” discussion. If you believe that it will take several slides to illustrate what is lost by not having a timestamp at all, or by the timestamp being optional, then it would be better to have a second contribution about the “what if we didn’t have any timestamp”.
This contribution combines the TX discussion with the RX discussion, which was contributions 1 and 2 from the memo. https://qipworks.box.com/s/ccsiiwcbcl413byixdyd06emmr0e0963

## Slide 2: Abstract
To discuss the implementation tradeoffs of performing timestamping at the TX vs RX side.
Provide proposals for including a timestamp in the measurement report frame.

## Slide 3: SFD Recap [1]
For the case when the sensing initiator is the sensing transmitter, the sensing initiator may optionally request the sensing responder to report sensing measurement results (Motion 60, 22/0038r2).
(Motion 21, 21/0908r2) A Sensing Measurement Report frame, which allows a sensing receiver to report sensing measurements, is defined. This frame contains at least the following two fields:
  Measurement report control field: Contains information necessary to interpret the measurement report field.
  Measurement report field: Carries CSI measurements obtained by a sensing receiver.
A WLAN sensing procedure may be comprised of multiple sensing measurement instances (Motion 14, 21/0145r4; Motion 29, 21/1543r1).

## Slide 4: SFD Recap Cont’d
7.1.4.2.4 Reporting phase
In the reporting phase of a sensing measurement instance, sensing measurement results are reported (Motion 15, 20/1851r4; Motion 29, 21/1543r1).
Results of measurements performed in a WLAN sensing procedure should be obtained by or reported to its initiator (Motion 11, 21/0147r3; Motion 29, 21/1543r1).
Transmission of the Sensing Measurement Report frame is initiated by an MLME primitive. Both immediate and delayed reporting are acceptable (Motion 21, 21/0908r2).
(Motion 34, 21/1438r1) In the reporting phase, sensing measurement results of multiple sensing measurement setups of a sensing responder may be included in a single Sensing Measurement Report frame for delayed reporting.
  Support for obtaining more than one sensing measurement result in a single Sensing Measurement Report frame sent by the sensing responder is optional for the sensing initiator.
  Support for buffering more than one sensing measurement result and sending it in a single Sensing Measurement Report frame to the sensing initiator is optional for the sensing responder.

## Slide 5: Non-SBP Cases
Due to scheduling, spectrum availability, etc, all sensing measurements subject to timing jitter.
We need to add a measurement timestamp to the MLME output (eventually provided to algorithm input).
Case (a) “Sensing Receiver MLME Output” – reported measurement contains timestamp
Case (b) “Sensing Transmitter MLME Output” - two possible options for timestamp:
  Option1: Sensing receiver timestamp present it in over-air-report (which can then be passed to MLME output)
  Option2: Sensing Transmitter generates timestamp, and adds into MLME output report
(2) MLME Output
(1) NDP
STA2
Sensing Transmitter
(a) Sensing Receiver MLME output
(b) Sensing Transmitter MLME output
(3) MLME Output
(1) NDP
STA1
Sensing Transmitter
(2) Report
(Measurement+Timestamp?)
Measurement
Timestamp
Measurement
Timestamp
STA1
Sensing Receiver
STA2
Sensing Receiver
APP
APP

## Slide 6: Non-SBP, Sensing Receiver MLME Output
(a) Timestamp Added by Receiver
Sensing Receiver
Sensing Transmitter
Over-the-air Measurement Report NOT required
MLME output for sensing application contains timestamp
(a) Sensing Receiver MLME output
(1) Build Report
- Obtain CSI_ESTIMATE
- Add corresponding RX Timestamp
- Deliver output to Sensing Application
1

## Slide 7: Non-SBP, Sensing Transmitter MLME Output
(b.1) Timestamp Derived by Receiver
(b.2) Timestamp Derived by Transmitter
Over-the-air Measurement Report IS required, two options for timestamping.
Sensing Receiver
Sensing Transmitter
Sensing Receiver
Sensing Transmitter
1
2
3
1
2
(1) Build Report (over-the-air)
- Obtain CSI_ESTIMATE
- Add corresponding RX Timestamp
(2) Output Received Report
- Deliver output to Sensing Application
(1) Record TX timestamp
- Maintain lookup table mapping identifier to TX timestamp
(2) Build Report (over-the-air)
- Obtain CSI_ESTIMATE
- NO Timestamp in report
(3) Obtain TX timestamp from (1) given identifier in report
- Deliver output to Sensing Application

## Slide 8: SBP Cases
Report to SBP Requester requires timestamp as it has no knowledge of measurement times
SBP cases transmit MLME measurement report to SBP Requester
When SBP AP is Sensing Receiver, equivalent to “Non-SBP, Sensing Receiver MLME Output”
When SBP AP is Sensing Transmitter, equivalent to “Non-SBP, Sensing Transmitter MLME Output”
  Option1: Sensing Receiver produces timestamp and includes it in report, which is then reported to SBP Requester
  Option2: Sensing Transmitter produces timestamp which is added to SBP report
(1) SBP Request
(2) NDP
STA1
SBP Requester
SBP-capable AP
Sensing Initiator
Sensing Receiver
STA2
Sensing Transmitter
(4) MLME Output
(3) Report
(Measurement + Timestamp)
Measurement
Timestamp
(1) SBP Request
(2) NDP
STA1
SBP Requester
SBP-capable AP
Sensing Initiator
Sensing Transmitter
STA2
Sensing Receiver
(5) MLME Output
(3) Report
(Measurement+Timestamp?)
(4) Report
(Measurement+Timestamp)
Measurement
Timestamp
(a) SBP-capable AP is Sensing Receiver
(b) SBP-capable AP is Sensing Transmitter
APP
APP

## Slide 9: Measurement Report Frame
Measurement Report Frame PDT defines the following [3]:
Measurement Report Frame (both public and private version) to contain one or more Sensing Measurement Report Elements
Report Element to contain a single measurement report
Report Control subfield to contain information necessary to interpret measurement report subfield.

## Slide 10: Option 1
Timestamp always added by sensing receiver, and always present in measurement report
Timestamp will be present in all over-the-air reports, SBP reports, and MLME reports

## Slide 11: Option 2
Timestamp added by device producing MLME output, or Sensing-By-Proxy AP, and optionally present in measurement report
Timestamp Present indication in Report Control field
  E.g., 1-bit indicating if timestamp is present or not in Measurement Report Element
Timestamp may not be present in over-the-air reports.
Timestamp will be present in SBP reports and MLME reports

## Slide 12: Option Tradeoffs
Evaluation | Option 1 | Option 2
Report Overhead | Non-SBP cases require TBD extra bits in measurement report. No extra overhead for SBP cases. | Non-SBP cases saves transmitting timestamp in over-the-air measurement report. No savings for SBP cases.
Handling delayed reports | Nothing additional required to manage delayed reports. | Transmitter must manage storage and lookup of transmit times (matched to IDs).
Dealing with NDP not received | Nothing additional required to manage missing NDP. | Logic required on Transmitter to identify missing reports and remove stale entries from transmit time lookup table.
STA time synchronization | Clock synchronization mechanism required for over-the-air reporting cases. Multiple sensing receiver STAs add their timestamp into the report, which require synchronization. | Simplified Synchronization. STA consuming measurements (or sending to SBP Requestor) adds timestamp, and hence a single clock used for all timestamping.
SBP Handling | No extra processing of Sensing Measurement Report elements to add timestamp. | SBP AP will need to manipulate Sensing Measurement Report elements to add timestamp before sending to SBP Requester.

## Slide 13: Conclusions
Given tradeoffs, Option 1 is preferred
  Eliminates state and LUT management introduced in Transmitter
  No extra manipulation of reports for SBP cases
  Cost is TBD bytes in report
TSF Synchronization handled by existing .11 components
  E.g., Partial TSF in NDPA used by FTM/11az for availability window
  More details on generating timestamp topic of next contribution

## Slide 14: SP1
Which of the following options do you prefer:
  In the Sensing Measurement Report Frame PDT (11-22-0235):
    A fixed length Timestamp field is to be added into the Measurement Report Element.
  In the Sensing Measurement Report Frame PDT (11-22-0235):
    An optional Timestamp field is to be added into the Measurement Report Element.
    A Timestamp Present subfield is to be added into the Report Control Field of the Measurement Report Element to indicate the Timestamp presence.
  Further Discussion on signaling of Timestamp.
  Abstain
a/b/c/d

## Slide 15: References
[1] 21/11-21-0504-07-00bf-specification-framework-for-tgbf
[2] 11-21-1924-02-00bf-timestamping-a-measurement-report.pptx
[3] 11-22-0235-04-00bf-proposed-draft-text-for-sensing-measurement-report-frame-excl-format.docx