## Slide 1: Discussion on PASN for sensing
Date: 2022-2-7
Authors:
Chaoming Luo (OPPO)
Name | Affiliation | Address | Phone | Email
Chaoming Luo | OPPO |  |  | luochaoming@oppo.com
Lei Huang |  |  |  | 
Pei Zhou |  |  |  | 

## Slide 2: Introduction
This contribution discusses whether PASN is mandatory for sensing and which categories of action frame are required accordingly.

## Slide 3: Recap: PASN
Preassociation Security Negotiation (PASN) derives a PTKSA with or without a PMKSA, allows any management frame to be protected for a STA in unassociated state. [2]
  With PMKSA, i.e., with mutual authentication, as for the case of cached PMK.
  Without PMKSA, i.e., without mutual authentication, similar to OWE (RFC8110), as for the case of no shared secret or shared side connection possible.

## Slide 4: Mandate PASN?
Support for unassociated STA for sensing?
  YES! Similar to ranging, it is important to enable a non-AP STA to perform sensing with an AP to which it is not associated with.
Mandate PASN for unassociated STA for sensing?
  Sensing data and result are privacy related, so data confidentiality, privacy are important for most use cases.
    One use case requires low security level, two use cases require low – medium security level, others are medium or high. [3]
  Low-end/IOT devices may not support PASN, but they may participate in sensing, typically as sensing responder & transmitter, but not sensing initiator or receiver.
  ‘B.4.3 IUT configuration’ indicates Support for PASN is optional. [1]
  Proposal: keep PASN as optional in sensing.

## Slide 5: Frame category
Public Action frame: Inter-BSS and AP to unassociated-STA communications, Intra-BSS communication, GAS. [1]
  code 4 in Table 9-51—Category values
Protected Dual of Public Action: allow robust STA-STA communications of the same information that is conveyed in Action frames that are not robust. [1]
  code 9 in Table 9-51—Category values
Protected Fine Timing Frame: supports a protected FTMR frame, protected FTM frame and protected LMR frame. [2]
  code 34 in Table 9-51—Category values
  In order to simplify selection of the frames to which the new replay counter applies, a new action category ‘Protected Fine Timing’ is created. [4][5]
Proposal: create a new action category ‘Protected Sensing Frame’.
  Similar with 11az, a new replay counter is needed.

## Slide 6: SP 1
Do you agree to add the following into 11bf SFD ?
  PASN for unassociated STA is used in sensing.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 7: SP 2
Do you agree to add the following into 11bf SFD ?
  A new action category of robust ‘Protected Sensing Frame’ is defined to separate PN segment.
  Y/N/A
Chaoming Luo (OPPO)

## Slide 8: Reference
[1] 80211-2020
[2] 80211az_D4.0
[3] 11-20-1712-02-00bf-wifi-sensing-use-cases
[4] 11-20-0797-00-00az-lmr-ftm-replay-counter
[5] 11-20-0889-05-00az-protected-lmr-replay-counter
Chaoming Luo (OPPO)