## Slide 1: STA Info field for the sensing NDPA frame
Date: 2022-02-15
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sang Kim |  |  |  | sanggook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
Feb. 2022

## Slide 2: Introduction
We are discussing the sensing NDPA frame as new NDPA variants for the sensing measurement.
  As in [1]~[3], the various methods were suggested to indicate or to define the sensing NDPA in 11bf.
Since it seems that the sensing NDPA will be defined as a new variant of the NDPA frame, the STA Info field in sensing NDPA also can be designed newly.
Thus, in this contribution, we consider the STA Info field in sensing NDPA frame.

## Slide 3: STA Info field
The STA Info field is configured as following according to each NDPA variants.
  STA info fields except for the VHT have an equal size as 4 bytes.
VHT
Ranging
HE
EHT

## Slide 4: Sensing NDPA frame
In the current 11bf SFD, sensing NDPA frame can be used in both the TB measurement phase and the Non-TB measurement phase.
  In each measurement phase, NDPA and NDP is used as follows
    TB measurement phase
    Non-TB measurement phase
  Since sensing NDPA frame is used in common regardless of measurement phase types( i.e. TB or Non-TB), the STA Info field should be designed by taking into account two measurement phases.

## Slide 5: STA Info field (1/3)
Generally, a STA Info field in NDPA frame includes the information related to NDP and feedback.
  In [1], we already introduced the some of information for the STA Info field in sensing NDPA.
Considering the Non-TB measurement phase, we can involve the following information in STA Info field.
  The information for the I2R NDP frame and the R2I NDP frame
    Similar to ranging NDPA, this information is used to indicate the LTF configuration of the I2R NDP frame and the R2I NDP frame.
  For this information, I2R N_STS and R2I N_STS subfields as defined in 11az can be considered.
    Each field can be configured as 3bit by considering the support of the Max N_NTS (e.g., up to 8).

## Slide 6: STA Info field (2/3)
Also, we can consider the following information for the STA Info field.
  AID (11bits)
    It is used to identify the STA that is intended to sensing measurement.
  Feedback type and Ng (TBD bits)
    Indicate the feedback type and the granularity of channel measurement.
    This two information can be indicated by using the separate information field in the STA Info field if it is decided later.
    In the current 11bf SFD, CSI feedback is only applied. and it is open to adding the new type of feedback type in 11bf SFD.
    Various values for Ng are discussed, but it is desirable to use one or two values to minimize complexity as developed in 11specs if there is no significant performance difference.
    In addition, we can consider that these two information can be decided on the sensing measurement setup phase and, it can be used as static or semi-static information during the one measurement setup duration.
      It needs further discussion

## Slide 7: STA Info field (3/3)
  Partial BW info (e.g., 9bits )
    As in [4], to support the preamble puncturing and partial bandwidth feedback in sensing measurement, this information may be included in STA Info field.
    This doesn’t necessarily mean to use OFDMA NDP, i.e. we can still reuse SU type NDP as in 11ax/11be and just indicate punctured or partial BW to measure and feedback when there are some interfered subchannels or the receiver is a smaller BW operating STA.
    Considering the wide bandwidth and various puncturing patterns, we can reuse the Partial BW info defined in 11be.
  Disambiguation (1bit)
    According to a decision to define the sensing NDPA frame as described in [1]~[3], it will be decided whether this information is included or not.

## Slide 8: Size of STA Info field
In the previous slides, we consider the various information that can be included in STA Info field.
For example, the total number of bit for indication of those information can be calculated as follows.
As explained above, the number of bits required is from 26 bits to 30 bits.
  It is possible to use the 3 to 6 bits for the new information if it needs.
Therefore, with an evaluation of the above related to information of STA info field, we can consider the use of the STA info field configured with 4 bytes .
Information | Number of Bits
AID | 11
Partial BW info | 9
I2R NDP NSTS | 3
R2I NDP NSTS | 3
Feedback type and Ng | 0/2
Disambiguation | 0/1
Reserved | 3/6
Total number of bits | 32
Reserved in TB sensing measurement instance
Needs further discussion if it is included or not

## Slide 9: Summary
In this contribution, we investigate the information that is included in STA info field of sensing NDPA.
  Since NDPA can be used in both the TB measurement phase and non-TB measurement phase, we should consider the all information for both cases.
  For support of punctured channel and partial BW feedback in the sensing measurement, the partial BW info field can be included in STA info field.
  As shown in slide 8, we can configure the STA Info field to be composed of 4 bytes information bits.

## Slide 10: Straw poll#1
Do you agree to add the following in the 11bf SFD?
  The STA info field in sensing NDPA includes the following information.
    AID11 (11bits)
    I2R NDP NSTS (3bits)
    R2I NDP NSTS (3bits)
    Whether Feedback type and Ng is included is TBD.

## Slide 11: Straw poll#2
Do you agree to add the following in the 11bf SFD?
  The STA info field in sensing NDPA includes the following information.
    Partial BW info
      The size of this information is TBD

## Slide 12: Straw poll#3
Do you agree to add the following in the 11bf SFD?
  The STA info field of the sensing NDPA frame consists of 4bytes of information.

## Slide 13: Straw poll#4
Do you agree to add the following in the 11bf SFD?
  The format of STA info field in the sensing NDPA is defined as follow.
    For TB sensing measurement
    For non-TB sensing measurement

## Slide 14: Reference
[1] 802.11-21/1751r2, Consideration for NDPA in 11BF, Dongguk Lim, LGE
[2] 802.11-21/1896r2, NDPA for Sensing, Junghoon Suh ,Huawei
[3] 802.11-21/2011r1, Sensing NDP Announcement, Liwen Chu , NXP
[4] 802.11-22/0337r0, Partial Bandwidth transmission of NDP in 11bf, Dongguk Lim, LGE