## Slide 1: TGbh solutions analysis
Date: 2022-02-16
Authors:

## Slide 2: Abstract
Quick analysis of the submitted “solutions” for TGbh, based on criteria from Feb 8 telecon.

## Slide 3: Reminder of Feb 8 considerations
During the Feb 8 TGbh teleconference, the following criteria/considerations were proposed, for evaluating the submitted solutions:
Use cases covered, affected by:
  During association&4WH or post-association/security context (e.g., robust action frame)
    # of message exchanges(s)
    Timing of the ID:
      Is the identifier needed before network services/access?
      Can it be changed during association?
  ID generation (Network or STA)
How much “new” is being designed? (“simplicity” measure?)
Protection against spoofing (of AP and/or STA)?

## Slide 4: Review of considerations, for submitted solutions
Solution and summary | During assoc/security or post assoc/security | # add’l msgs | ID timing | ID generation | How much “new” | Spoofing protected?
Signature-based: AP gets STA’s public key, identifies STA by matching signature of address to key | During | 0 | @Assoc | N/A | STA needs to generate public/private key, send sig per Assoc | AP – no, non-AP - yes
IRMA: AP gets STA’s IRMK, identifies STA by matching hash of address | During | 2 (one time) | @Assoc (after first) | N/A | STA generates 48 bit IRMK, send hash per Assoc | Yes
ID Query: STA provides any ID, within secured Action frame | Post | 2 (per Assoc) | STA control – right after Assoc? | STA, arbitrary string | Action frame exchange | No
Transient STA ID: “TSID” generated from PTKSA, updated by knowing the previous one | During | 0 | @Assoc | N/A | TSID generation from PTKSA, hashing | ?
Secure Device ID: Adds keypair encryption to ID Query | During/Post | 2 In the case of post (from ID Query) | STA control – during or right after Assoc | STA | Public/private key pair generated by AP, new Action frame to send | Yes

## Slide 5: Review of considerations, for submitted solutions (cont)
Solution and summary | During assoc/security or post assoc/security | # add’l msgs | ID timing | ID generation | How much “new” | Spoofing protected?
Opaque device ID: AP creates blob, STA returns it on future assocs | During | 0 | @Assoc | AP | Blob generation, added to HS #2 and #3 | ?
STA generated device ID: STA provides any ID, within handshake frames | During | 0 | @Assoc | STA | KDE added to HS #4 | ?
MAC address designation (MAAD): AP allocates “next address” that the STA uses on next association | Before | 2 (per Assoc) | @Previous Assoc | N/A (AP) | Action frame exchange with MAADs | Yes
Network generated device ID: AP creates blob, STA returns it on future assocs (refinement of Opaque device ID) | During | 0 | @Assoc | AP | Blob generation, added to HS #2 and #3 | ?