## Slide 1: Discussion of NSTR and EMLSR
Date: 2021-03-06
Authors:
Name | Affiliations | Address | Phone | Email
Yunbo Li | Huawei | Shenzhen, China |  | liyunbo@Huawei.com
Yiqing Li |  |  |  | 
Ming Gan |  |  |  | 
Yuchen Guo |  |  |  | 
Guogang Huang |  |  |  | 
Yuxin Lu |  |  |  | 
Yousi Lin |  |  |  | 
Edward Au |  |  |  | 
Stephen McCann |  |  |  | 
Notes: September 2012

## Slide 2: CID 5773
CID | Commenter | Section | Page.Line | Comment | Proposed Change | Resolution
5773 | Laurent Cariou | 35.3.15 | 281.17 | eMLSR has been introduced a bit late compared to other modes like NSTR and has therefore been introduced as optional. However, support for operation with non-AP MLD with the other main modes is mandatory at the AP MLD side (NSTR, STR). It would make sense that all the main modes are actually mandatory supported on all AP MLDs. On top of that, eMLSR has shown significant gains and is clearly a very important features for MLO in 11be. Also complexity to support eMLSR for an AP MLD that already supports operation for NSTR or STR non-AP MLD is relatively minor. | Make eMLSR support mandatory on AP MLD side. | 

## Slide 3: Background
A pair of links on which a regular AP MLD operates is mandate to be STR.
A pair of links on which a non-AP MLD operates could be STR, NSTR, MLSR, or EMLSR, depending on the cost, size, frequency gap between these two links and so on;
MLSR can obtain performance gain by using link selection according to the traffic load and link quality, but it has worse performance on throughput and latency than NSTR and EMLSR;
This presentation focuses on NSTR and EMLSR and provides their performance comparison.

## Slide 4: Performance loss compared with STR
NSTR
  For UL channel access, there may exist waiting time on one link for another link if an NSTR non-AP MLD intends to transmit on these two links simultaneously;
  When an AP MLD schedules the UL/DL transmission for an NSTR non-AP MLD, cross link interference constraint should be taken into account
  Blindness exists on one link due to the transmission on another link
EMLSR
  Overhead of initial control (MU-RTS/CTS, or BSRP/BSR)
  Overhead of switch delay between receiving mode and listen mode
  Blindness exists on one link due to the transmission on another link
  Blindness exists during the frequent switch
  Lack of frequency diversity resulting from more than one link

## Slide 5: Comparison between NSTR and EMLSR
 | NSTR | EMLSR
MIMO | Flexible to be SISO or MIMO | Mandatory to support MIMO
RF switch | No | Frequent
Peak throughput (1+1 for NSTR; 2*2 for EMLSR) | Higher because of the frequency diversity | Lower due to Overhead of Initial Control and switch delay Interference among those streams, resulting in low MCS Sounding overhead
Whether UL transmission on link 1 will cause blindness on link2 or not? | No for single short packet (<72us) ; Yes for long packet (≥72us) | Yes
Whether DL transmission on link 1 will cause blindness on link2 or not? | No for most cases because BA is shorter than MediumSyncThreshold in many cases | Yes
Is simultaneous transmission allowed on more than link? | Yes | No
Probability for blindness | Relative Low | Relative high

## Slide 6: Setting of System Level Simulation
Parameters | Value
# of AP MLDs | 2
# of affiliated APs for each AP MLD | 2
# of associated non-AP MLDs for each AP MLD | 8
coverage of BSS | 10 m * 10 m
Distance between two AP MLDs | 30 m
BW | 80 MHz
MCS | 11
Traffic direction | UL + DL
DL PPDU type | MU-MIMO (4*4)
UL PPDU type | MU-MIMO for TB PPDU (4*4); SISO for NSTR EDCA; 2*2 MIMO for EMLSR EDCA
MPDU size | 1500 Bytes for throughput simulation, 200Bytes for delay simulation
Switch delay of EMLSR | 128 us
Blindness period | 5.484 ms

## Slide 7: Simulation Results of Throughput
MPDU size = 1500Bytes; Max number of aggregation = 256
8.5% for Aggr=1
14.8% for Aggr=2
7.7% for Aggr=4
4.3% for Aggr=8
23.1% for Aggr=4
13% for Aggr=8
7.5% for Aggr=16
16.7% for Aggr=32
12.5% for Aggr=64
10.4% for Aggr=128
37.6% for Aggr=64
31.3% for Aggr=128
28.2% for Aggr=256
100% for Aggr=64
100% for Aggr=128
94% for Aggr=256
3.1% for Aggr=1
5.7% for Aggr=2
4.1% for Aggr=4
2.5% for Aggr=8
12.4% for Aggr=4
7.6% for Aggr=8
5.6% for Aggr=16
15.1% for Aggr=32
13% for Aggr=64
12.5% for Aggr=128
39% for Aggr=64
37.6% for Aggr=128
36% for Aggr=256
100% for Aggr=64
100% for Aggr=128
100% for Aggr=256
Note 1: Aggr=n means there are n MPDUs in an A-MPDU.
Note 2: the traffic loads are rough estimations, not accurate loads Note 3: OBSS load refers to traffic load since two BSSs have the same traffic load in simulation
Traffic load of EMLSR:
Traffic load of NSTR:

## Slide 8: Simulation Results of Throughput
Interference level between two APs is about -76dBm
For simulation in previous slide, interference level between two APs is about -66dBm;
Two more simulations are provided with different interference levels between APs.

## Slide 9: Simulation Results of Throughput
For simulation in previous slide, interference level between two APs is about -66dBm;
Two more simulations are provided with different interference levels between APs.
Interference level between two APs is about -56dBm

## Slide 10: Simulation Results of Delay
MPDU size = 200 Bytes, Max number of aggregation = 256; MPDU life time = 20ms

## Slide 11: Summary
A pair of links on which a non-AP MLD operates is not STR, there are three possible modes: NSTR, MLSR and EMLSR.
Based on the performance analysis, NSTR has much better performance compared with EMLSR
Given that NSTR and MLSR are mandatorily supported at AP MLD side and they provide flexibility to the non-AP MLD (One is for good performance, the other is for low cost ), it is not reasonable to mandate EMLSR at AP MLD side.

## Slide 12: Straw Poll
Do you agree to resolve CID 5773 as below?
CID | Commenter | Section | Page.Line | Comment | Proposed Change | Resolution
5773 | Laurent Cariou | 35.3.15 | 281.17 | eMLSR has been introduced a bit late compared to other modes like NSTR and has therefore been introduced as optional. However, support for operation with non-AP MLD with the other main modes is mandatory at the AP MLD side (NSTR, STR). It would make sense that all the main modes are actually mandatory supported on all AP MLDs. On top of that, eMLSR has shown significant gains and is clearly a very important features for MLO in 11be. Also complexity to support eMLSR for an AP MLD that already supports operation for NSTR or STR non-AP MLD is relatively minor. | Make eMLSR support mandatory on AP MLD side. | Rejected. Base on the performance analysis in doc 11-22/0349r0, NSTR is the best, EMLSR is the second, and MLSR is the worst. Since NSTR and MLSR already been mandated at AP MLD side, mandating EMLSR at AP MLD side will add too many options and the complexity to AP MLD side.