## Slide 1: Discussion of CID2323 in LB258 on 802.11m D1.0
4 March 2021
Authors:
Name | Company | Phone | email
Andrew Myles | Cisco | +61 418 656587 | amyles@cisco.com

## Slide 2: CID2323 notes a problem with Table E-12 caused by overloading
CID | Comment | Proposed change
2323 | The Regulatory Info subfield definition has been generalized to apply to all countries, therefore this field should not be reserved in any country - rather the field should be set correctly according to the AP type. Note that if an AP considers the field reserved and sets value 0, this could be misinterpreted by a STA, causing the STA to incorrectly think the AP is an Indoor AP. | Remove the paragraph beginning "The Regulatory Info subfield..." (3 sentences), and replace with the following: "The Regulatory Info subfield carries information related to regulatory rules, and is interpreted per Table E-12 in E.2.7. In addition, add a note in E.2.7 below note 2, as follows: "Since an indoor enabled device operates conditionally on reception of an enabling signal from an indoor AP or indoor standard power AP, it is important that an AP only advertises the corresponding values (0 and 4) in Regulatory Info subfield if it is an indoor AP per regulatory rules."

## Slide 3: The problem noted in Table E-12 is based on a false premise
Situation
  The CID2323 comment starts by stating:
    The Regulatory Info subfield definition has been generalized to apply to all countries …
Problem
  A more accurate statement is that the Regulatory Info subfield definition has been generalized in a way that is hoped to apply to all countries
    The text describing Table E-12 even notes at least some values defined in Table E-12 might not be valid in all regulatory domains
  The reality of Table E-12 is that the functionality specified is often country specific or not defined/agreed
    The US-focused justifications in CC35 to refine Table E-12 no longer support the table

## Slide 4: The reality of Table E-12 is that its contents are often country specific or not defined/agreed
  A review of Table E-12 suggests every of one of the defined values are problematic in that they are defined in terms that are country specific and/or are subject to regulations not yet defined/agreed
    Indoor AP: outdoor vs indoor is a regulatory question that is country specific
    Standard Power AP: standard power has not yet been agreed in Europe et al
    Very low power AP: the definition of very low transmit power is a function of country specific regulations; VLP rules are still under discussion in the US
    Indoor enabled AP: this value has been defined to support C2C, but C2C has not yet been allowed in the US and agreement on the details of inclusion in EN 303 687 in Europe has been delayed (one major country is considering not allowing C2C); there has been virtually no discussion about using an indoor standard power AP to enable C2C (Europe has no standard power, and the US has no C2C)
    Indoor standard power AP: there is a hint of a definition for an indoor standard power AP in the US in an FCC KDB, but the concept is marked as a Phase 2 discussion; Indoor standard power AP is not defined at all in Europe
  …

## Slide 5: The US-focused justifications in CC35 to refine Table E-12 no longer support the table
  The most recent changes to Table E-12 were made after CC35 on the basis of the justification in 11-21-0790-06
  Part of the justification was that it was expected that:
    VLP operation would be allowed in the US by end of 2021
    C2C operation in the US would be allowed as defined by proposals to the FCC
    An Indoor Standard Power AP could be used to enable C2C operation
  As of Mar 2022, there appears to very little likelihood of either VLP or C2C being allowed in the US in the foreseeable future
    Even if VLP and/or C2C are allowed in the future, it is quite possible that the rules associated with them will be significantly different from current proposals
    The concept of an Indoor Standard Power AP also currently seems to be problematic in the US, including as part of any C2C rules
  Given these justifications have proven to be “enthusiastic”, the basis for the changes to Table E-12 are no longer valid

## Slide 6: A solution to the problem highlighted in CID2323 is further generalisation & a “none of the above” value
  While the premise of CID2323 is false, the problem highlighted in CID2323 is real
    ie the reserved value and the Indoor AP value potentially overlap
  That said, the proposed solution does not work because current regulatory uncertainty means that it is possible none of the defined values apply in a particular regulatory domain
  A solution is to define a value in Table E-12 that indicates that “none of the above” represent a description of the AP
    It is proposed that a value of 7 is used for this purpose
  An extension to the solution is to generalise Table E-12 even further so that it is more likely the “none of the above” value is never used
    Further generalisation of Table E-12 would allow blocking of C2C enablement in some environments

## Slide 7: Further generalisation of Table E-12 would allow blocking of C2C enablement in some environments
Further generalisation
  It is desirable to block C2C enablement in some environments
    Operation without infrastructure agreement could cause unnecessary interference in some use cases, eg industrial IoT
    Some regulators may want to the ability to block C2C enablement in sensitive areas
    Disabling C2C allows better auditing of sources of interference in a particular location
  This can be easily implemented by the addition of values 5 & 6 to Table E-12
    This refinement is backward compatible with the current proposal
Value | Description
0 | Indoor AP (may enable C2C operation)
1 | Standard Power AP
2 | Very Low Power AP
3 | C2C AP (shall not be used to enable another C2C AP)
4 | Indoor Standard Power AP (may enable C2C operation)
5 | Indoor AP (shall not be used to enable C2C operation)
6 | Indoor Standard Power AP (shall not be used to enable C2C operation)
7 | Reserved

## Slide 8: It is proposed that the response to CID 2323 is REVISED
Proposed response: REVISED
  The premise of CID2323 that “The Regulatory Info subfield definition has been generalized to apply to all countries …” is incorrect
    The expected convergence of regulations in 2021 that might have made this more true than it is as of March 2022 did not occur, and is unlikely to occur in the near future.
  However, the problem highlighted in CID2323 is real, in that there is potential ambiguity of the meaning of the value 0 in Table E-12, with overlap between reserved and Indoor AP
  The revised solution has two components:
    Define the value 7 as “none of the above”, which can be used when none of the other values are applicable, thus avoiding overlap with value 0 (Indoor AP)
    Generalise Table E-12 further, in support of the premise of CID2323, by allowing an AP to disable C2C enablement, which is sometimes desirable

## Slide 9: It is proposed that the response to CID 2323 is REVISED
Proposed Table E-12 revisions
Value | Description | C2C enablement
0 | Indoor AP An AP whose operation does not require control from an external system such as an Automated Frequency Coordination (AFC) system but that is subject to additional regulatory requirements intended to prohibit outdoor operation. | Receipt of this value may be used as an enabling signal for C2C operation, if allowed by regulation
1 | Standard power AP An AP whose operation requires control from an external system such as an AFC system. | Receipt of this value shall not used as an enabling signal for C2C operation
2 | Very low power AP An AP whose operation does not require control from an external system such as an AFC system, is not subject to additional regulatory requirements intended to prohibit outdoor operation, and is restricted to very low transmit power. | Receipt of this value shall not used as an enabling signal for C2C operation
3 | Indoor enabled AP An AP whose C2C operation relies on being able to successfully receive an enabling signal (as defined by the regulatory rules) from an indoor AP or an indoor standard power AP. | Receipt of this value shall not used as an enabling signal for C2C operation

## Slide 10: It is proposed that the response to CID 2323 is REVISED
Proposed Table E-12 revisions
Value | Description | C2C enablement
4 | Indoor standard power AP An AP whose operation requires control from an external system such as an AFC system and that is subject to additional regulatory requirements intended to prohibit outdoor operation. | Receipt of this value may be used as an enabling signal for C2C operation, if allowed by regulation.
5-7 | Reserved | 
5 | Indoor AP An AP whose operation does not require control from an external system such as an Automated Frequency Coordination (AFC) system but that is subject to additional regulatory requirements intended to prohibit outdoor operation. | Receipt of this value shall not used as an enabling signal for C2C operation.
6 | Indoor standard power AP An AP whose operation requires control from an external system such as an AFC system and that is subject to additional regulatory requirements intended to prohibit outdoor operation. | Receipt of this value shall not used as an enabling signal for C2C operation
7 | An AP whose operation does not operate according to any of the descriptions for values 0-6. | Receipt of this value may be used as an enabling signal for C2C operation, if allowed by regulation.