## Slide 1: The identification issue in pre-association
Date: 2022-02-19
Authors:

## Slide 2: Abstract
Further discussion on some user cases in Reference [1]
Supplement some new user cases

## Slide 3: 4.3 Post-association home automation (including arrival detection)
NOTE: “Post-association” means after both association is complete, and security context is established.
Similarly, two trends in home automation are converging: use of 802.11 technologies as the ‘backbone’ of the automation system; and a feature of the automation system which allows it to recognize when one of the residents arrives and “welcoming” them home by turning on lights, music, etc., tailored to the individual. This convergence means that using the 802.11 network to detect the individual’s arrival, by detecting their personal 802.11 device (smartphone, etc.) is a highly desirable capability. Currently, this device recognition is usually done based on the MAC address.
Key point: the device (user) is voluntarily opting-in to this system. Also key that protection from third-party tracking is included.
This scenario can be handled with an “opt-in” method for providing a device or user identification that is hidden from third party snooping, and provided only to trusted infrastructure (for example, where RSN has been established). Any broader solution (not explicitly “opt-in”, not secured from snooping, or not restricted to trusted infrastructure) is considered out of scope for 802.11bh.
Details of “device or user” are left to solution debate.

## Slide 4: Further discussion on user case 4.3 in reference [1]
Reference[1] subclause 4.3 discloses the case that smart home system based on Wi-Fi network can perform a certain reaction after detecting the device that is associated with the AP. E.g. turn on the light, open the door, etc.
Let’s think about the case: if the end user lost the password of the AP by misoperation on his/her cellphone, his/her will be blocked out of the door forever.

## Slide 5: 4.8 Infrastructure (home or enterprise): Probes are randomized, even to/heard by associated AP
A client that is using Local-ID MAC addresses could easily have an implementation that generates a new Local-ID MAC address for every Probe Request. This could even apply to Probe Requests that are directed to the associated SSID, when the client would otherwise use a consistent MAC address for transmissions within an association.
If the client has this extreme (or approaching this extreme) of an implementation of MAC address randomization, it will have a strong impact on the infrastructure’s ability to making steering decisions for that client.
When attached to a multiple-AP infrastructure, if the client uses the stable MAC address when probing, the infrastructure can help steer the client across both APs and bands, to give the entire network better experience. This could apply to both directed probes and broadcast probes, too.
Recommendations could be added to the Standard, to discuss the use of MAC addresses in scanning. There are trade-offs to be considered for a client to balance privacy and providing information to the network that could improve user experience.
It should also be noted that passive scanning is becoming more common, so reliance on identifiable probes for client steering has other problems, already.

## Slide 6: Further discussion on user case 4.8 in reference [1]
For the associated STA in multiple-AP infrastructure, the associated AP may send Beacon request frame to the associated STA to trigger an active scan (i.e making STA to send probe req) for steering purpose in practice, and thus there is no issue if the steering mechanism is based on the probe request frame sent by the STA.
We propose to delete the sentence “It should also be noted that passive scanning is becoming more common, so reliance on identifiable probes for client steering has other problems, already.” as we already has implementable solution to address such concern.

## Slide 7: User case-1
The Administrator will allocate an account(SSID/password) for new employee to access the company’s network via a special AP based on the cellphone’s MAC address shown in the system.
If there is no user connected to AP, the system will close the some APs to save power and to improve the channel condition, at least enable one general AP with constraint permission is always powering on to monitor the probe request frame sent by the STA so that the system can enable the corresponding AP immediately once the STA MAC address recorded in the DB detected.
The similar issue can broaden to the residential environment as well.
e.g.
the AP1 with SSID of “Guest” is always powering on to provide the basic access service.
The system will enable the AP with the SSID of “Employee-1” once detecting the known STA1’s probe request frame.

## Slide 8: Problem
Random MAC mechanism involved in 11aq makes such mechanism broken.
The System can’t identify the STA as a “know STA” in the probe request frame with the Random MAC address(RMA).
the corresponding AP can’t be enabled once it’s disabled.
On the STA side, the employee can’t find the AP to access the company’s network.

## Slide 9: User case-2
allow/deny MAC address list feature is widely used in current AP products
The owner of the AP may log on to the AP management page to disable some active STAs by adding their current MAC address to the deny list.
The system will disconnect these STAs by sending disconnection frame or de-auth frame to them.
AP will reject the auth/association request once the MAC address of requesting STA is in deny list.

## Slide 10: Problem
Random MAC mechanism in auth/association phase makes such mechanism broken.
The traditional deny/allow list function doesn’t work once the STA sends association request frame with an RMA after it back again.

## Slide 11: Motivation: the known STA with RMA still can be identified
We propose to define an solution to identify the known STA with RMA in pre-association phase(revert MAC mechanism).e.g. the AP can convert the RMA MAC of the probe request frame or auth/association frame to the True MAC.
STA
AP
Change True MAC to RMA MAC
Convert RMA MAC to True MAC and then make the decision
Probe/Auth/Association request carrying RMA MAC
Probe/Auth/Association response from AP
MAC Encrypt
MAC Decrypt

## Slide 12: reference
[1] 11-21-0332-28-00bh-issues-tracking

## Slide 13: SP1
Do you agree to supplement user case 1-3 in the slide to “11-21-0332-28-00bh-issues-tracking “ ?

## Slide 14: SP2
Do you agree the known STA with RMA can be identified in pre-association phase by the AP in 11bh?
Note: the identification mechanism is TBD.