## Slide 1: TG bh MAAD MAC-2
Date: 2022-02
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2
MAAD MAC-1
In original MAAD MAC scheme the AP allocates a MAAD MAC address to the STA after association, and the STA uses that allocated address the next time it associates
Hence AP recognizes STA pre-association.
MAAD MAC – 2
AP assigns MAAD MAC address during RSN association

## Slide 3: MAAD MAC - 2
Important differences to “Opaque device ID” 22/0154 and “Network Generated device ID” 22/0187
In these schemes, the AP sends an ID to the STA and the STA sends this ID to the AP during RSN association.
  The STA ID can be permanent for that AP
  STA ID is not related to the TA
In MAAD MAC-2, the AP allocates a MAAD MAC address to the STA, every association; and STA uses that as the TA in the next association.

## Slide 4: Outline
AP and STA show support for MAAD in Extended Capabilities
  NOTE: Maybe STA need not indicate support.
STA associates first time using 4 W HS
A MAAD MAC Address sent by AP in EAPOL-Key msg 3/4 (as per opaque device ID)
  48 bit MAC address, Locally administered (maybe SLAP?)
  AP stores the allocated MAAD MAC for that STA
  STA stores the allocated MAAD MAC for that AP
When STA comes back it uses that MAAD MAC Address as TA
AP instantly recognizes the STA from TA Association Request etc.
  AP can identify the STA pre-association – e.g. directed probe
STA Associates using the allocated MAAD MAC as TA
At association, AP provides new MAAD MAAC address in EAPOL-Key msg 3/4
NOTES (as per network generated device ID):
For FILS new MAAD MAC address is received in Association Response frame
For FT new MAAD MAC address is received in EAPOL-Key msg 3/4, but not during the FT protocol reassociations within the same ESS

## Slide 5: Options for consideration
Does STA need to advertise support?
  AP could allocate MAC address anyhow. If STA knows what to do then it uses it, if not, the STA won’t use it.
  Is it important that 3rd party knows that scheme is being used?
  Simplest is that STA does indicate support.
AP could embed something in MAAD MAC address for recognition purposes.
  Could be simple like a unique OUI
  Could be an embedded code
  AP could instantly know “STA is known”
  Nice, but out-of-scope

## Slide 6: Discussion
Changes from “Opaque device ID” and “Network generated device ID”
STA receives a new “ID”, every association
STA ID is a new MAC Address
STA does not provide an ID in the association, it uses the allocated “ID” as its TA.
Advantages:
TA is identified pre-association
TA changes every time, but is identified only by the AP

## Slide 7: Straw Poll
Do you consider this scheme as high, medium or low priority for TGbh?