## Slide 1: TG bh MAAD MAC-2
Date: 2022-02
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2
MAAD MAC-1
Only AP advertises support (3rd party cannot tell if scheme in use)
AP allocates a MAAD MAC address to the STA after association, using robust action frame exchange, initiated by STA
MAAD MAC – 2
Both STA and AP advertise support
AP assigns MAAD MAC address during RSN association
Common
STA uses that allocated address the next time it associates
AP recognizes STA pre-association
Reassociation uses MAC address used for the association

## Slide 3: MAAD–2 Intro
Important differences to “Opaque device ID” 22/0154 and “Network Generated device ID” 22/0187
In these schemes, the AP sends an “ID” to the STA and the STA sends this ID to the AP during RSN association.
  The STA “ID” can be permanent for that AP (it is not defined)
  STA “ID” is not related to the TA
In MAAD-2, the AP allocates a MAAD MAC address to the STA, every association; and STA uses that as the TA in the next association.
The STA does not send an ID, the TA is the identification (as was pre-RCM)

## Slide 4: Outline
AP and STA show support for MAAD in Extended Capabilities
STA associates first time using 4 W HS
A MAAD MAC Address sent by AP in EAPOL-Key msg 3/4 (as per opaque device ID)
  48 bit MAC address, Locally administered (maybe SLAP?)
  AP stores the allocated MAAD MAC for that STA
  STA stores the allocated MAAD MAC for that AP
When STA comes back it uses that MAAD MAC Address as TA
AP instantly recognizes the STA from TA Association Request etc.
  AP can identify the STA pre-association – e.g. directed probe
STA Associates using the allocated MAAD MAC as TA
At association, AP provides new MAAD MAC address in EAPOL-Key msg 3/4
NOTES (as per network generated device ID):
For FILS new MAAD MAC address is received in Association Response frame
For FT new MAAD MAC address is received in EAPOL-Key msg 3/4, but not during the FT protocol reassociations within the same ESS

## Slide 5: Options for consideration
Does STA need to advertise support?
  AP could allocate MAC address anyhow. If STA knows what to do then it uses it, if not, the STA won’t use it.
  Is it important that 3rd party does not know that scheme is being used?
  Conclusion is that STA does indicate support.
AP could embed something in MAAD MAC address for recognition purposes.
  Could be simple like a unique OUI
  Could be an embedded code
  AP could instantly know “STA is known”
  Nice, but out-of-scope
Does STA need to acknowledge?
  Could add an acknowledgement in message 4.

## Slide 6: Discussion
Changes from “Opaque device ID” and “Network generated device ID”
STA receives a new “ID”, every association
STA ID is a new MAC Address
STA does not provide an ID in the association, it uses the allocated “ID” as its TA.
Advantages:
TA is identified pre-association
TA changes every time, but is identified only by the AP
Comparison with original MAAD scheme (uses robust action frame exchange)
MAAD 1 MAAD 2
3rd party knows scheme in use No Yes
STA controls initiates the provision Yes No

## Slide 7: Straw Poll (3/8/2022)
How much priority do you put on continuing work on the MAAD MAC 2 proposal (11-22/0424)?
High 5
Medium 16
Low 7