## Slide 1: Trigger frame for 11bf
Date: 2022-03-22
Authors:
Name | Affiliation | Address | Phone | Email
Dongguk Lim | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | dongguk.lim@lge.com
Insun Jang |  |  |  | insun.jang@lge.com
Sang Kim |  |  |  | sanggook.kim@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
March 2022

## Slide 2: Introduction
Based on the current 11bf SFD, we agreed to define a Trigger frame variant for the sensing measurement.
Also, the various types of Trigger frames are used in the TB sensing measurement instance.
  The Trigger frame is used in the polling phase and the Trigger frame sounding phase.
  In addition, it can also be used in the reporting phase.
But the current 11bf SFD did not include the details, so in this contribution, we investigate the Trigger frames for purpose of the sensing measurement.

## Slide 3: Recap. 11bf SFD
Regarding the Trigger frame, 11bf SFD included the following motions.
  (Motion 25c, 21/0990r2; Motion 27, 21/1015r2)
    A Trigger frame variant is defined that allows an AP STA to solicit NDP transmission(s) from STA(s) to obtain sensing measurements.
      Details of the format of the Trigger frame variant are TBD.
  (Motion 25c, 21/0990r2).
    In the polling phase, an AP sends a Trigger frame to check the availability of STAs. If a STA is available, it responds with a CTS-to-self.
  (Motion 25c, 21/0990r2; Motion 27, 21/1015r2)
    The TF sounding phase consists of
      The transmission of a Trigger frame by an AP to solicit NDP transmission(s) from STA(s); and
    The transmission of an NDP by STA(s) SIFS after receiving the Trigger frame.
    Note: TF sounding is defined for HE and/or EHT STAs. Supporting other STAs is TBD

## Slide 4: Trigger frame format in 11ax (1/2)
The Trigger Dependent Common Info subfield in the Common Info field is optionally present based on the value of the Trigger Type subfield.
The Trigger frame for EHT also have a similar format.

## Slide 5: Trigger frame format in 11ax (2/2)
Trigger Type subfield encoding
  In 11ax, various Trigger frame variants were defined and for the indication of each variant, the Trigger type subfield was used.
    There were some reserved values in the Trigger Type subfield.

## Slide 6: Consideration for Trigger frame for the sensing measurement
For the definition of Trigger frame variant for the sensing measurement, we can consider two options.
  Option 1 : newly define the Sensing Trigger frame variant
  Option 2 : reuse the Ranging Trigger frame variant
In the next slides, we investigate more about each option.

## Slide 7: Opt. 1: New Sensing Trigger frame variant
Similar to 11az, we can use the reserved value in the Trigger Type subfield to indicate the all sensing Trigger frames for 11bf.
  Trigger Type subfield encoding as in 11az
  The reserved values (9-15) can be used to define another trigger variant for future amendments.
    So, using the 1 value among the reserved values in Trigger Type subfield, we can easily represent the sensing Trigger frame for 11bf.
  Thus, we propose to use the Trigger type subfield value of 9 as a Sensing Trigger frame variant.

## Slide 8: Opt. 1: New Sensing Trigger frame variant
Based on the current 11bf SFD, 3 different Trigger frame variants have been identified for the sensing measurement.
  Trigger frame for the polling phase
    Identify the STAs that intend the sensing measurement.
  Trigger frame for the sensing measurement phase
    Solicit the UL NDP from the STA(s)
  Trigger frame for the feedback from the STA(s)
Additional Trigger frame variants can be defined within the 11bf (if it needs)

## Slide 9: Opt. 1: New Sensing Trigger frame variant
To indicate the various Sensing Trigger variants explained in slides 8, we can adopt the same way as defined in 11az.
  For that, the Trigger Dependent Common Info subfield should be included in the Sensing Trigger frame.
  Also, for the indication of each Sensing Trigger variant, a Trigger Subtype subfield should be included in the Trigger Dependent Common Info subfield.
In addition to what is defined, additional variants of the Sensing Trigger frame that need to be defined can be considered. So, 3/4 bits for the Sensing Trigger Subtype subfield can be considered.
  In 11az, 4bits for the Ranging Trigger Subtype subfield are assigned.

## Slide 10: Opt. 1: New Sensing Trigger frame variant
In the sensing measurement, the multiple sensing measurement setup ID and measurement instance ID can be used.
  And, above IDs are only used in the sensing Trigger frame for the sensing measurement.
    If the measurement instance contains the both TF sounding phase and NDPA sounding phase, the equal IDs are used in both phases.
  So, for the indication of setup ID and instance ID, that information also can be included in the Trigger Dependent Common Info field.
Trigger Dependent Common Info subfield format for the Sensing Trigger is configured as follows

## Slide 11: Opt.2: Reuse of Ranging Trigger frame variant
The Sensing Trigger frame variant use the same value with the Trigger Type subfield
  Trigger Type subfield encoding for 11bf
We need to consider the signaling to indicate the Sensing Trigger frame variant due to the use of the same value of the Trigger Type subfield.
  For that, it seems better to use the Trigger Dependent Common Info subfield in the Ranging trigger frame variant.
Trigger Type subfield value | Trigger frame variant
8 | Ranging/Sensing
9-15 | Reserved

## Slide 12: Opt.2: Reuse of Ranging Trigger frame variant
The Trigger Dependent Common Info subfield in the Sensing Trigger frame variant can be composed as follow.
  The reserved bit (B4) is used to indicate the Sensing Trigger frame variant.
  If B4 is set to the sensing, the Token subfield can be rephrased to measurement setup ID.
  In addition, to signaling the measurement instance ID, the measurement instance ID subfield is added in the Trigger Dependent Common info field in the Sensing Trigger frame variant.
    If the measurement instance ID does not need to be included in the Trigger frame, the additional part as noted by the dotted line is not included. So, we can inherit the Trigger Dependent Common info subfield of the Ranging Trigger variant.

## Slide 13: Opt.2: Reuse of Ranging Trigger frame variant
We can leverage the indication defined in 11az to indicate the various trigger frame subvariants that are used in the sensing measurement.
  As shown in slide 12, the Sensing Trigger Subtype subfield in the Trigger Dependent Common Info subfield is used.
  Also, the value of the Sensing Trigger Subtype subfield for the Sensing Trigger frame may be encoded differently from11az.
    For example, the Sensing Trigger Subtype is configured as follows.
Sensing Trigger Subtype subfield value | Sensing Trigger frame subvariant
0 | Poll
1 | Sounding
2 | Report
3~15 | Reserved

## Slide 14: Summary
We reviewed the Trigger frame format defined in 802.11ax and 11az.
For the Sensing Trigger frame format, we considered the two options.
  Opt. 1 - newly define the Sensing Trigger frame variant
    The Trigger type subfield value of 9 is used
  Opt. 2 - reuse the Ranging Trigger frame variant
    The same value(i.e., 8) of the Trigger type subfield value for 11az is used
    To indicate the Sensing Trigger frame, the Reserved bit (B4) in the Trigger Dependent Common Info subfield in the Ranging Trigger frame variant is used.
Regardless of options, the proposed Trigger frame format for sensing has the following features.
  The Trigger Dependent Common Info subfield is included in the sensing trigger frame.
  The Sensing Trigger Subtype subfield included in the Trigger Dependent Common Info subfield is used to define the variants of the Sensing Trigger frame defined in 11bf.
  The sensing measurement setup ID and measurement instance ID are included in the Trigger Dependent Common Info subfield.

## Slide 15: Straw poll#1
Which option do you prefer to define the Sensing Trigger frame format?
  Opt. 1 : Newly define the Sensing Trigger frame variant
    The Trigger type subfield value of 9 is used
  Opt. 2 : Reuse of Ranging Trigger frame variant
    The Trigger type subfield value of 8 is used, i.e., same as the Ranging Trigger frame.
  Abs.

## Slide 16: Straw poll#2
If majority is option1
Do you agree to add the following to the 11bf SFD?
  A single Trigger Type subfield value is used to define the Sensing Trigger frame for the 11bf.
    The Trigger type subfield value of 9 is used.
  The Sensing Trigger frame includes the Trigger Dependent Common Info subfield.
  The Trigger Dependent Common Info subfield includes the Sensing Trigger Subtype subfield.
    The Sensing Trigger Subtype subfield consists of 4bits.
    The Sensing Trigger Subtype subfield signals the Sensing Trigger frame subvariant.
  The Three Sensing Trigger frame subvariants are defined.
    Poll, Sounding, and Report
    Other subvariant is TBD.
  Other bits of the Trigger Dependent Common Info subfield are TBD.
  The details for the common info field format of Sensing Trigger frame format is TBD.
  Y/N/A

## Slide 17: Straw poll#2-a
If majority is option2
Do you agree to add the following to the 11bf SFD?
  The value of the Trigger type subfield value in the Sensing Trigger frame is set to 8.
    The same as the Ranging Trigger frame.
  The reserved bit B4 of the Trigger Dependent Common Info subfield is used to indicate the Sensing Trigger frame.
  The Ranging Trigger Subtype subfield is rephrased as the Sensing Trigger Subtype subfield.
  The Three Sensing Trigger frame subvariants are defined.
    Poll, Sounding, and Report
    Other subvariant is TBD.
  The definitions of other bits of the Trigger Dependent Common Info subfield are TBD
  Y/N/A