## Slide 1: Rule-based random MAC STA identification
Date: 2022-03-10
Authors:

## Slide 2: OUTLINE
Background
Motivation
Rule-based random MAC STA Identification
Reference

## Slide 3: Background
Conventional 802.11 standards are designed in a way that each STA uses its own fixed unencrypted MAC address.
  This causes a security concern by allowing others to track STAs based on their MAC address.
To reduce this privacy risk, using MAC randomization (STAs using random MAC address) became a common technique.
Within this context, 11bh focuses on the identification issue on the STA with Random Mac Address (RMA) in pre-association phase:
  The STA uses a MAC address in the first-time association, and connects to AP.
  After a while, STA disassociates and wants to connect to the AP with a new MAC address (RMA).
  In this case (pre-association phase), how can AP identify the STA with its new MAC address (RMA)?
  Note that STA never changes its MAC address after association (post-association).

## Slide 4
11bh provides several identification solutions [1]:
  Signature
  ID (device ID, SID, any ID)
  Designated MAC
  Public-Private Key
Generally speaking, all these solutions can address the identification issue requested by 11bh group.
However, the overhead becomes a problem for these solutions:
  AP assigns some kinds of RMA/ID/KEY to a STA in an action frame (if used) after association. This action frame causes overhead.
  AP assigns some kinds of RMA/ID/KEY to a STA very frequently (i.e. each association). This frequent assignments cause overhead.
  Using long IDENTIFIER in management frame or EPOL frame also causes high overhead.
Our proposal would like to provide a secure RMA identification in pre-association without much overhead issue.
MOTIVATION

## Slide 5
Basic Idea (“rule-based” mechanism)
  Based on RAAD solution, we provide an enhanced designated RMA solution to mitigate the overhead issue.
  AP designates the rule of generating RMA to the STA instead of sending any form of RMA/ID/KEY itself.
  Afterwards, whenever STA with RMA establishes a new connection with AP, because both AP and STA generates the RMA based on the same rule, AP can recognize STA with RMA
  For security reasons, each user gets a unique rule.
  Note: The Rule of generating RMA is TBD.
Rule-based random MAC STA Identification

## Slide 6
Basic Idea (“rule-based” mechanism)
AP
STA1 (MAC1)
1st time Association
STA2 (MAC2)
STA3 (MAC3)
Rule1
Rule2
Rule3
AP
STA1 (RMA1)
2nd time Association
STA2 (RMA2)
STA3 (RMA3)
AP side:
MAC1 x Rule1 -> RMA1
MAC2 x Rule2 -> RMA2
MAC3 x Rule3 -> RMA3
STA1 side:
MAC1 x Rule1 -> RMA1
STA2 side:
MAC2 x Rule2 -> RMA2
STA3 side:
MAC3 x Rule3 -> RMA3
Additional information:
AP shares a unique rule to each STA only one time (such as in the first association phase)
  => resulting in less overhead (no extra additional frame exchange needed)
Each STA and AP use the same rule for future associations (rule will not change for a particular STA. If rule needs to change, AP assigns a new rule)
AP needs to keep a database to match RMA-MAC relationship
The rule of generating RMA can be possibly:
  Unique token
  Unique key
  Some sort of function
  (other possible solutions)
Rule-based random MAC STA Identification

## Slide 7
[1] 11-22-0296-08-00bh-tgbh-proposals.pptx
Reference

## Slide 8
THANK YOU 