## Slide 1: TG bh Way ahead
Date: 2022-02
Authors:
Name | Company | Address | Phone | email
Graham Smith | SRT Group | Sunrise , FL |  | gsmith@srtrl.com

## Slide 2: Way Ahead Intro
Meeting on 3/9/2022
Appeared to have consensus that Network generated ID preferred to STA generated.
We have two proposals using network generated
  Network generated device ID (NGID)
  MAC address designation (MAAD)

## Slide 3: NGID
AP allocates an ID to the STA during the 4-way HS, STA provides that ID on next association
  Any ID can be used, network controls the ID
  STA opts-in by showing Capability bit and by providing the ID when it associates.

## Slide 4: MAAD
MAAD - AP allocates a MAC address to the STA, STA uses that address as TA on next association
  TA is known so can be used pre-association
2 methods
MAAD MAC sent in m3 of 4-way HS
  STA opts-in by setting capability bit.(3rd party knows scheme is in use)
MAAD MAC sent with robust Action frame
  STA does not indicate support (3rd party does not know scheme is being used
  STA asks for the MAC address (STA initiates, AP allocates)

## Slide 5: Methods are complimentary
NGID is well suited to applications where pre-association recognition not needed and network is a very ‘busy’ one.
MAAD is well suited to applications where pre-association recognition is required/used.
Propose that both schemes could be included as they are complimentary
  Application chooses which method suits best
  Network can support one or both no problem.

## Slide 6: Proposal
Simply provide both NGID and MAAD text as they are distinctly different and each is suited to different applications
Suggest that the robust action frame scheme for MAAD be used, as it ticks 2 boxes
  STA does not set capability bit
  STA has more control as it decides to send MAAD Request.
Draft text exists for both schemes.