## Slide 1: Differential Quantization for CSI Report
Date: 2022-03-15
Authors:
Name | Affiliations | email
Qinghua Li | Intel | Qinghua.li@intel.com
Hao Song |  | Hao.song@intel.com
Xiaogang Chen |  | Xiaogang.c.chen@intel.com
Cheng Chen |  | Cheng.chen@intel.com
Robert Stacey |  | 

## Slide 2: Outline
Discussions about time-domain TCIR [2]
Frequency-domain differential quantization
Simulations
Conclusions

## Slide 3: Time-Domain TCIR
Quantizer
IFFT
Delay
Truncated
Fed back
FD channel response

## Slide 4: Assumption
CSI reporter only does simple IFFT and feeds back a few time-domain samples
Multipaths from reflecting objects are of interest
Concern
Signal obtained by simple IFFT differs from the actual multipaths such that the reflecting object of interest can’t be identified

## Slide 5: Signal Model
The band limited system serves as a filter concatenated with the multipath channel
The system response can be viewed as another multipath channel that needs to be deconvolved or equalized
Multipaths of interest
System impulse response
Channel estimates in time

## Slide 6: Long Tail
f
Edge
DC
Side lobe 3 samples away from the peak is still above 10% of the peak

## Slide 7: Inter-Path Interference
The impulse response of Tx/Rx system is not time-limited
  The system is band-limited
  No sounding signal on DC and edge tones
  No sounding signal on punctured sub-band
  Discontinuous 80 + 80
  DC notch filtering at Rx
Inter-path interferences are introduced such that interference mitigation is required to identify the multipaths

## Slide 8: Ambiguity due to Inconsistent Sampling Time
One main peak
Two main peaks
Same object?
The same channel results into two different TCIR feedbacks

## Slide 9: Harder to track variations among multipaths
Which two are the same?
Wraparound side lobes

## Slide 10: Lack of Identifiability
It is infeasible to identify the multipaths from a few feedback samples

## Slide 11: Effect of DC Notching
Receiver filters the time-domain signal for removing DC component

## Slide 12: Filtered Signal in Time
The DC notch filter convolves with the channel impulse response and increases the channel memory as if the multipath delay is increased
Increase inter-path interference
Multipaths
DC notch filter
Extended spread

## Slide 13: Additional Concerns
The wraparound of the long tails in IFFT window
  Which time samples should be fed back?
Interpolation and extrapolation
  Should DC tones, edge tones, and punctured sub-band be filled before IFFT?

## Slide 14: Wraparound Effect of FFT Window
One main peak
Two main peaks
Same object?
Or same object?
Large fake peak

## Slide 15: Pros and Cons of TCIR
 | Pros | Cons
Compatibility |  | Incompatible with legacy frequency domain implementation
Complexity |  | High complexity at sounding receiver due to additional IFFT and feedback sample selection
Application |  | Limited. Inapplicable to discontinuous band like 80+80 and punctured band.
Overhead | Low | 
Multipath identifiability |  | Poor identifiability and consistency due to inter-path interference, sampling time variation, and FFT window shifting

## Slide 16: Frequency Domain Approach
Feed all information back to sounding transmitter with minimum complexity
Be compatible with legacy channel estimation done in frequency domain
Reduce the feedback overhead by frequency domain down sampling
Can further reduce the feedback overhead by differential quantization, exploiting the channel correlation due to the main multipath cluster

## Slide 17: Correlation across Frequency
Channel responses of each link are correlated across frequency
The correlation decreases with Ng but it always exists thank to the dominant multipath cluster
The correlation can be exploited to improve quantization accuracy
f
h(f)
τ
Dominant cluster provides wideband correlation.
 | Ng = 4 | Ng = 8 | Ng = 16 | Ng = 32 | Ng = 64
Correlation | 0.95 | 0.90 | 0.82 | 0.55 | 0.32
Feedback subc spacing (MHz) | 0.3125 | 0.625 | 1.25 | 2.5 | 5.0

## Slide 18: Exploiting the Correlation
The input signal can be decomposed into two parts, the predictable and the unpredictable
is the prediction of from the quantized signal of the previous subcarrier,
The unpredictable is independent of the previously quantized signal and requires quantization and feedback
Since the entropy of is smaller than the original , less feedback overhead or higher quantization accuracy can be achieved
Predictable part of
Unpredictable part of

## Slide 19: Linear Prediction
Linear prediction of using
Signal model:
where is determined by the correlation between and ; the variables represent complex numbers.
Differential signal for quantization:

## Slide 20: Reduction of Quantization Range
If is chosen properly, e.g., close the correlation coefficient, and become independent such that
Namely, the quantization range is reduced by the differential operation. For example, Ng = 4 for 4x LTF, is about 1/20 of .
and

## Slide 21: Differential Quantization
f
Quantization:
Reconstruction:
Type equation here.

## Slide 22: Differential vs Non-Differential
Quantizer
Quantizer
-
Non-Differential
Differential

## Slide 23: Complexity Reduction
Estimate and only from few subcarriers, e.g., 10, spread evenly across the band (no full scan of the data)
d1
d2
dQ
f

## Slide 24: Simulation Configuration (1/2)
Channel D, NLOS, 80 MHz, MIMO with 4 Tx and 2 Rx antennas
4x LFT with DC notch filtering, subcarrier spacing 78.125 kHz
Four schemes are simulated with Nb = 6 and Np = 3
  Per-matrix scaling quantization, “Low Complexity Scaling and Quantization” in [1], 3+2x8x6 = 99 bits per H
  802.11n, 3+2x8x6 = 99 bits per H
  FD differential quantization, 2x8x6 = 96 bits per H
  TCIR [2] with the same total number of feedback bits as FD diff. quantization
 | Ng = 4 | Ng = 8 | Ng = 16
Correlation | 0.95 | 0.90 | 0.82
Feedback subc spacing (MHz) | 0.3125 | 0.625 | 1.25

## Slide 25: Simulation Configuration (2/2)
The total overhead is kept the same for TCIR and FD diff. quantization
  For example, TCIR: 12 bits per sample, which is 2x of the diff. quantization, but the number of samples only half of the diff. quantization
Low-complexity estimation of and for diff. quantization
  and are estimated from the mean of 10 subcarriers evenly distributed over the band
CDFs of QNSR are plotted
QNSR = Quantization noise power / Signal power

## Slide 26: Nb = 6, Ng = 4
With the same feedback overhead, differential quantization and TCIR deliver the highest accuracy

## Slide 27: TCIR with different numbers of time samples
Feeding back time samples of 1.6 μs performs the best for Channel Model D
3.2 μs
1.6 μs

## Slide 28: 3-bit Differential vs 6-bit Non-Differential
Differential quantization cuts the feedback overhead by half

## Slide 29: Conclusions
Time-domain TCIR is incompatible with existing transceiver implementation and incurs high complexity, e.g., IFFT and sample selection. Issues like sample selection need to be addressed for TCIR
In contrast, frequency-domain differential quantization is straightforward and fully compatible with the existing implementation
Frequency-domain differential quantization can either increase the feedback accuracy or cut the feedback overhead by half as compared with non-differential frequency-domain schemes

## Slide 30: References
Steve Shellhammer, et al., “Low-Complexity Scaling and Quantization for CSI Report,” IEEE 802.11-21/1573r0, September 2021
Rui Du, et al., “Truncated Power Delay Profile - follow up,” IEEE 802.11-21/1288r5, February 2022

## Slide 31: Straw Poll 1
Do you support to include frequency-domain differential quantization as an optional mode for 11bf CSI report?
Y/N/A