## Slide 1: Some proposals further discussion

## Slide 2: Background-1
In 332r37, 11bh group agrees to have a solution to address use case 4.1,4.2.4.8 and 4.26.
 Not complete at present.
Straw Poll 1: Given that multiple schemes can be easily be accommodated, should TGbh include more than one scheme in the Draft such that, for example, pre-association use cases may be addressed? Y: 17/ N: 3/A: 2
Not complete at present.
11bh group plan to deliver draft1.0, which means all features design is completed.
11bh group has to defer its schedule again if it can’t complete the task.

## Slide 3: Motivation
To make some progress and move forward, 11bh group should support at least one solution to address the use case 4.1,4.2, 4.8 and 4.26 before/in the following plenary meeting.
Candidate proposals list:
(1) RRCM (Okan)
(2) MAAD (Graham)
(3) IRMA (Graham)
(4) Other possible solutions

## Slide 4: WPA3_specification
9.1.3 Active Scanning Procedures
When performing active scanning procedures, the STA shall construct a randomized MAC address following the requirements defined in in Section 12.2.10 of [1], for transmission of Probe Request frames. The STA shall use a randomized MAC address for scanning while the STA is not associated to a BSS. The STA shall construct a new randomized MAC address for each active scanning instance.
9.1.4 ANQP Procedures
For each ANQP exchange, a STA shall use a new randomized MAC address following the requirements defined in Section 12.2.10 of [1], while the STA is not associated to a BSS

## Slide 5: TGbh PAR Scope (emphasis added)
This amendment specifies modifications to the medium access control (MAC) mechanisms to preserve the existing services that might otherwise be restricted in environments where STAs in an ESS use randomized or changing MAC addresses, without affecting user privacy. User privacy includes exposure of trackable information to third parties or exposure of an individual's presence or behavior.
This amendment introduces mechanisms to enable session continuity in the absence of unique MAC address-to-STA mapping. For STAs in an ESS that use randomized or changing MAC addresses, this amendment preserves the ability to provide customer support, conduct network diagnostics and troubleshooting, and detect device arrival in a trusted environment.
There is a need to:
Ensure that IEEE Std 802.11 provisions that refer to a STA MAC address remain valid when that MAC address is random or changes.
Design mechanisms that enable an optimal user experience when the MAC address of a STA in an ESS is randomized or changes. These mechanisms should not decrease user privacy.

## Slide 6: Comparison among the proposals-1
 | RRCM | MAAD | IRMA
Use case 4.1(pre-association client steering) | Different RMAs for different mgmt. frames. RMA1probe RMA2ANQP RMA3 authentication | Same RMAs for different mgmt. frames. RMA1 probe RMA1ANQP RMA1  authentication | Same RMAs for different mgmt. frames. RMA1 probe, RMA1ANQP RMA1 authentication
Use Case4.2(access control) | Similar to use case 4.1 | Similar to use case 4.1 | Similar to use case 4.1
Use case 4.8(post-association client steering) | Different RMAs for different probes. RMA1 for probe1. RMA2 for probe2. | Same RMAs for different probes. RMA1 probe(s) | Same RMAs for different probes. RMA1 probe(s)
Use case 4.26(VBSS) | Similar to use case 4.8 | Similar to use case 4.8 | Similar to use case 4.8

## Slide 7: Comparison among the proposals-2
 | RRCM | MAAD | IRMA
Overhead issue | Low Overhead, STA may not generate RMA(s) in each association. | High overhead, AP has to assign a new RMA in each association | High overhead, STA has to generate a new RMA in each association
RMA Conflict issue | No (RMA relies on PTK) | No (AP assigns RMA) | Yes (Different STAs may use same RMA)
WPA3 specification scope | Supported (each probe use different RMAs) | Not Supported (such as use case 4.8 and 4.26) | Not Supported (such as use case 4.8 and 4.26)
3rd party tracking issue based on unprotected MGMT. frame | Can’t be tracked. MGMT. frames use different RMAs. | Easy to be tracked. MGMT. frames uses same RMA. | Easy to be tracked. MGMT. frames uses same RMA.
11bh PAR scope | Supported (STAs using several RMA(s), not deceasing user privacy) | Not supported (3rd party can locate the user based on STA’s “same” RMA) | Not supported (3rd party can locate the user based on STA’s “same” RMA)
Computational cost | Yes (key and RMA generation) | No | No
Extend to 11bi | Possible in the future | Not clear | Not clear

## Slide 8: Computational Cost of old IRMA
Example, 1 million STAs information stored in the network.
In their first association, STAs generate their keys IRMKs (IRMK1… IRMK-1M), send them to AP. AP maps them and stores them.
In the subsequent association,
  A STA generates its IRMA –x and HASH-x and sends HASH-x to AP in association req frame.
  When AP wants to identify the STA-x, the procedure is as follows:
    Use the stored IRMK-m and IRMA-x to calculate the HASH-m, if HASH-m doesn’t match HASH-x, use the next IRMK to repeat.
    In the worst case, AP needs to go though the whole DB and calculate 1M times to find the matched HASH value.
STA1 <-> IRMK1 | …. | STA-1M <-> IRMK-1M
HASH1 == HASH(IRMA-x, IRMK1). -> NO HASH2 == HASH(IRMA-x, IRMK2). -> NO …………………………………………………………… HASH-1M == HASH(IRMA-x, IRMK-1M). -> YES
Therefore, the computational cost relies on the DB length.
e.g. n STAs keys stored in the DB, the AP may calculate N times to identify each STA in worst case.(computation NO. =n)

## Slide 9: Computational Cost of RRCM
Example, 1 million STAs information is stored in the network. (note: each STA generates two RMAs)
In their first association, STAs and AP generate their keys (RMAK1, RMAK2, RMAK3) and RMAs (RMA1.1, RM1.2 etc). AP maps RMAs and stores them.
In the subsequent association,
  STAs uses the generated RMAs.
  AP receives RMAs (from STAs SA) and identifies the STA immediately.
STA1 <-> RMA1.1, RMA1.2 | …… | STA-1M <-> RMA-1M.1,RMA-1M.2
RMA1.1, RMA1.2 => STA1 ……………………………. RMA-1M.1, RMA-1M.2 => STA-1M
In this example (1M STAs), to identify one STA , AP computational NO. = 2 (equal to generated no of RMAs). Generally speaking (n STAs), to identify one STA, AP needs m computation for each STA, where m is the number of generated RMAs and m << n.

## Slide 10: Computational Cost of RRCM & old IRMA
Chart: Computations needed to identify one STA
IRMA | 1 | 2 | 3
RRCM (single RMA) | 1 | 1 | 1
RRCM (multiple RMAs) | 1.2 | 1.2 | 1.2
The reason of high computation in old IRMA is that -> In first association, AP just stores many key values. -> In the subsequent association, AP goes though the whole DB to calculate HASH and compares it one by one.

## Slide 11: Reference
[1] 802.11bh draft 0.2
[2] 11-22-0924-00-00bh-802-11bh-telecon-minutes-june-21-2022.docx
[3] 11-21-0332-37-00bh-issues-tracking.docx
[4] WPA3 Specification version 3.0
[5] 11-22-0908-01-00bh-multiple-schemes-for-tgbh.pptx

## Slide 12: SP1
In order to move forward and make some progress, do you agree Opt(X) should be used as the solution to the use case 4.1, 4.2, 4.8 and 4.26?
Opt1: RRCM (Okan)
Opt2: MAAD and/or IRMA (Graham)
Opt3: Abstain

## Slide 13: SP2
Do you agree the proposed text in 11-22/888r2 should be incorporated into TGbh Amendment?
Y/N/A

## Slide 14
THANK YOU 