## Slide 1: WLAN Sensing Measurement CSI Report with Rx Frequency Response Category Index
Date: 2022-08-03
Authors:
Name | Affiliation | Address | Phone | Email
Shuling (Julia) Feng | Mediatek Inc | 2840 Junction Ave, San Jose, CA 95134, USA |  | julia.feng@mediatek.com
Jianhan Liu |  |  |  | jianhan.liu@mediatek.com
Thomas Pare |  |  |  | thomas.pare@mediatek.com
Kevin Tsai |  |  |  | kevin.tsai@mediatek.com

## Slide 2: Introduction
Sensing receiver adjusts LNA, VGA, and digital gain settings when receiving a NDP frame [1].
  Due to power measurement errors, the receiver may use different LNA, VGA, and digital gain settings receiving different sensing NDP frames even if they are transmitted at the same power level in the same channel environment.
LNA switches / VGA adjustments may cause RF / analog filter changes and result in variations of normalized Rx frequency response.
  Rx frequency response can be obtained as CSI in a loopback test. It can further be normalized with total gain in the receiver chain leading to CSI estimation.
  Rx frequency response vs gain variations my change with bandwidth

## Slide 3: Rx frequency response variations are product dependent
Some receivers may have frequency response variations significant enough to affect CSI estimation accuracy, and further affect sensing performance, especially when small CSI variations are expected between sensing instances [1].
Some receivers have consistent frequency response, and variations can hardly be distinguished.
  It maybe achieved by chip vendors design consistency
  It maybe achieved by chip vendors specially designed calibrations and compensations
Some receivers have frequency response variations only in limited cases
Since 11bf targets minimum PHY changes, we need to have a scheme to accommodate all these existing Rx frequency response cases.

## Slide 4: Categorize Rx Frequency Response Variations
Rx frequency responses can be categorized into limited groups with underlying circuit conditions based on their variations
  If a receiver’s frequency responses vary with LNA/VGA gain settings, they can be categorized into major groups. Each group corresponds to one or multiple of the LNA/VGA gain settings, and it can be numbered with a Rx operating point (OP) index.
  Within each group, Rx frequency response variation is considered insignificant.
  Categorization could be based on metric(s) derived from magnitude and/or phase variations of the Rx frequency response
  The details of rules to categorize Rx frequency response will be further discussed

## Slide 5: Benefit of Reporting Rx OP Index in 11bf Sensing
Sensing initiator may use Rx OP index to control combination or comparison of CSIs obtained from successive sensing NDPs for the same measurement setup ID in a sensing session
  Rx OP index is fed back to sensing initiator along with CSI during sensing measurement report.
  Rx OP index may help sensing initiator to detect small CSI variations reliably.
    CSIs with the same valid Rx OP index are generated with the same category of normalized receiver frequency response, and they can be combined for better sensing performance or compared for sensing detection if necessary.
  Depending on types of applications, initiator can also choose to combine or compare CSIs with different Rx operating index after assessing CSI variation risks caused by Rx frequency response changes.
  Rx OP index is determined by sensing receiver with its best effort.

## Slide 6: Rx OP Index Values
A chip vendor has flexibility with Rx OP index depending on normalized Rx frequency response variations.
  A chip vendor may not categorize Rx frequency response variations and will set Rx OP index to an invalid value to indicate this status.
  A chip vendor may set Rx OP index to a fixed valid value to indicate its Rx frequency response doesn’t vary significantly across all gain settings.
  For example, a chip vendor finds its Rx frequency responses vary in 4 major patterns in lab sample tests or selected gain setting product tests. It can categorize these variations and their underlying circuit conditions into 4 categories and map them to 4 valid Rx OP index values.

## Slide 7: Summary
Rx OP index helps to improve sensing performance when small CSI variations need to be detected by allowing combination or comparison of CSIs obtained from successive NDPs with the same valid Rx OP index value.
Rx OP index provides chip vendors flexibility to categorize Rx frequency response variations.
  Rx frequency response doesn’t vary significantly with the same valid Rx OP index value.

## Slide 8: Proposals
We propose to add Rx OP index along with CSI in 11bf sub-7GHz sensing measurement report to indicate categorization of normalized Rx frequency response variations
  Rx OP index is a category index of receiver operating point. It indicates various effects on CSIs caused by normalized receiver frequency response variations
We propose to add Rx_OP_Gain_Type to allow either Rx OP index or Rx gain index report
  Rx_OP_Gain_Type provides means to meet different types of requirements
  Receiver reports Rx OP index or Rx gain index at best effort
  Rx gain index report is proposed in 11-22/0647r7

## Slide 9: SP
Do you agree to add fields RX_OP_Gain_Type and Rx_OP_Gain_Index along with CSI in 11bf sub-7GHz sensing measurement report to indicate the Rx OP index or Rx gain index?
  RX_OP_Gain_Type: 2 bits (b1b0)
    00: neither Rx OP index nor Rx gain index is reported, and Rx_OP_Gain_Index values are invalid
    01: Rx OP index is reported in Rx_OP_Gain_Index. The details of receiver OP categorization method(s) are TBD
    10: Rx gain index is reported in Rx_OP_Gain_Index. The details of Rx gain index definition are TBD
    11: reserved
    Note: Receiver determines value of Rx_OP_Gain_Type as it sees the best fit. Rx_OP_Gain_Type value doesn’t change during a sensing measurement setup. No need of capability info to use this field. No need of initiator assigning the use of this field.
  Rx_OP_Gain_Index:
    It’s a fixed size field, number of bits TBD.
    Its content depends on the value of RX_OP_Gain_Type
    Reporting value per receive antenna is TBD
  Y
  N
  Abstain
Rx_OP_Gain_Type
Rx_OP_Gain_Index
(contains Rx OP Index or Rx Gain Index)
2 bits
# of bits TBD
Added fields

## Slide 10: Reference
[1] IEEE doc 802.11-22/0647r7, Information Exchange of WLAN Sensing Link