## Slide 1: Use Cases of smart manufacturing
Date: 2022-08-16
Authors:
Name | Affiliation | Address | Phone | Email
Shichao Zhao | Haier |  |  | zhaoshichao@haier.com
Zhaojuan Du |  |  |  | duzhaojuan@haier.com
Doc.: IEEE 802.11-22/1339r0
August 2022

## Slide 2
  Asset Management and Worker tracking
  Identification of human beings and assets including production materials, storage tanks, etc.
    Inventory check
    Anti-counterfeiting via ID tracing
    Attendance check
  Horizontal and vertical positioning of materials and products.
  Potential Requirements
  Small size, maintenance-free, battery-free, and ultra-low-cost IoT devices
  Coverage: 10-30 meters for indoor (a product line has an area of 25 thousands m2)
  Positioning accuracy: 1~3 m horizontal accuracy and 1~2 m vertical accuracy
Use Case 1: Identification and Positioning
Internet
Asset Management Platform
Shichao Zhao (Haier)
Doc.: IEEE 802.11-22/1339r0
August 2022
Slide 2

## Slide 3
  Sensing and Real Time Monitoring
    Motion and pressure detection
    Detection of gas leakage in gas tanks and pipelines
    Real-time temperature and humidity monitoring for computing and data centres, distribution boxes, and other equipment
  Potential Requirements
    Battery-free thus no need to replacing battery, low complexity and energy consumption
    Long lifespan, e.g., more than 10 years
Use Case 2: Environmental Sensing
Temperature/Humidity Sensor
Pressure Sensor
Gas Sensor
Motion Sensor
Ambient IoT Device
AP
Shichao Zhao (Haier)
Doc.: IEEE 802.11-22/1339r0
August 2022
Slide 3

## Slide 4
Example: Washing Drum Factory
Major Issues
Extremely high density deployment of RFID readers is required (one Reader for one process)
The placement of the readers should be adjusted frequently to avoid incorrect identification between adjacent working spots
RFID tags on the product trays can not be properly scanned even with a slight change of facing direction
Requirements:
Larger coverage thus less readers
Simpler and more efficient data collection
Much less stringent requirements for reader and RFID tag placement
State of the Art
Real time quality inspection and tracing of the assembly line is based on conventional RFID tags on the product trays
  The Product line occupies an area of 25 thousand m2 and it supports more than 20 process
Deploying a large number of readers to determine the product trays 'position
Collected info passed to the digital twin platform.
21.Automatic screw tightening
20. Automatic energy consumption sticker paste
18. Energy consumption sticker printer
19. Automatic backing
11. Automatic detection
10.Residual water extractor
9. Automatic draining pipe reinstall
7. Automatic water injection
6. Counterweight elevator
22. Automatic barcode paste
15. Foamed cabinet weight detection
3. Horizontal cabinet dimension detection
16. Vertical cabinet dimension detection
2. Inner and outer washing drum placement
3. Inner and outer washing drum reversal
4. Automatic cabinet scanning
17.Top computer board inspection
5.Automatic cabinet tilting
14. Real-time sensing of cabinet form temperature
8. Automatic vibrating block reinstall
12.Nameplate printer
13.Multi-code detection
Shichao Zhao (Haier)
Doc.: IEEE 802.11-22/1339r0
August 2022
Slide 4

## Slide 5: Summary
July 2022
Doc.: IEEE 802.11-22/1339r0
This submission presents
  Use of smart manufacturing
  The typical requirements of the use case, including
    Support Inventory, positioning, sensor data collection
    Small size, maintenance-free, battery-free, and ultra-low-cost IoT devices
    Coverage: 10-30 meters for indoor
    Positioning accuracy: 1~3 m horizontal accuracy and 1~2 m vertical accuracy