## Slide 1: IEEE 802.11 Coexistence SC Sep 2022 (hybrid) closing report
Date: 20220916
Authors:

## Slide 2: IEEE 802.11 Coexistence SC achieved its goals as a discussion forum for coexistence issues
802.11 Coex SC summary for Sep 2022 (11-22-1305)
  A summary of major outstanding issues given in mid session WG plenary (see 11-22-1613)
    Poor coex between Wi-Fi & LAA/NR-U likely in practice, with two obvious mitigations:
      LAA/NR-U is not used very much (a market decision)
      Avoidance by allocating 1200 MHz of unlicensed spectrum in 6 GHz (a regulatory decision)
    Possible coex issue between 802.11ax/be in 5 GHz in Europe, with contention on problem/solution
      802.11be defined to enable use of ED/PD @ -72/-72 dBm (an 802.11 WG decision)
      EN 301 893 (5 GHz) redefined to use ED-only @ -62 dBm (an ETSI BRAN decision)
  Similar (but slightly deeper) discussions occurred in the Coex SC session
    The request in both forums is for submissions ready for Nov 2022 to help determine whether there is a problem & an appropriate solution
  Coex SC also heard updates on increasing list of coex issues related to:
    SL-U, 60 GHz, BT in 6 GHz, 802.15.4ab UWB in 6 GHz, NB FH in 6 GHz, C2C & 6 GHz spectrum

## Slide 3: IEEE 802.11 Coexistence SC will continue promoting good coexistence with 802.11 in Nov 2022
IEEE 802.11 Coex SC will meet in hybrid mode in Nov 2022 …
  Updates on ETSI BRAN status
  Straw polls to start developing consensus on issues related to
    Coex between LAA/NR-U and Wi-Fi
      Possible submission from Sumit Roy (UoW) based on simulations
    Coex between 802.11ax/be in 5 GHz in Europe
      Submissions requested, particularly on ED-only @ -62 dBm proposal
  Updates on coex issues related to
    SL-U, 60 GHz, BT in 6 GHz, 802.15.4ab UWB in 6 GHz, NB FH in 6 GHz, 6 GHz & C2C
      Some submissions already promised, other submissions sought
… hopefully with Chair present
  …
Contributions are sought & encouraged!