## Slide 1: 802.15 Liaison Report – Sep. 2022
Date: 2022-09-15
Authors:

## Slide 2: 802.15.16t Narrow Band Licensed Operation (NB-Lic)
What is it:
  Licensed Narrow Band (NB) Operation in channels bandwidth between 5 – 100KHz in the VHF/UHF bands such as 160MHz, 450MHz, 700MHz and 900MHz, taking advantage of the superior channel propagation properties. Targeted usages mission critical operation.
Status:
  Completed the Use case, System Requirements and System Description documents and in the draft text development phase and supporting material.
Main discussion topics:
  Reviewed proposal for 16t channel model, basic PHY signal properties (PAPR analysis, Windowing, repetition, FEC) and initial air protocol proposals review.

## Slide 3: 802.15.4ab Next Generation UWB
What is it:
  Builds on 802.15.4z increasing footprint usefulness of the technology to additional usages beyond range measurement. Area of enhancements relates to ranging resiliency, sensing, data rates, support for additional spectrum, improved detection and many more.
Status:
  In Technical Specification Document (TSD) development phase.
Main discussion topics:
  Narrow Band Assisted UWB - transmission of 2MHz signal in the UNII3/5 bands to improve channel budget of the main UWB signal by providing synchronization base. On going discussion on coex and CCA mechanism.
  Additional modulation and coding schemes - Currently HRP UWB limited to BPM-BPSK, providing upto 27.24Mbps, seeking support for QPSK as well as additional FEC schemes.

## Slide 4: 802.15.4ab Next Generation UWB
Main discussion topics:
  Channelization schemes - Definition additional channels using partially overlapping channels for sensing purposes.
  Channel access mechanism - SSBD – Spectrum Sensing Based Deferral, mechanism similar to exponential backoff CSMA, but with linear window backoff.

## Slide 5: 802.15.13 Multi-Gbit/s Optical Wireless Communication
What is it:
  MAC and PHY project for the 10,000nm – 190nm wavelength for multi gigabit communication, with up to 10Gbps to distance of up to 200m, in LoS conditions.
Status:
  Draft in SA ballot series, just completed 3rd recirculation on D7.0.
  3rd SA Recirculation Ballot results: 78T, 1G, 74E, 97% approval rate.
  Targeting completion of ballot series and move to REVcom past the Nov. meeting (early Dec.).

## Slide 6: 802.15.6ma - Enhanced Dependability Body Area Network (ED-BAN)
What is it:
  Enhancements to the BAN (Body Area NW) Ultra Wideband (UWB) physical layer (PHY) and media access control (MAC) to support enhanced dependability to a human BAN (HBAN) and support for vehicle body area networks (VBAN).
  This revision focuses on international operation.
Status:
  Complete the Channel Model Document (CMD)
  Complete technical Document on MAC for enhanced dependability
  Complete Technical Requirement Document(TRD)

## Slide 7: 802.15.7a Optical Camera Communication
What is it:
  Amendment to provide higher rate, longer range optical camera communication.
Status:
  Completed response for WG comment collection, published D2.0 and initiate WG letter ballot on the D2.0 and the accompanying Coexistence Assessment document.

## Slide 8
TG4me
Cor1 15.4 2020 Revision 1
TG4ab
Next Generation UWB
TG6ma
Body Area Networks
Revision
TG7a
Optical Camera Communications
TG13
Multi Gigabit/sec
Optical Wireless Communication
TG15
Ultra Wide-Band Ad-Hoc Networks
TG16t
Ultra Wide-Band Ad-Hoc Networks
TG3mb
TG HDR
High Data Rate
Revision
SCTHz
Standing Committee THz
SCmaint
Maintenance Group
SCWNG
Wireless Next Generation
SCIETF
IETF liaison