## Slide 1: Wi-Fi Meets ML: Re-thinking Next-generation Wi-Fi Networks (Nov tutorial)
Date: 2022-11-14
Authors:

## Slide 2: Abstract
In this tutorial, we provide a brief and concise overview of standard ML techniques, as well as how they have been applied to 802.11 by the research community in the last years. Finally, we show what can be done by the WG to support ML in the 802.11 standard.

## Slide 3: Boris Bellalta
Full Professor at UPF
Head of the Wireless Networking group
  Unlicensed bands, 802.11
  XR Immersive Communications (over 802.11)
ML interest: ‘intelligent’ adaptive systems; low-complexity RL agents; interplay between ML agents;
Contact: boris.bellalta@upf.edu

## Slide 4: Szymon Szott
Associate professor at AGH University of Science and Technology, Kraków, Poland
Research interests
  Wireless local area networks
  Channel access
  Quality of service
  Security
  Inter-technology coexistence
ML interest: clever ways to improve performance
Contact:
  szott@agh.edu.pl
  https://szymonszott.github.io/

## Slide 5: Acknowledgements
Katarzyna Kosek-Szott, Piotr Gawłowicz, Jorge Torres Gómez, Anatolij Zubow, Falko Dressler, co-authors of the survey paper “Wi-Fi Meets ML: A Survey on Improving IEEE 802.11 Performance with Machine Learning” in IEEE Communications Surveys & Tutorials, vol. 24, no. 3, pp. 1843-1893, third quarter 2022, doi: 10.1109/COMST.2022.3179242. [1]
From projects:
  WI-XR PID2021-123995NB-I00 (MCIU/AEI/FEDER,UE)
  National Science Centre, Poland, under Grant DEC-2020/39/I/ST7/01457

## Slide 6: Outline
Does 802.11 need ML?
Using ML to build models from data
  AI/ML definitions
  Overview of ML techniques: supervised, unsupervised, reinforcement learning
Model training and deployment: centralized and distributed solutions
  Definitions and concepts
  Federated and Transfer Learning
Open challenges, missing pieces and summary

## Slide 7: 1. DOES 802.11 NEED ML?

## Slide 8: Challenges of IEEE 802.11 Networks
Increasing complexity of each new PHY/MAC amendment
  Plethora of parameters
  Optimal configuration outside scope of the standard
  Joint parameter optimization: non-linear!
New application requirements
  VR/AR/metaverse, cloud gaming, TSN
  Ultra-high reliability
Uncertainty
  Coexistence with other technologies
  Network densification
  Uncoordinated deployment
Band [GHz] | 2.4, 5, 6 …
Channel number | 32, 36, 40, …
Channel width [Mhz] | 20, 40, 80, …
Guard interval [ns] | 400, 800, 1600, …
Coding rate | 1/2, 2/3, 3/4, 5/6, …
Modulation | BPSK, QPSK, 16-QAM, 64-QAM, …
Contention window | 15, 31, 63, …

## Slide 9: Solution: Machine Learning (ML)
In ML, “algorithms can learn from training data without being explicitly programmed” [9]
Questions that ML could answer for 802.11:
  In XR streaming, can we predict connection degradation enough in advance to perform preventive actions?
  In 802.11ad/ay, can we reduce beam sector alignment time by learning from historical data?
  In MLO, can we select the best links based on monitored statistics?

## Slide 10: Augmented 802.11 with AI/ML
Should we expect that the use of ML techniques will…
  … improve raw ‘performance’ (i.e., throughput, delay and reliability)?
  … improve QoE in general (i.e., better AP selection)?
  … contribute to avoid BSS ‘starvation’ in dense scenarios?
  … contribute to reduce ‘overheads’ by reducing the amount of exchanged data?
  … contribute to improve the operation/performance of some functionalities?
  …
Any initial target? 4x gains? 10%? Only qualitative?
?

## Slide 11: Research applications of ML to 802.11
802.11 Area | ML objective | ML methods | Improvement
Channel access | Select CW value, modify CW update rule | Mostly RL | Higher throughput
Link adaptation | Select transmission rate Predict link-layer throughput | Mostly RL SL | Higher throughput
PHY | Classify signal source, de-noise signals estimate interference | Mostly SL | Higher accuracy
Beamforming | Select beam sector, beamwidth, transmit power Predict channel characteristics | Mostly SL | Higher throughput, reduced exploration time
Multi-user | Select users, schedule RUs | SL and RL | Higher throughput
Spatial reuse, channel bonding | Select channel, transmit power, carrier sense threshold | Mostly RL | Higher throughput, lower latency

## Slide 12: Which ML methods are used?
SL and RL are frequently used, while UL is less popular.
The most often used ML mechanisms are Q-learning, multi-armed bandit, as well as different neural network types (mostly ANN, DNN, and CNN), usually implemented to optimize a constrained set of 802.11 parameters.
With the increase in available computing power, DL methods are gaining in popularity.
Federated learning and transfer learning are a recent introduction in the 802.11 domain.

## Slide 13: IEEE 802.11be and beyond
Is there any 802.11be feature suitable to be enhanced with ML?
  New MCSs (4096-QAM)
  Up to 16 spatial streams
  320 MHz channels
  Wide-band channel access + OFDMA improvements (Multi-RUs per user)
  Multi-link Operation - new feature!
  Multi-AP coordination
ML research done for similar features in previous amendments could be re-used & extended: improved symbol detection under ‘low’ SNR, beamforming, group selection for MU-MIMO transmissions, channel width selection and DBCA policies, etc.

## Slide 14: Multi-link Operation
Several operation modes:
  MLSR, eMLSR
  eMLMR-STR
  eMLMR-NSTR
Improving MLO with AI/ML?
  Selection of the active links based on both traffic prediction and link occupancy (trade-off between power consumption and latency)
  Enhanced channel access schemes: predict when multiple links will be simultaneously available to improve link aggregation in NSTR.
  Learn optimum traffic allocation to different links
  …
Illustration of SLO, MLO-STR, and MLO-NSTR operations [8]

## Slide 15: Outline
Does 802.11 need ML?
Using ML to build models from data
  AI/ML definitions
  Overview of ML techniques: supervised, unsupervised, reinforcement learning
Model training and deployment: centralized and distributed solutions
  Definitions and concepts
  Federated and Transfer Learning
Open challenges, missing pieces and summary

## Slide 16: 2. USING ML TO BUILD MODELS FROM DATA

## Slide 17: Artificial Intelligence and Machine Learning
Artificial Intelligence: collect/sense (get the data), reason (interpret the data), act (based on how the data is interpreted), enjoy (or not) the result, and self-correct / adapt.
  AI uses ML techniques to extract “knowledge” (learn) from the data
  Data + ML Algorithms + Reasoning + Actions→ (A)Intelligence
Machine Learning: Set of algorithms / techniques / mechanisms that are able to learn from data.
  Learn: map output to inputs, i.e., build the function f(.) that represents the ‘knowledge’
  General mechanisms, not explicitly programmed for a single family of functions f(.); In some cases, their performance/learning bounds are known
Deep Learning: Includes learning the relevant ‘features’ of the model.
Intelligent agent:
body + policy (brain)
AI
ML
DL

## Slide 18: Building models
The ML model is f(.), it describes a system.
ML enables to model extremely complex systems by characterizing the hidden relationships between input parameters x (features) and outputs y (labels).
Example: To train a model able to suggest the best MCS to exchange data between the AP and laptop.
MCS?
Features
- RSSI
- Throughput
- PER
- Coll. prob.
- SS
- Bandwidth
MCS
Model

## Slide 19: Why is having a model useful?
A model can give us some useful information before taking (better) decisions.
It can predict what will be the ‘performance’ (output) given a certain configuration (input).
Example: Given a certain scenario, we want to find the configuration that maximizes the throughput

## Slide 20: Why is having a model useful?
A model can give us some useful information before taking (better) decisions.
It can predict what will be the ‘performance’ (output) given a certain configuration (input).
Example: After gathering data from different APs (load, number of associated clients, technology & capabilities, RSSI, etc. ) a STA can sequentially predict which is the best AP to associate.
?
good RSSI, 11ax, 80% busy
medium RSSI, 11n, 10% busy
A
B
B

## Slide 21: ML techniques build models from data (training)
Two training cases:
  Off-line: using a static dataset (present from the beginning).
  On-line: the dataset is created in real-time, so the model is updated as more data is collected.
Training is based on minimizing the error between what is known (in the dataset) and predicted (by the model) outputs.
Models should be as general as possible: the aim is not to exactly map inputs and outputs, but to learn the context behind any existing relationship (no overfitting).
A model can be first trained off-line, deployed and then improved with on-line training

## Slide 22: Taxonomy of ML models
Supervised Learning (SL)
Unsupervised Learning (UL)
Reinforcement Learning (RL)
How are these models trained?
  Centralized; Decentralized / Distributed
  Single player; Multiple players
Ex: Distributed Federated Learning

## Slide 23: Supervised Learning
Goal: Training data includes x and y, so the goal is to learn f(.)
Dataset: We need a consolidated dataset to train the model, retraining it as the dataset updates
Techniques: Time series analysis, Regressions, Vector Machines, Decision Trees, Neural Networks, etc.
Main uses: Prediction (output is a real value), Classification (output is a label, e.g., 0 or 1)
802.11 example: AP selection
  The STA uses a trained model that predicts which is the best AP to associate. The input of the model should consist of the info gathered by the STA for each AP.

## Slide 24: An 802.11 dataset
The dataset was created running 100,000 simulations with input parameters selected randomly.

## Slide 25: Example: Linear Regression
Results can be easily improved by using multivariate regression and a nonlinear model

## Slide 26: Example: Neural Network
Matlab NN representation
Input layer
Hidden layer
Output layer
Predicted Throughput
Prediction (Mbps)
Real Value (Mbps)
CWmin

## Slide 27: Example: Neural Network
Matlab NN representation
Input layer
Hidden layer
Output layer
Predicted Throughput
CWmin
We can use the NN model to try different CWmin values to see which is the best performing one.

## Slide 28: Unsupervised Learning
Goal: Find patterns/trends/similarities in a dataset when only the features are available
Dataset: We need a consolidated dataset to train the model, retraining it as the dataset updates
Techniques: K-means, Self-Organizing Maps (SOMs), hidden Markov model (HMM), Auto encoders (AEs), Principal Component Analysis (PCA), Restricted Boltzmann machine (RBM), fuzzy C-means etc
Main uses: Cluster the data in similar groups
802.11 example
  AP selection from a dataset that contains only the features. Then, identifying which APs are similar may reduce the ‘testing’ phase by only requesting association to an AP of each representative ‘cluster’.

## Slide 29: Reinforcement Learning
Goal: Learn from experience (relationship between actions and rewards)
Dataset: sequence of actions and rewards obtained
Techniques: Multi-armed Bandits, Q-learning, DQL
Main uses: Adaptive systems in dynamic environments
802.11 examples: exploration – exploitation tradeoff
  AP selection by trying and rating different APs
  Dynamic channel selection: given a set of unknown channels, we need to find the best one (the emptiest one)
  Dynamic configuration of Tx Power and CCA to support Spatial Reuse
  etc.

## Slide 30: Reinforcement Learning
An ‘agent’ learns by interacting with the ‘environment’
  The agent can play different ‘actions’
  For each action, the agent receives a ‘reward’
  If possible, the agent may characterize the environment through a set of ‘states’
The ML algorithm tells the agent how to select the actions to maximize the reward

## Slide 31: RL vs standard ‘rule-based’ protocols?
RL naturally adapts to different situations.
but…
  … requires time to learn.
  … higher computational resources.
The two approaches can be also combined.
Example: We can learn the protocol.
A
B
C
D
A
B
C
D
Pre-programmed
Learned

## Slide 32: Actions, Rewards and States
Consider the case of a robot moving in a map.
Each position of the map is a ‘state’.
Actions: the movements that can be done in each state.
Rewards: how close is the robot to the End; and/or if there is an obstacle.
Moving results in a reward, but also moves the system to a new state.
It is not clear how to define states in 802.11, as sometimes the state is equivalent to the ‘action’ (i.e., the selected AP or channel).
Wireless scenarios are hardly ‘static’, and so the same action may have different outcomes.

## Slide 33: Multi-armed Bandits (MABs)
Sequential interaction between the ‘agent’ and the environment.
No states (or just a single state), only actions and rewards.
Exploration-exploitation trade-off. The agent:
  Explores: selects an action randomly
  Exploits: selects the action with higher reward from the table
Different approaches: simple, low-computing res.
  ε-greedy, Thompson Sampling, UCD, EXP3, etc.
Contextual MABs consider different situations:
  E.g. AP selection at home, at work
  Moving to a new ‘context’ may allow to reuse past info.

## Slide 34: Example: Channel Selection (MABs)
Smart AP
1
2
3
N
channels
ai
bi
0
1
ρ(i) = Occupancy of channel i [0,1]
(measured every 1 second)
Reward using channel i: V(i) = 1-ρ(i)
?
Only the channel in use can be measured

## Slide 35: Example: Channel Selection (MABs)
Smart AP
1
2
3
N
channels
ai
bi
0
1
Reward using channel i: V(i) = 1-ρ(i)
?
Only the channel in use can be measured
ρ(i) = Occupancy of channel i [0,1]
(measured every 1 second)

## Slide 36: Q-learning
It requires states:
  Same or different actions depending on the state
  Actions can result in a ‘change’ of state
  Rewards depend on the state
We need a mechanism to explore the environment
  e.g., ε-greedy
We need a mechanism to update Q-table based on the obtained rewards (Bellman eq.)

## Slide 37: Example: Channel Selection (Q-learning)
Smart AP
?
1
2
channels
Actions: remain in the same channel; change channel
States: channel 1 and empty; channel 1 and busy; channel 2 and empty; channel 2 and busy
remain
change
A channel can be busy or empty

## Slide 38: Example: Channel Selection (Q-learning)
Smart AP
?
1
2
channels

## Slide 39: Deep Q-learning (DQN)
Problem: Accurate learning of the Q-table is difficult (or impossible) and time consuming when the number of states is large as the agent needs to go through all the different states and actions several times.
Solution: Model the Q-table response with a (Deep) Neural Network.
  If the system is in state ‘s’, the agent asks the (D)NN to predict the reward the agent will obtain if plays any of the available actions in state ‘s’.
  The agent selects the action with a higher predicted ‘reward’.
  DQN’s additional deep neural network allows for more efficient extrapolation of rewards for yet unseen states as compared to basic Q-learning.
Challenge: to train on-line the (D)NN, as it may require large CPU/GPU resources.

## Slide 40: Example: DQN for CW optimization [2]
Agent - installed at the AP
State - status of all connected devices
Action - select CW (value of integer a)
Reward - network throughput
Observation - collision probability
DNN: 8 × 128 × 64
Exploration: random action w/ low probability

## Slide 41: Example cont’d
Throughput improvement over 802.11
Mean selected CW in consecutive training rounds
(static scenario: 30 stations)
DQN - Discrete action space
DDPG - Continuous action space

## Slide 42: Re-cap
Machine Learning → techniques to create ‘models’ from data
  Supervised Learning: Make predictions, classify
  Unsupervised Learning: leverage similarity
  Reinforcement Learning: interact with the environment
Use-cases / Examples:
  Pre-trained SL models for AP selection (association)
  RL for CW/channel selection in dynamic environments
The capability of ML to go beyond rule of thumb strategies by automatically learning (and adapting) to (un)seen situations can cope with heterogeneous wireless network scenarios

## Slide 43: Outline
Does 802.11 need ML?
Using ML to build models from data
  AI/ML definitions
  Overview of ML techniques: supervised, unsupervised, reinforcement learning
Model training and deployment: centralized and distributed solutions
  Definitions and concepts
  Federated and Transfer Learning
Open challenges, missing pieces and summary

## Slide 44: 3. MODEL TRAINING AND DEPLOYMENT

## Slide 45: Training and deploying an ML model
Training: building the model from data.
Deployment: place where the model is used.
Example: Realization of the ITU’s ML architecture for IEEE 802.11 WLANs through a hybrid ML-based solution for AP (re)association and handover.
Francesc Wilhelmi, Sergio Barrachina-Muñoz, Boris Bellalta, Cristina Cano, Anders Jonsson, and Vishnu Ram. "A flexible machine-learning-aware architecture for future WLANs." IEEE Communications Magazine 58, no. 3 (2020): 25-31. [3]
SSF - Strongest signal first (802.11 baseline)

## Slide 46: Training an ML model
Local models: Only the data available in a single device is used.
  Example: A non-AP device learns the best MCS to use for its uplink transmissions
Global models: The data from multiple devices is used to build the model.
  From the same BSS: Data coming from different devices is used to build a single model
    Example: non-AP devices send data to the AP to build a ML model
  From different BSSs, etc.

## Slide 47: Data and model exchange
Devices exchange the data to:
  A single point (centralized), where the ‘global’ model is trained using all data collected.
  Between them (distributed), each device is able to compute the ‘global’ model using all data collected.
Devices share their ‘local’ models to:
  A single point (centralized), where the ‘global’ model is computed by combining the different ‘local’ models.
  Between them (distributed), each device is able to compute the ‘global’ model by combining the different ‘local’ models.

## Slide 48: Deploying a (global) ML model
In the centralized case, the device training the ‘global’ model distributes it to the end devices.
In the distributed case, since all devices compute it, they already have it.
Pros and Cons
  Sharing the data:
    Large overheads
    Computing resources required to compute the model
    Accurate models can be built
  Sharing the model
    Less overheads (but depends on the model type)
    Loss of accuracy as the model is ‘averaged’, but it can be also seen as a ‘generalization’
    Lower computing resources required
  Distributed vs centralized
    Distributed supports higher flexibility and resilience, but likely more overheads

## Slide 49: Training and deploying an ML model
Federated Learning: devices exchange their locally trained ‘global’ models.
  Centralized or distributed.
  Iterative process: The deployed ‘global’ model is re-trained locally using the data gathered by each device to generate a new updated ‘local’ model.
  Only the ‘model’ is shared by participating devices.
    SL: the weights of a NN
    RL: Q-table, instantaneous rewards
Example / Proposal [12]
  Leverage the over the air Multi-AP Coordination framework to exchange local models to support FL in next-gen. 802.11 networks

## Slide 50: Example: FL with MABs for SR [4]
Un-coordinated Spatial Reuse can result in unfairness
APs share their ‘rewards’ and agree to maximize a certain utility function:
  average, max-min, proportional fairness, etc.
Individual AP rewards can be shared periodically in beacon frames
Wilhelmi, Francesc, Sergio Barrachina-Munoz, Boris Bellalta, Cristina Cano, Anders Jonsson, and Gergely Neu. "Potential and pitfalls of multi-armed bandits for decentralized spatial reuse in WLANs." Journal of Network and Computer Applications 127 (2019): 26-42.
AP #1
AP #2
‘Model’ sharing
Configuration update
Performance Monitoring
beacon

## Slide 51: Example: FL with MABs for SR [4]
AP A and B a) RL (2 local models); b) FRL (1 global model)
Wilhelmi, Francesc, Sergio Barrachina-Munoz, Boris Bellalta, Cristina Cano, Anders Jonsson, and Gergely Neu. "Potential and pitfalls of multi-armed bandits for decentralized spatial reuse in WLANs." Journal of Network and Computer Applications 127 (2019): 26-42.

## Slide 52: Transfer Learning
Transfer the already distilled ‘knowledge’ between different (but similar) ML tasks.
Motivation: reduce learning / training time.
Example: AP on/off switching scheme for energy saving
ML vs TL [7]

## Slide 53: Re-cap
Training and deploying models: centralized vs distributed
Federated Learning: sharing models (knowledge) instead of the data
Transfer Learning: reusing knowledge from different technologies

## Slide 54: Outline
Does 802.11 need ML?
Using ML to build models from data
  AI/ML definitions
  Overview of ML techniques: supervised, unsupervised, reinforcement learning
Model training and deployment: centralized and distributed solutions
  Definitions and concepts
  Federated and Transfer Learning
Open challenges, missing pieces and summary

## Slide 55: 4. OPEN CHALLENGES, MISSING PIECES, & SUMMARY

## Slide 56: AI/ML for 802.11 - Open Challenges
More research is required
New simulation & experimental tools
Assessment of AI/ML gains in practice
IEEE 802.11 contribution
  Architecture & interfaces
  New ‘components’ to support ML
  Reference scenarios
Real use-cases & practical use-cases required

## Slide 57: Research
Optimizing new 802.11 features
  Not yet well-known how ML can improve the performance of existing features
  What about new ones? Multi-link operation, multi-AP coordination
Joint parameter optimization
  Complex interplay between different features
  E.g., transmit power and carrier sensing threshold, channel/link selection
Distributed and transfer learning; hierarchical learning
  Training and sharing/deploying models in a distributed way
  Reuse of knowledge between features

## Slide 58: New simulation & experimental tools
802.11 networks are becoming extremely complex, with many new features, and deployed in many different scenarios.
We need (new) evaluation tools (and metrics) to obtain reliable and reproducible performance results: analysis, simulations, testbeds.
  Include AI/ML support
The case of ns-3:
  Full TCP/IP stack, 802.11, community validated
  Not all 11ax features yet implemented; some 11be ones in development
    Developing new features requires expertise and time
  AI/ML support:
    ns3-gym: OpenAI Gym integration

## Slide 59: Datasets
The existence of open-source and standardized datasets is essential for training and comparing ML-based algorithms.
Very few datasets are currently available.
Examples of datasets:
  Herzen et al. [10] provide a dataset to predict throughput based on basic performance metrics (e.g., received power, channel width) collected in a small testbed.
  Karmakar et al. [11] provide the IEEE 802.11ac performance dataset that contains information regarding normalized throughput achieved under five link configuration parameters (i.e., channel bandwidth, MCS, guard interval, MIMO, and frame aggregation) and the channel quality measured as SNR.
It would be beneficial to create standardized procedures for data collection to build new datasets.

## Slide 60: AI/ML in practice
Most of current results in the literature come from simulations:
  Many simplifying assumptions:
    Controlled (simple) scenarios, discrete time (iterations)
    Instantaneous and noise-free data: ideal ‘devices’ (no need to calibrate data), no estimation errors, etc.
    No ML overheads (data and model exchange) usually considered
  The ‘gap’ with performance results from real implementations could be significant
Engineering effort to set-up and test AI/ML solutions in practice is still required
  Suitable KPIs are required, including how and when to measure them
  When should AI/ML agents be triggered?
    Instability vs slow reaction;
    Should ‘thresholds’ be used to activate ML mechanisms?

## Slide 61: AI/ML in practice
Performance gains in practice
  While AI/ML MAC/PHY enhancements affecting specific mechanisms may be easy to evaluate (link parameter selection, CW adjustment, beamforming, etc.), it may not be easy to assess other AI/ML performance gains since they may appear only in particular situations (i.e., high loaded scenarios).
    Example: network-controlled client device association and band steering
  Fairness issues between AI/ML-enabled devices and legacy devices.

## Slide 62: What is required from 802.11? (1)
802.11 architecture
  Support for running AI/ML agents (i.e., entities in charge of executing ML models)
    A single complex agent per device vs multiple simple agents -per functionality- cooperating
    Embedded (802.11 layers) vs external (edge / cloud)
  Interfaces and protocols to exchange data and models between agents placed at the stations, APs, and edge/cloud servers
    Universal format to accommodate different data types
  Interfaces and protocols to exchange ML agents (logic installation)
    Network controllers install agents at both APs and client stations

## Slide 63: What is required from 802.11? (2)
Extra components (processing capacity, dedicated network interfaces) for ML
  Support for the AI/ML control loop
      Observe/monitor network
      Run ML model to predict future outcomes
      Make decisions based on the output of the ML model
… which may require:
    - Dedicated computing resources to run agents and train models
    - Dedicated network resources (either in-band or out-band) for data, models and agent exchange.
Reference evaluation scenarios
  They should include non-stationary and changing conditions (i.e., sudden change in number of devices, changes in spectrum occupancy, etc).

## Slide 64: Example Use Case: Airport Hotspot
Scenario | Without ML | With ML at AP | With ML at STAs
Operation | AP sends static parameters in beacons | AP runs ML algorithm and updates parameters on-the-fly and distributes them in beacons | AP sends pre-trained ML agent to stations upon association, stations run agent
New signaling over the 802.11 interface | No | No (*Yes) | Yes
Monitoring | N/A | At AP (*With info from STAs) | At STAs
Parameter optimization | None/minimal | Based on AP (*STA) knowledge | Based on STA knowledge
Performance | Good | Better | Best
Dense network, changing conditions, room for performance optimization
Parameter configuration set: CCA threshold, max TX power

## Slide 65: Summary & take-home messages
ML is a set of general techniques to create models for making predictions. They can be used to empower autonomous ‘agents’ to find suitable configurations in particular scenarios.
Given the decentralized nature of 802.11 deployments, the use of RL techniques looks like the natural choice to dynamically improve several features such as channel selection, spatial reuse, channel access parameters, etc.
Performance gains in practice may not be so obvious. AI/ML enhanced 802.11 networks should improve user’s Quality of Experience by providing a fast response to challenging situations.
The 802.11 architecture should be updated to effectively support AI/ML

## Slide 66: References
[1] S. Szott; K. Kosek-Szott; P. Gawłowicz; J. Torres Gómez; B. Bellalta; A. Zubow; F. Dressler, "Wi-Fi Meets ML: A Survey on Improving IEEE 802.11 Performance with Machine Learning," in IEEE Communications Surveys & Tutorials, doi: 10.1109/COMST.2022.3179242.
[2] Wydmański, Witold, and Szymon Szott. "Contention window optimization in IEEE 802.11 ax networks with deep reinforcement learning." In 2021 IEEE Wireless Communications and Networking Conference (WCNC), pp. 1-6. IEEE, 2021.
[3] Wilhelmi, Francesc, Sergio Barrachina-Muñoz, Boris Bellalta, Cristina Cano, Anders Jonsson, and Vishnu Ram. "A flexible machine-learning-aware architecture for future WLANs." IEEE Communications Magazine 58, no. 3 (2020): 25-31.
[4] Wilhelmi, Francesc, Sergio Barrachina-Munoz, Boris Bellalta, Cristina Cano, Anders Jonsson, and Gergely Neu. "Potential and pitfalls of multi-armed bandits for decentralized spatial reuse in WLANs." Journal of Network and Computer Applications 127 (2019): 26-42.
[5] Carrascosa, Marc, and Boris Bellalta. "Multi-armed bandits for decentralized AP selection in enterprise WLANs." Computer Communications 159 (2020): 108-123.
[6] Barrachina-Muñoz, Sergio, Alessandro Chiumento, and Boris Bellalta. "Multi-Armed Bandits for Spectrum Allocation in Multi-Agent Channel Bonding WLANs." IEEE Access 9 (2021): 133472-133490.
[7] Nguyen, Cong T., Nguyen Van Huynh, Nam H. Chu, Yuris Mulya Saputra, Dinh Thai Hoang, Diep N. Nguyen, Quoc-Viet Pham, Dusit Niyato, Eryk Dutkiewicz, and Won-Joo Hwang. "Transfer learning for future wireless networks: A comprehensive survey." arXiv preprint arXiv:2102.07572 (2021).
[8] M. Carrascosa, G. Geraci, E. Knightly and B. Bellalta, "An Experimental Study of Latency for IEEE 802.11be Multi-link Operation," ICC 2022 - IEEE International Conference on Communications, 2022, pp. 2507-2512, doi: 10.1109/ICC45855.2022.9838765.
[9] J. Wang, C. Jiang, H. Zhang, Y. Ren, K.-C. Chen, and L. Hanzo, “Thirty years of machine learning: The road to Pareto-optimal wireless networks,” IEEE Commun. Surveys Tuts., vol. 22, no. 3, pp. 1472–1514, 3rd Quart., 2020.

## Slide 67: References
[10] J. Herzen, H. Lundgren, and N. Hegde, “Learning Wi-Fi performance,”in 2015 12th Annual IEEE International Conference on Sensing Communication, and Networking (SECON), 2015, pp. 118–126.
[11] R. Karmakar, S. Chattopadhyay, and S. Chakraborty, “A Deep Probabilistic Control Machinery for Auto-Configuration of WiFi Link Parameters,” IEEE Transactions on Wireless Communications, vol. 19, no. 12, pp. 8330–8340, 2020.
[12] Wilhelmi, Francesc, Jernej Hribar, Selim F. Yilmaz, Emre Ozfatura, Kerem Ozfatura, Ozlem Yildiz, Deniz Gündüz et al. "Federated Spatial Reuse Optimization in Next-Generation Decentralized IEEE 802.11 WLANs." arXiv preprint arXiv:2203.10472 (2022).

## Slide 68: Backup slides

## Slide 69: Examples
ML-enhanced Decentralized AP selection using MABs
  Carrascosa, Marc, and Boris Bellalta. "Multi-armed bandits for decentralized AP selection in enterprise WLANs." Computer Communications 159 (2020): 108-123.
Gap analysis on feasibility: from research to practical implementation

## Slide 70: ML-enhanced Decentralized AP selection
Default AP selection is implemented considering only RSSI values
  A station associates to the ‘closest’ AP
This may cause that some APs are overloaded, while others are almost empty
ML solution: STAs use an ML agent to find an AP that is good enough to satisfy their traffic requirements.
The ML agent implements a MAB:
  Actions: APs in sight
  Reward: ratio Throughput/Load

## Slide 71: ML-enhanced Decentralized AP selection
Default ε-greedy MAB is enhanced with ‘stickiness’.
Stickiness aims to improve stability by reducing the number of STAs switching APs simultaneously, or in a short time interval
Idea: STAs stick to the last AP that satisfied their requirements for several association rounds before switching

## Slide 72: ML-enhanced Dec. AP sel.
Non overlapping channel allocation
16 APs, 64 STAs
Load STA: 4 Mbps

## Slide 73: ML-enhanced Dec. AP sel.
Pros:
Easy to implement without any major update on 802.11 devices
All network devices benefit even if they are not ML-enhanced
Fully decentralized solution
Reactive, adapts to any environment
Cons:
Learning by interacting with the environment is required, implying periods of ‘low performance’ due to bad choices
AP switching overheads
Practical aspects:
Temporal window to assess throughput performance
It could be the used in combination with pre-trained SL models to boost AP selection performance, or with 802.11 mng. approaches

## Slide 74: ML-enhanced Dec. AP sel. vs Load-aware AP sel.

## Slide 75: Examples
ML-enhanced decentralized channel selection (primary, width) using MABs and Q-learning
  Barrachina-Muñoz, Sergio, Alessandro Chiumento, and Boris Bellalta. "Multi-Armed Bandits for Spectrum Allocation in Multi-Agent Channel Bonding WLANs." IEEE Access 9 (2021): 133472-133490.
Gap analysis on feasibility: from research to practical implementation

## Slide 76: ML-enhanced Decentralized Channel Selection
“Realistic” 802.11 simulation environment (Komondor)
  Path-loss, SNIR, Dyn. Bandwidth Access, etc.
Traffic load AP (only DL traffic): 50 Mbps
80 MHz available (shared by all 4 BSSs)
W=20, 40 and 80 MHz
12 different channels
  4 x 20 MHz channels (1 position for the primary)
  2 x 40 MHz channels (2 positions for the primary)
  1 x 80 MHz channels (4 positions for the primary)
The goal is to ‘learn’ a good channel allocation as fast as possible

## Slide 77: ML-enhanced Decentralized Channel Selection
Multi-armed Bandits
Available actions correspond to the set of available channels
Rewards are computed taking into account the actual throughput during the simulation (in intervals of 5 s)
Channel switching time not considered (few ms)
Practical considerations:
Easy to implement on top of current 802.11 devices
Channel switching overheads need to be considered

## Slide 78: ML-enhanced Decentralized Channel Selection
Only the simplest MAB algorithms perform well
Unstable!

## Slide 79: ML-enhanced Decentralized Channel Selection
Can contexts or states aid learning?
  Two states (contexts) per BSS: satisfied (true) or not (false).
  Different actions can be selected taking the current state into account.
RL algorithms harnessing states or contexts do not boost the learning rate in short-term finite horizons like those studied in this work.

## Slide 80: ML-enhanced Decentralized Channel Selection
Large deployments:
  20x20 m^2
  6, 10 and 16 BSSs
Random per BSS traffic loads: 50, 100, 150 Mbps
W = 20, 40, 80, 160 MHz
160 MHz available spectrum
  32 combinations of channels
Both exploration-first and e-greedy can learn even in high-density deployments, outperforming by far static configurations. Besides, while exploration-first performs worse than e-greedy at the early stages of the simulation, it reaches much better performance as the simulation progresses.