## Slide 1: Thoughts on M-AP Coordination Principles
Date: 01-10-2022
Authors:
Name | Affiliation | Address | Phone | Email
Genadiy Tsodik | Huawei Technologies |  |  | genadiy.tsodik@huawei.com
Arik Klein |  |  |  | arik.klein@huawei.com
Shimi Shilo |  |  |  | Shimi.Shilo@huawei.com
Oded Redlich |  |  |  | oded.redlich@huawei.com

## Slide 2: Introduction
802.11be discussed Multi-AP coordination as a set of features that will bring additional efficiency gain and increase throughput when multiple OBSS share resources for a coordinated transmission
There were several high-level discussions and analyses of various M-AP coordination schemes. However, the main development phase was not carried out within the scope of 802.11be
Preliminary discussions of UHR SG show high interest in this topic
We see M-AP coordination as a wide topic with many aspects to analyze, discuss and design, thus it’s very important to create a set of assumptions that might be used as a baseline for a simpler and shorter development process
In this contribution we want to share our thoughts on M-AP coordination and provide assumptions and principles that can lay the foundations for an efficient and flexible M-AP support in UHR and beyond

## Slide 3: Short Recap
In [1] and [2] TGbe agreed on the following points:
Two main roles for APs that participate in a coordination were defined [3]:
  Sharing AP – the TXOP holder that shares its resources with other APs
  Shared APs – all the APs allocated with resources for coordinated transmission by the Sharing AP
The roles above are dynamic: A single AP is designated as a Sharing AP in a TXOP it obtains and can be designated as a Shared AP in a TXOP(s) obtained by other APs
There are several schemes discussed and considered as candidate schemes to be supported: Co-TDMA ,Co-OFDMA, Co-SR, Co-BF, JT and Co-UL MU-MIMO [4], [7] – [11]
In most of the discussions it was assumed that all the coordinated transmissions are triggered by the Sharing AP
Some discussions also mentioned the overhead required to manage the coordinated transmissions

## Slide 4: High-level M-AP Coordination Flow
M-AP coordination is composed of the following actions:
  OBSS M-AP Discovery – At first, APs need to discover other potential candidates for coordination and their capabilities, traffic needs, etc. on a constant basis [5], [6]
  General Coordination Parameters Setting and Approval – need to get a response (approval) from an AP before it can participate in coordinated M-AP transmissions using agreed static parameters
  Per Transmission Info Update – Sharing AP shares with other APs specific parameters (e.g. per PPDU) that are important for aligning a coordinated transmission
  M-AP Coordination Teardown – teardown of current M-AP Coordinated transmission

## Slide 5: Main M-AP Coordination Assumptions
As we mentioned in previous slides, M-AP coordination is a completely new feature with a lot of aspects to discuss
Following that we would like to bring up the following assumptions that may simplify and shorten the development process
  Coordination as a Long-term operation mode
  No relay among coordinating APs.
  The operating BW of Coordinated transmission includes all Primary channels of involved BSSs
  Preserve current BSS operation rules for Data Delivery
At the next slides we will provide more details for each of the assumptions above

## Slide 6: Coordination as a Long-term operation mode
We should consider M-AP coordination as a long-term operation mode (in particular, longer than a single TXOP) for the following reasons:
  AP will be willing to share its resources in TXOP it obtains with other AP(s) knowing that other AP(s) will reciprocate by sharing their resources with it when they will obtain their TXOP.
  Furthermore, analyzing the main actions of M-AP coordination, we recognize that some of the information and coordination parameters are independent of TXOP holder (Sharing AP) and are relevant for a period longer than a single TXOP
We can therefore divide the information and coordination parameters to two main categories:
  Long-term Info: to be updated with very low periodicity (for example, the network structure and candidates for coordination)
  Short- term Info: to be updated frequently, for example per each TXOP (or per PPDU if needed)
Thus we may consider M-AP coordination as a long-term operation mode (in particular, longer than a single TXOP) where some of the coordination parameters are constant during the coordination period and other parameters are updated at least per TXOP
Coordinated transmission
Coordinated transmission
Long-term info and parameters
Short-term info and parameters
Coordinated transmission

## Slide 7: No Relay among Coordinating APs
In order to simplify the design of the M-AP Coordination feature, we shall avoid relay of frames exchanged among APs
Thus, the Sharing AP shall be within range of all Shared APs in order to establish a coordinated transmission (i.e. the Shared APs can “hear” the Sharing AP and vice versa)
For example, in the figure on the right:
  AP4 and AP5 are not within the range of AP1 and AP2
  When AP1 is the sharing AP:
    AP2, AP3 are potential candidates for Shared APs.
    AP4, AP5 are not potential candidates for Shared APs.
  When AP3 is the sharing AP:
    AP1, AP2, Ap4, AP5 are potential candidates for Shared APs.
The above doesn’t apply to non-AP STAs (associated with a Sharing AP or Shared APs)
AP3
AP1
AP4
AP2
AP5

## Slide 8: M-AP coordination Operating BW
In order to assure the frame exchange between the sharing AP and each of the shared APs:
  The operating BW of the sharing AP has to include each of the 20MHz Primary channels corresponding to the (one or more) shared APs.
  The operating BW of the shared AP has to include the 20 MHz primary channel of the sharing AP.
  NOTE: see also [4]

## Slide 9: Preserve current BSS rules for Data Delivery
In order to simplify the design and avoid major fundamental changes in WLAN topology, each BSS should maintain its operation principles for data delivery independent of the other coordinated OBSSs as much as possible
From both AP’s & STA’s perspective, in majority of coordination schemes, M-AP coordination has no impact on data delivery operations within the BSS (compared to communication without M-AP coordination)
Joint transmission may be a special case where BSS rules might need to be modified
  Unlike other coordination schemes, in joint transmission there is data exchange between an AP and OBSS STAs
  This needs to be further discussed and investigated by the group

## Slide 10: Summary
This contribution brings our thoughts on several high-level aspects related to M-AP coordination
M-AP coordination is a new operation mode that should be wisely incorporated into the WLAN network
Due to the large scope of this feature, as a first step it’s very important to create a set of baseline assumptions
  Agreed baseline may promise easier and shorter development time period

## Slide 11: References
[1] 11-20-0566-99-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document
[2] 11-20-1935-66-00be-compendium-of-straw-polls-and-potential-changes-to-the-specification-framework-document-part-2
[3] 11-20-1895-02-00be-setup-for-multi-ap-coordination
[4] 11-20-0560-00-00be-multi-ap-configuration-and-resource-allocation
[5] 11-19-1931-02-00be-multi-ap-group-formation-follow-up
[6] 11-19-1582-02-00be-coordinated-ap-time-and-frequency-sharing-in-a-transmit-opportunity-in-11be
[7] 11-19-1919-03-00be-coordinated-ofdma
[8] 11-20-0548-02-00be-discussion-on-coordinated-ul-mu-mimo
[9] 11-20-0033-01-00be-coordinated-spatial-reuse-operation
[10] 11-20-0071-01-00be-joint-transmission-for-11be
[11] 11-20-0099-01-00be-coordinated-beamforming-for-802-11be