## Slide 1: 802.15 Liaison Report – Nov. 2022
Date: 2022-11-15
Authors:

## Slide 2: 802.15.16t Narrow Band Licensed Operation (NB-Lic)
What is it:
  Licensed Narrow Band (NB) Operation in channels bandwidth between 5 – 100KHz in the VHF/UHF bands such as 160MHz, 450MHz, 700MHz and 900MHz, taking advantage of the superior channel propagation properties. Targeted usages mission critical operation.
Status and main discussion topics:
  During the Sep. meeting: completed the Use case, System Requirements and System Description docs.
  Now in draft text development phase with target to generate D1.0 out of Nov. meeting.

## Slide 3: 802.15.4ab Next Generation UWB
What is it:
  Builds on 802.15.4z increasing footprint usefulness of the technology to additional usages beyond range measurement. Area of enhancements relates to ranging resiliency, sensing, data rates, support for additional spectrum, improved detection and many more.
Status:
  In Technical Specification Document (TSD) development phase.

## Slide 4: 802.15.4ab Next Generation UWB
Main discussion topics:
  Narrow Band Assisted UWB - transmission of 2MHz signal in the UNII3/5 bands to improve channel budget of the main UWB signal by providing synchronization base. Discussed channel hopping mechanism, message formats in the NB channel,
  Additional modulation and coding schemes - addition of LDPC to improve the PHR link budget and higher bit rate.
  UWB Sensing – freq. stitching; increasing the affective channel BW by using partially overlapping channels.
  “How do we go about” discussion on 802.15.4ab co-existence with 802.11: preparation for the Co-Ex SC.

## Slide 5: 802.15.13 Multi-Gbit/s Optical Wireless Communication
What is it:
  MAC and PHY project for the 10,000nm – 190nm wavelength for multi gigabit communication, with up to 10Gbps to distance of up to 200m, in LoS conditions.
Status:
  4th SA Recirculation Ballot results: 78T, 1G, 74E, 97% approval rate.
  5th recirculation initiated and completed (Nov. 14): 98% approval / 2% disapprove, 17 comment received.
  Targeting completion of ballot series and move to REVcom past the Nov. meeting (early Dec.) – on track.

## Slide 6: 802.15.6ma - Enhanced Dependability Body Area Network (ED-BAN)
What is it:
  Enhancements to the BAN (Body Area NW) Ultra Wideband (UWB) physical layer (PHY) and media access control (MAC) to support enhanced dependability to a human BAN (HBAN) and support for vehicle body area networks (VBAN).
  This revision focuses on international operation.
Status:
  Complete the Channel Model Document (CMD)
  Complete technical Document on MAC for enhanced dependability
  Complete Technical Requirement Document(TRD)

## Slide 7: 802.15.7a Optical Camera Communication
What is it:
  Amendment to provide higher rate, longer range optical camera communication.
Status:
  Recirculated out of the Sep. meeting D2.0 and the CA document.
  Letter Ballot LB192 results:
    Total voters responding: 88
    68 Approve (93%)
    5 disapprove (7%)
    15 abstain (17%)
    Total comments received: 400

## Slide 8: Other recent developments
TG3mb High Data Rate maintenance project completed LB191
  Maintenance project for 802.15.3-2016 (high data rates multimedia applications in WPAN).
  Completed LB191, results:
    Total voters responding: 88
    71 Approve (96%)
    3 disapprove (4%)
    12 abstain (13%)
    Comments received: 351 total (340 E / 11 T)

## Slide 9
TG4me
Cor1 15.4 2020 Revision 1
TG4ab
Next Generation UWB
TG6ma
Body Area Networks
Revision
TG7a
Optical Camera Communications
TG13
Multi Gigabit/sec
Optical Wireless Communication
TG15
Ultra Wide-Band Ad-Hoc Networks
TG16t
Ultra Wide-Band Ad-Hoc Networks
TG3mb
TG HDR
High Data Rate
Revision
SCTHz
Standing Committee THz
SCmaint
Maintenance Group
SCWNG
Wireless Next Generation
SCIETF
IETF liaison