## Slide 1: Enhanced Security Discussion
Date: 2023-02-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Yan Zhang Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Security in 802.11
The unicast Data/Management frames can be protected through PTK.
The broadcast Data frames can be protected by GTK.
The broadcast Management frames can be protected by IGTK.
The Beacon frames can be protected by BIGTK.
The BA’s operation may introduce some security attack
  frames discarding because of wrong updating of the scoreboard context, reorder buffer
    BAR is not protected
    The replay checking is after the reorder buffer
  PBA is proposed to further give protection to BA agreement
    Action frame is used to update the reorder buffer.
      The processing time of Action frame is not predictable.
      The replay checking is done after the reorder buffering.

## Slide 3: Control Frame Protection
Same as Data/Management frame, there are unicast Control frames, broadcast Control frames.
If the protection is applied to Control frames, both unicast and broadcast frames should be protected.
  The unicast Control frames and broadcast Control frames should use the different keys, CPTK, CGTK.
Under MLO, the CGTK should be per link key.
Under MLO, the CPTK should be per link key.
Integrity protection should be used.

## Slide 4: Protected Control Frame
The different methods can be considered for protected Control frames
  Option 1: Reuse the current control subtype
    The carrying of PN, Key ID, MIC should be designed carefully so that the non-UHR devices are not be confused.
      For Control frame with per STA field, the PN, Key ID, MIC can be carried in the Per STA fields with specific AID value, (User Info field in Trigger frame, Per STA field in NDPA, Per AID TID Info field in Mul-STA BA)
      The optimization could be no explicit transmission of MIC, e.g. by using the similar method of 11ba.
      The method is difficult for unicast frame.
  Option 2: define the new control subtype for protected control frame
  Prefer option 1

## Slide 5: PBA Enhancement
Once the MU BAR, BAR is protected, the PBA can use the protected MU BAR, BAR to adjust the scoreboard context and reorder buffer.
  The protected ADDBA Request is not needed.
  Another method is that the initiator notifies its MSDU lifetime to the recipient.
However a 3rd-party device can still use the Data frame to let the BA agreement recipient to adjust its scoreboard context and reorder buffer, the reason is that the replay check is done after the reorder buffer.
  The solution could be to allow the replay check no later than the reorder buffering.

## Slide 6: Additional Processing Time Before the Responding
The SIFS may not be enough for some device to provide the protected response with SIFS inter-frame space.
In order to address this, the transmitter of the protected responder can announce the padding requirement.
  The transmitter of the soliciting frame needs to add the padding, e.g. MPDU delimiters, padding fields, to guarantee the padding requirement of the transmitter of the responder.

## Slide 7: Summary
The methods to further improve the security of 802.11 are discussed.
  Unicast Control frame protection,
  Broadcast Control frame protection,
  BA agreement protection.
The security enhancement should be optional