## Slide 1: DPWiFi: A Proposed IEEE802.11bn PHY
Date: 2024-01-26
Authors:

## Slide 2: Abstract
Breakthrough Dynamic Polarization Multiplexing and Beamforming (“DPWiFi”) multi-signal processing combines unrestricted order RF stream MIMO Multiplexing with steerable high directivity Tx/Rx Beamforming to yield EHT-based P2P radios transporting 92 Gbps beyond 28 km and PMP radios distributing 27 GbE across 79 km2

## Slide 3: What’s new this time around
At the September 802.11WNG session TWI unveiled DPWiFi, a proposed PHY for the nascent TGbn, that employs patented digital polarization modulation to MIMO-multiplex up to 32 EHT streams within a single 320 MHz channel
The DPWiFi tutorial presented in September has been affixed hereto as Appendix A
A manual closed form analysis of a 4-stream DPWiFi Tx-Rx has been added as Appendix B
Also, at that last session’s end an esteemed colleague raised a truly existential question: “Wouldn’t the so-claimed 92 Gbps information transport within only 320 MHz completely violate Shannon’s Theorem?” Appendix C, also attached hereto, explains why not
The following slides expand/refine upon two previously identified key DPWiFi Use Cases, and incorporate a call for TGbn to also develop certain DP-complementary PHY/ MAC extensions arguably essential to ultimately successful IEEE802.11bn products and services

## Slide 4: Proposed IEEE802.11bn PHY
32 IEEE802.11be concurrent, cochannel RF streams
  32x32 MIMO Dynamic Polarization Multiplexing (“DP-32”)
  32x32 MIMO Tx/Rx DLOS/ nLOS/ NLOS Beamforming/Beamsteering
  AP MU-MIMO Tx Multi-beaming
  Client MU-MIMO Rx Interference Cancellation
  Client MU-MIMO Rx NLOS Multipath Recombination
  5-7 GHz UNII Operation
  4096 QAM 5/6
  320 MHz BW
  92.2 Gbps Peak Data Rate
  80 GbE P2P Throughput over 28 km Free-Space Range
  27 GbE PMP Throughput across 79 km2 Foliage-obstructed Region

## Slide 5
Contemplated 92.2 Gbps DPWiFi Access Point (32 Polarization-Multiplexed and Transceived EHT RF Streams)
DP-32 PDMux
TTD xBF
92/46 Gbps 320/160 MHz 6/5 GHz DP-32 AP/MeshNode

## Slide 6: Contemplated 5.8 Gbps DPWiFi Client (32 Polarization Multiplexed/ 2 Transceived EHT RF Streams )
5.8/2.9 Gbps 320/160 MHz 6/5 GHz DP-32 Client
DP-32 PDMux
TTD xBF

## Slide 7: Point to Point DPWiFi Terrestrial Internet Backhaul Application
    By Regulatory Fiat, the above P2P DPWiFi link’s Free Space Path Loss works out to
    DPWiFi FSPL|MCS13 = PTx + GTx + GRx – kTBF - SNR = 138 dB
    And the corresponding P2P DPWiFi 92 Gbps Free-Space Range to
    R = SQRT(FSPL)c/4πfc = 28.2 km
P2P DPWiFi AP Configuration | 
Modulation/Coding | MCS13 (4096Q5/6)
Bandwidth (B) | 320 MHz
TRX Frequency (fc) | 6705 MHz (6 GHz Ch 151)
Tx Power (PTx) | +36 dBm (Regulatory Maximum)
SDPA Element Gain (GElement) | 19 dBi (30o Beamwidth)
SDPA Array Gain (GArray) | 16 dBi (6Hx6W-2Hx2W Boresight)
Ambient Temperature T | 25o C
Noise Figure (F) | 2.2 dB
P2P DPWiFi AP-AP Link Configuration | 
Signal/Noise Ratio (SNR) | 55 dB (1e-6 PER)
SDPA Gain (GTx = GRx) | 35 dBi (GElement + GArray)
Noise Power (kTBF) | -87 dBm

## Slide 8: Point to Multipoint DPWiFi Terrestrial Internet Distribution Application
    PMP DPWiFi Data Rate vs Range: FSPL = EIRPTx + GRx – kTBF – SNR FSPL = 155 - SNR
PMP DPWiFi Link Configuration | 
GRx | 32 dBi (GRxElement + GRxArray)
kTBF | -87 dBm
ObsR* (km) | Eq FSR (km) | FSPL (dB) | SNR (dB) | MCS Range | Tpt (Gbps)
1.0 | 2.0 | 115 | 40 | MCS13-MCS7 | 59.7
2.5 | 5.0 | 123 | 32 | MCS13-MCS5 | 43.8
5.0 | 10.0 | 129 | 26 | MCS13-MCS3 | 31.3
10.0 | 20.0 | 135 | 20 | MCS13-MCS1 | 18.4
PMP DPWiFi AP/ Client Configuration | 
Modulation/Coding | MCS13 (4096Q5/6) to MCS0 (B1/2)
Bandwidth (B) | 320 MHz
TRX Frequency (fc) | 6705 MHz (6 GHz Ch 151)
AP EIRP (EIRPTx) | +36 dBm (Regulatory Maximum)
Client SDPA Element Gain (GRxElement) | 16 dBi (45o Beamwidth)
Client SDPA Array Gain (GRxArray) | 16 dBi (6Hx6W-2Hx2W Boresight)
Ambient Temperature T | 25o C
Noise Figure (F) | 2.2 dB
PMP DPWiFi Link Obstruction RF Attenuation | 
Outdoor Foliage | 1 dB/ meter
Indoor Drywall | 2 dB/ Wall
Exterior Stucco | 6 dB/ Wall
Exterior Masonry | 15 dB/ Wall
Mod/Cod | BDR (Mbps) | XDR (Gbps) | SNR (dB) | FSPL (dB) | FSR (km)
MCS13 4096Q5/6 | 2882 | 92.2 | 55 | 100 | 0.36
MCS12 4096Q3/4 | 2594 | 83.0 | 53 | 102 | 0.45
MCS11 1024Q5/6 | 2402 | 76.9 | 49 | 106 | 0.71
MCS10 1024Q3/4 | 2162 | 69.2 | 47 | 108 | 0.90
MCS9 256Q5/6 | 1922 | 61.5 | 43 | 112 | 1.4
MCS8 256Q3/4 | 1799 | 55.3 | 41 | 114 | 1.8
MCS7 64Q5/6 | 1441 | 46.1 | 36 | 119 | 3.1
MCS6 64Q3/4 | 1297 | 41.5 | 34 | 121 | 4.0
MCS5 64Q2/3 | 1153 | 36.9 | 30 | 125 | 6.3
MCS4 16Q3/4 | 865 | 27.7 | 27 | 128 | 9.0
MCS3 16Q1/2 | 577 | 18.5 | 23 | 132 | 14.1
MCS2 4Q3/4 | 432 | 13.8 | 21 | 134 | 17.9
MCS1 4Q1/2 | 288 | 9.2 | 17 | 138 | 28.2
MCS0 B1/2 | 144 | 4.6 | 14 | 141 | 38.2
    *- 6m Outdoor Foliage
    PMP DPWiFi Peak Data Rate at Free Space Range:
    PMP DPWiFi Average Data Rate across Obstructed Range:

## Slide 9: Key DPWiFi Use Cases
    Point to Multipoint Ultra-High-Capacity Fixed WiFi Access (“FWiFiA”) Last Mile Broadband BBDP (i.e., a “Dynamic Polarization Trunk-Drop”) to Broadband CPE connectivity
    Point to Point Ultra-High-Capacity FWiFiA Backhaul (“WiFiBH”) Middle Mile Broadband Internet Exchange Point (Broadband Source) to Broadband Distribution Point connectivity

## Slide 10: Dynamic Polarization Trunk-Drop Architecture

## Slide 11
    Although possessed of the world’s fastest Physical Layer, the proposed DPWiFi constructs need further associated PHY/MAC extensions to yield truly compelling products and services:
    Link Throughput Maximization TDMA MAC (Let’s max out the already massive pipe)
      AP up to 90%/ 10% Downstream/ Upstream traffic split
      AP up to 32k Client Access List
    Direct-/ near-/ Non-Line-of-Sight Link Optimization PHY (Gotta deal with those pesky almost universally obstructed Base Station-Subscriber links)
    MIMO AP Tx DLOS Beamforming/ Beamsteering
    MU-MIMO AP Tx Adaptive Sectorization
    MIMO Client Rx DLOS/ nLOS/ NLOS Beamforming/ Beamsteering
    MU-MIMO Client Rx AP Beamsplit Multipath Aggregation/ Diversity Combining
    Resilient Unlicensed Band Operations PHY (Just like at 2.4 and 5, it’s ultimately gonna be a jungle at 6 GHz)
    MU-MIMO Client Rx Interference Cancellation
  This is a call for any and all interested doteleveners to collaborate with TWI in developing these mission-critical DPWiFi capabilities
Proposed Dynamic Polarization-complementary TGbn Tasks

## Slide 12: Representative “Municipal Fixed WiFi Access” Network
Link Type | Data Rate | Range | Network Capacity
WiFiBH AP-AP | 92.2 Gbps | 28.0 km/ Free Space | 80 GbE @ 87/13 TS
FWiFiA AP - Client | 92.2 Gbps 46.1 Gbps 36.9 Gbps 18.5 Gbps 13.8 Gbps | 300 m/ Free Space 1 km/ 6m Foliage 2.5 km/ 6m Foliage 5km/ 6m Foliage 10 km/ 6m Foliage | 80 GbE/ 32.0k Subs 52 GbE/ 20.8k Subs 38 GbE/ 15.2k Subs 27 GbE/ 10.8k Subs 16 GbE/ 6.4k Subs
Subscriber-Allocated Muni FWiFiA Costs | 6 GHz RF Attn
DPWiFi Infrastructure | <$10
DPWiFi CPE | $99
60/60/24/7 10Mbps BB | <$1/ mo
A single “Muni FWiFiA” DPWiFi AP distributes <$20/mo 60/60/24/7 10 Mbps to over 10k Subscribers

## Slide 13: Representative “Metropolitan Fixed WiFi Access” Network
Link Type | Data Rate | Range | Network Capacity
12x FWiFiA AP - Client | 1.11 Tbps 553 Gbps 443 Gbps 222 Gbps 166 Gbps | 300 m/ Free Space 1 km/ 6m Foliage 2.5 km/ 6m Foliage 5km/ 6m Foliage 10 km/ 6m Foliage | 960 GbE/ 384k Subs 624 GbE/ 250k Subs 456 GbE/ 182k Subs 324 GbE/ 130k Subs 192 GbE/ 77k Subs
User-Allocated Metro FWiFiA Costs | 6 GHz RF Attn
DPWiFi Infrastructure | <$2
DPWiFi CPE | $99
60/60/24/7 10Mbps BB | <$1/ mo
~$60k/mo
~$250k
A dozen “Metro FWiFiA” DPWiFi APs distribute <$20/mo 60/60/24/7 10 Mbps to over 125k Subscribers

## Slide 14
What Does All This Mean to Us 802.11 folk? (One Guy’s Idle Musings, Analyses and Conclusions )
Musing 1: DPWiFi FWiFiA will promptly obsolete all other WAN Broadband connectivity technologies Analysis 1: DPWiFi can deliver Any Time, All the Time 4kHD Home BB for, what, ~$15/mo? $10? $5? Cable delivers Sometimes 4kHD Home BB for ~$60/mo 5G does NOT deliver Any 4kHD Home BB, at any price FTTP and LEOSat BB aren’t even in the conversation Conclusion 1: Most of the world’s 1.4B fixed Broadband connections will rapidly migrate to DPWiFi once WiFiBH and FWiFiA equipment become widely available
Musing 2: There will be enormous, immediate and lasting demand for DPWiFi Analysis 2: Assuming just 1.2B DPWiFi BB migrations means ~400M new DPWiFi subs/yr for 3 years, or 400M (3-yr life) DPWiFi Clients sell annually for the foreseeable future Given 1 FWiFiA AP per 2000 Clients, 2 WiFiBH APs per FWiFiA AP and a systemic 3x network overbuild means (4e8/2e3 x 3 x 3 =) 1.8M DPWiFi APs sell yearly, also ftff Conclusion 2: WiFi chip/radiomakers will sell as much DPWiFi as they can build, as fast as they can build it
Musing 3: DPWiFi equipment could come available much faster than many would expect Analysis 3: As the DPWiFi PHY comprises a trivial WiFi-7 spin, DP-32 SoC platforms could arrive by 2025 100k’s of WiFiBH/FWiFiA APs and 10M’s of FWiFiA Clients then should come available by 2026 Conclusion 3: To much popular acclaim, IEEE802.11bn-compatible APs and Clients, as well as thereby-enabled breakthrough Internet services, could long precede formal TGbn standardization

## Slide 15
A Substantiating Concrete, Imminent Example (One Guy’s Not so Idle MA&C)
      NsI Musing 1: Per the graph, ~12.5k towns in the USA boast between 500 and 50k residents NsI Analysis 1: Those towns comprise ~75M (generally Broadband-underserved) households
      Represent the entire (overwhelmingly untapped) market for ~1k US WISPs
      Just 1-2 TownWiFi buildouts each would well-BB-serve ALL those towns Those 1k WISPs are ready, willing and able to build out the instant DPWiFi arrives!
      NsI Conclusion 1: The USA market demand for DPWiFi APs and Clients on Day 1 of availability:
      70M FWiFiA Clients + 70k WiFiBH/ FWiFiA APs

## Slide 16
    The novel DPWiFi PHY presented here, a way-out-of-left-field MIMO Multiplexing re-think, would launch 802.11 into the rarefied 100GbE-over-kilometers realm long dominated exclusively by fiber
    Further PHY and MAC extensions deliver the ultra-high reliability performance required by carrier class PMP and P2P DPWiFi
    Dynamic Polarization and recommended extensions deserve serious consideration for adoption by the new IEEE802.11bn standard
Proposed Dynamic Polarization PHY Summary

## Slide 17: One Final Thought
Having studiously avoided those trite 4 little words until now:
IEEE802.11bn Dynamic Polarization WILL finally, uniquely, definitively and irreversibly BtDD for anyone and everyone, anytime and all the time, anywhere and everywhere on the planet

## Slide 18
DPWiFi Analysis
Appendix A

## Slide 19: Reciprocally Interference-Free Cochannel Propagation of Unrestricted Count RF Spatial Streams in DLOS Channels
DPWiFi Propagation Channel Model
[HDP] represents the DPWiFi medium transfer function as well as the TRX Polarization Multiplexer
If [HDP] is non-singular, it has an inverse [HDP]-1 representing the TRX Polarization Demultiplexer
The analysis following will verify [HDP] non-singularity and gauge its computational tractability
MIMO Dynamic Polarization Multiplexing and Beamforming

## Slide 20
  “n” selectable Dual-Pol Tx Antennas (“DPAs”) distinctly Polarize n RF Spatial Streams [S] (Si, i = 1, 2 … n) with n respective Walsh-m (m>n) binary orthogonal codes [DPC] to yield the polarization-decorrelated [DPS]
  Transmit Beamforming (TxBF) aggregates all the DPSi for high directivity transmission toward n Rx DPAs
  n Rx DPA “matched polarization filters” De-polarize [DPS] using the same Tx Walsh sequences prior to high directivity RxBF detection, thereby yielding the (DPWiFi) polarization-multiplexed [S*] (S*ij, i, j = 1, 2 … n)
[HDP] Characterization

## Slide 21
As the DPCi all comprise Walsh binary orthogonal sequences,
ALL S*i=j = 1 and ALL S*i≠j = r, where r (in theory) equals 0.5
[HDP] Operation

## Slide 22
  In practice, however, the [HDP] DPWiFi Propagation Channel correlation index r corresponds to the cross-pol isolation measured between a realizable Rx DPA’s selectable orthogonally polarized elements
    For example, commercially available X-band Dual-Pol antennas spec xpol iso at -25dBc typical
    Therefore, [HDP] can be expressed as
    [HDP] is non-singular (as well as deterministic, time-invariant and uniform), meaning there exists an [HDP]-1 DPWiFi Polarization Demultiplexer that is also deterministic, time-invariant and uniform (!)
[HDP] Dynamic Polarization Multiplexer Representation

## Slide 23
    So, given the DP Propagation Channel/Polarization Multiplexer represented by
    There exists a DPWiFi Polarization Demultiplexer (“PDMX”)represented by
[HDP]-1 Dynamic Polarization Demultiplexer Representation

## Slide 24
    The DPWiFi Polarization Demultiplexer operation [S’] = [S*] x [HDP]-1 (= [S]) may be equivalently expressed computationally and by hardware (i.e., the physical TRX PDMX) by:
    and
    The Dynamic Polarization Demultiplexer comprises trivial hardware
Dynamic Polarization Demultiplexer Implementation

## Slide 25
DPWiFi TRX Model
[HDP] DPWiFi Propagation Channel
[HDP-1] DPWiFi PDMX

## Slide 26
Illustrative Dynamic Polarization Example:
Closed Form Analysis of a DPWiFi Tx-Rx Link featuring n = 4, r = 0.505
Appendix B

## Slide 27
DPWiFi TRX Analysis Part 1

## Slide 28
DPWiFi TRX Analysis Part 2

## Slide 29
DPWiFi and the Shannon Limit
Appendix C

## Slide 30: Dynamic Polarization and the Shannon Limit, Part 1 How does DP-n NOT exceed Shannon’s maximum channel capacity law?
    Consider the canonical Shannon Tx-Rx Channel of Figure A, below A signal S0 of bandwidth BW transmitted through a directional antenna of gain GTX at power level EIRP0 , detected through another antenna of gain GRX and ultimately received as S’0 with a S/N ratio SNR0 propagates across the transmission channel of Shannon capacity C0 = BW log2 (1 + SNR0) shown
    Consider now a perfectly equivalent Tx-Rx channel in Figure B Directional antennas GRX and GTX replaced by perfectly equivalent phased arrays GRX and GTX

## Slide 31: Dynamic Polarization and the Shannon Limit Part 2
And yet another perfect equivalent Tx-Rx in Figure C:
S0 and S’0 1:n splits replaced by equivalent n x S0 and S’0 replicas, all traversing distinct C0 capacity channels
And finally, consider the not-really-sleight-of-hand of Figure D:
n S0 and S’0 replaced by perfectly equivalent distinct Si, i = 1, 2 … n, the phased array antennas by SDPAs and the Rx n:1-1:n splitter combiner by a Pol- Demux, all traversing distinct C0 capacity channels
An nth order DPWiFi link comprises n Shannon channels, not just one
PDMX