## Slide 1: High Criticality Use Cases and Requirements
Date: 11-9-2023

## Slide 2: Goals
Discuss the classification and requirements of the traffic found in an 802.11 network
Identify the 802.11 features needed depending on traffic requirements and characteristics

## Slide 3: Introduction
UHR targets the improvement of packet delivery by reducing the transmission latency and enhancing network reliability [1]
Previous contributions have presented different UHR features depending on the nature of the traffic in the application layer [2]
Other contributions have focused on the low latency features for fast delivery of the data frames (i.e., preemption) [3]
Low latency applications have also been linked to Real-Time Applications (RTA) [4]

## Slide 4: Problem Statement
Many new features are being proposed in the context of UHR
  These features need to be evaluated and understood in the context of the final application
In this contribution we classify different network applications and identify their needs, to select the features that may apply

## Slide 5: Network Traffic Pattern
One way to classify Network traffic patterns is according to inter-arrival time between burst packets
  Periodic pattern, having a nearly predictable behavior
  Non-periodic (or aperiodic) pattern, based on random external events
    Exact frame transmission impossible to predict

## Slide 6: Network Traffic Criticality
Network Traffic can also be classified as low or high criticality (a measure of reliability and latency)
High critical data must be reliably delivered to the destination within a known time window (time latency)
  Latency value depends on the application, therefore we should talk about bounded latency requirement
Low critical data has more relaxed requirements
  Sporadic communication errors do not imply an application malfunction

## Slide 7: Application Matrix
Based on the previous criteria, we build the following matrix
 | Periodicity | 
Criticality | Periodic / Low Critical Applications: video streaming, IoT devices (home appliances) | Aperiodic / Low Critical Applications: web browsing, chat, mobile applications, IoT devices (home appliances)
 | Periodic / High Critical Bounded latency applications: VR/AR, real-time video, gaming, video streaming over TCP/IP, industrial IoT (Factory Automation), home surveillance, cloud-based applications, medical equipment | Aperiodic / High Critical Critical events applications: safety alarms, industrial IoT (Process Automation), medical equipment
Already covered by 802.11
Objective of the PAR
Notes: https://www.sidnlabs.nl/en/news-and-blogs/visualisations-of-periodic-iot-traffic
https://nvlpubs.nist.gov/nistpubs/ams/NIST.AMS.300-8r1-upd.pdf
https://mentor.ieee.org/802.24/dcn/23/24-23-0011-02-0000-low-latency-communications-white-paper-pdf-for-comment.pdf
https://www.mdpi.com/2624-831X/2/1/8#:~:text=IoT%20traffic%20is%20the%20aggregation,e.g.%2C%20temperature%20and%20humidity).

## Slide 8: Low Criticality Applications
Current 802.11 features usually provide enough performance (throughput, reliability, latency) for good functionality of the network services
Improvements in OBSS interference mitigation will help increase the availability of the communication link
Periodic traffic applications: Video streaming, Smart Home IoT devices (several seconds of periodicity) [5]
Event-driven (aperiodic) applications: web browsing, chat, mobile applications, Smart Home IoT devices
Limited effort needed in UHR, focused on improvement in OBSS interference scenarios
Notes: Paper 1: IoT Traffic: Modeling and Measurement Experiments

## Slide 9: Periodic and High Critical
Applications with real-time (RTA) traffic requirements [6,7,8]
  Closed-loop communication (downlink and uplink sequence)
  Constant update rate (periodic communication)
  High reliability and Bounded latency (value depends on the application)
Applications: VR/AR, real-time video, gaming, industrial IoT, home security, Smart Home IoT, cloud-based applications
  Applications covered in the 802.24 whitepaper about low latency [7]
  Bounded latency in the range of 1 to 20 milliseconds [6,7,9]
  Throughput in the range of 1 to 400 Mbps [6,7,9]
Deterministic scheduling features are needed for the strict control of the QoS for the traffic streams in DL and UL communication
In summary, this is the case where UHR needs to focus
Notes: * Paper: Network Traffic Characteristics of IoT Devices in Smart Homes

## Slide 10: Aperiodic and High Critical
Applications that generate random events, where the data must arrive at the destination reliably due to its critical data
Applications: safety alarms, critical monitoring sensors, safety systems, etc. (e.g., home security system events have a response time under 15 seconds)
For industrial applications, data needs to be delivered within a bounded latency, in the range of 50 to 100 milliseconds, depending on the application [7, 10]
Reliability is a key requirement, being more critical than meeting the latency, which could not be that challenging to accomplish with the current 802.11 technology
These cases require features that focus on reliability rather than low latency

## Slide 11: Reliability vs. Low Latency
Aperiodic and High Critical data delivery appears to require reliability more than it requires very low latency
Within the categorization presented earlier, we see no applications that are both non-periodic and very low–latency (< 5 msec)
The various forms of preemption [3,13-16] appear to be tailored towards non-periodic and very low–latency applications
  Does this solve real-world problem?
  Should solution focus on periodic traffic instead?

## Slide 12: Summary
Low Criticality | Limited effort needed, focused on improvement in OBSS interference scenarios
High Critical and Periodic | Many contributions have proposed features for improving these use cases [8,12,13], mainly for optimizing the transaction scheduling to lower the latency within the bound limits Scheduling for RTA Multi-AP (repeater/mesh) topologies scheduling OBSS interference mitigation
High Critical and Aperiodic | Attending to the previous requisites, this use case is not necessarily about low latency, but reliability is mandatory Bounded latency (50 – 100ms) Application frame tagging Specific modulation/coding for increased reliability

## Slide 13: Conclusion
We have identified the high criticality (reliability and bounded latency) use cases as one of the main focus of UHR, attending to the PAR
We question whether any non-periodic traffic requires very low latency (< 5 msec)
  Note that reliability remains a key requirement
High criticality applications that follow periodic traffic patterns need special attention to provide them with adequate features

## Slide 14: References
[1] IEEE 802.11-23/0028r6， UHR PAR discussion
[2] Serhat Erkucuk and et al. (Offino), “Enhanced Scheduling Method for Low Latency Traffic”, 23/0378r0, May 2023.
[3] Juan Fang and et al. (Intel), “Preemption for Low Latency Application”, 23/0092r0, March 2023.
[4] Peshal Nayak and et al. (Samsung), “QoS Enhancements for Next Generation Wi-Fi Networks” 23/1207r0, July 2023.
[5] Nguyen-An H, Silverston T, Yamazaki T, Miyoshi T. IoT Traffic: Modeling and Measurement Experiments. IoT. 2021; 2(1):140-162. https://doi.org/10.3390/iot2010008
[6] Kate Meng and et al. (Tencent Technology), “RTA report summary”, 19/0065r6, March 2019.
[7] Oliver Holland and et al. “Low Latency Communication White Paper”, P802.24-23-0010r4, July 2023.
[8] Dmitry Akhmetov and et al. (Intel), “Medium efficient scheduled channel access in next generation 802.11”, 23/0936r0, July 2023.
[9] M. Mainuddin and et al., "IoT Device Identification Based on Network Traffic Characteristics," IEEE GLOBECOM 2022, Rio de Janeiro, Brazil, 2022, pp. 6067-6072, doi: 10.1109/GLOBECOM48099.2022.10001639

## Slide 15: References
[10] Karl Montgomery et al., “Wireless User Requirements for the Factory Workcell”, NIST Advanced Manufacturing Series 300-8 (Rev. 1), doi: https://doi.org/10.6028/NIST.AMS.300-8r1/upd
[11] Kazi Huq and et al. (Ofinno), “Enhanced Trigger-Based Uplink Transmission”, 22/1923r1, November 2022.
[12] Dmitry Akhmetov and et al. (Intel), “Challenges to achieve deterministic low latency in next generation 802.11”, 22/1926r0, November 2022.
[13] Kiseon Ryu and et al. (NXP), “TXOP preemption follow up”, 23/1174r0, July 2023.
[14] Daniel Verenzuela and et al. (Sony), “Overlapped indication to support preemption”, 23/1194r0, July 2023.
[15] Juan Fang and et al. (Intel), “Preemption for low latency application (Follow up)”, 23/1229r1, August 2023.
[16] Juseong Moon and et al. (KNUT), “Considerations on Inter-PPDU based Preemption Scheme”, 23/1242r1, August 2023.