## Slide 1: Coordinated Medium Access for Multi-AP Deployments
Date: 2024-01-15
Authors:

## Slide 2: Problem Statement
Objective: reduce the latency, increase the throughput, and improve the reliability in networks with latency-sensitive traffic with some degree of predictability
Problem: today, in most deployments, APs don’t coordinate which leads to the inability of effectively serving latency-sensitive traffic, this is due to
  Delayed access due to ongoing OBSS TXOP(s)
  Overlapping transmissions between different BSSs resulting in high PER and increased latency due to collisions, retransmissions, hidden nodes, etc.
Solution: introduce coordination between APs

## Slide 3: Design Principles
Coordinated Medium Access for APs in UHR can leverage hooks introduced in EHT as Restricted TWT (rTWT)
  In rTWT, STAs terminate their TXOP before the start time of an rTWT service period (SP) so that the AP can access the medium to serve latency-sensitive traffic
  rTWT is an intra-BSS mechanism
For UHR, a set of APs could coordinate to respect each others rTWT
  Consider a Coordinated rTWT (C-rTWT) between APs
  Consider Coordinated APs (C’ed APs) to behave similarly to STAs in EHT rTWT
  Consider Coordinating AP (C’ing AP) to behave similarly to AP in EHT rTWT
  Coordinated APs terminate their TXOP before the start time of the C-rTWT SP
  An AP can be a C’ed AP in a given C-rTWT and a C’ing AP in another C-rTWT
The coordination scheme between APs will facilitate the transmissions of participating APs at the start of the respective SPs to reliably serve latency-sensitive traffic

## Slide 4: TXOP rules visualization
BSS1
BSS2
t
t
TXOP AP2
rTWT SP
Issue1: TXOP of AP2 is ongoing and AP1 cannot access to serve latency-sensitive traffic during its rTWT SP
BSS1
BSS2
t
t
Issue2: clients of AP1 (e.g., STA1 hidden from AP2) will unnecessarily terminate their TXOP before AP1’s rTWT SP
TXOP STA1
BSS1
BSS2
t
t
TXOP AP2
C-rTWT SP
TXOP STA1
APs end their BSS transmissions before the C-rTWT SPs
Avoid delayed access at the start of the coordinated SP
Reduces overlapped transmissions between APs
STA1 and AP2 will terminate their TXOP and facilitate AP1’s medium access at the start of the C-rTWT
11be rTWT
11bn C-rTWT
R-TWT SP
R-TWT SP
TXOP
TXOP
Issue3: If both APs manage to access the medium (e.g., beyond ED range) overlapping transmissions may degrade PER

## Slide 5: Levels of coordination
Two options for the levels of coordination:
  Level 1: Only C’ed APs terminate their TXOP before the C’ing AP’s SP
    C’ing AP can setup rTWT SPs for its STAs and use MU EDCA to reduce contention
  Level 2: C’ed APs and their associated STAs terminate their TXOP before the C’ing AP’s SP
    C’ed APs announce the SP of the C’ing AP to their associated STAs (e.g., as an EHT rTWT SP)
    EHT rTWT supporting STAs will also end the TXOP before the C’ing AP’s SP

## Slide 6: TSF adjustment for LV2 coordination
  For LV2 the TSFs may be different at different Aps, two solutions:
    Option 1: APs synchronize their TSF
    Option 2: each AP corrects the start time of SPs announced by other APs before announcing other APs Coordinated SP information to its associated STAs (e.g., in its transmitted Beacon frames)
      requires extensions for TWT field to support different offsets between APs when Coordinated SP is communicated through R-TWT
AP1
AP2
Beacon of AP1
t
SP 1
t1 (w.r.t AP1)
t1 (w.r.t AP2)
SP 1
Correct start time
SP 1
t
If AP2 announces Coordinated SP1 without correcting the Target Wake Time, then AP2 will announce a start time that is different from the correct start time of SP1
Coordinated SP information

## Slide 7: Gain Analysis: Single Family Home
Two floors with 3 APs
  13 dB floor loss and 10 dB wall loss
Each AP having 2 clients
  2 AP are in Floor 1, 1 AP is on Floor 2
  AP and STA location are random
Traffic:
  STA1 – DL low latency traffic (served on AC_VO)
    VR with 60 Kbytes at 60 fps
    CBR with 1500 Bytes at 60 fps
  STA2 – DL full buffer traffic served on AC_BE

## Slide 8: Gain Analysis: Single Family Home (Cont’d)
Chart: 99 Percentile Latency (msecs)
Baseline | 509.07
11be R-TWT | 307.16
UHR C-R-TWT | 2.057
Latency Statistics for VR traffic scenario at STA1 (low latency traffic)
Chart: 99 Percentile Latency (msecs)
Baseline | 20.947
11be R-TWT | 20.936
UHR C-R-TWT | 0.202
Latency Statistics for CBR traffic (1500 Bytes) scenario at STA1 (low latency traffic)

## Slide 9: Next steps
APs coordination will require investigating and developing additional aspects such as:
Coordination setup/negotiation:
  In proprietary environments (e.g., enterprise) simply a network configuration can setup AP coordination
  In non-proprietary environments negotiation between Aps might be needed
Coordinated EDCA:
  To improve prioritization of a C’ing AP at the beginning of its C-rTWT SP aspects of coordinated EDCA may need further investigation/development
Details of the above aspects will discussed in next steps.

## Slide 10: Conclusion
We introduced the APs coordination framework for UHR
The coordination framework leverages the EHT rTWT framework
Two levels of coordination have been considered (LV1: for coordinated APs only and LV2: for coordinated APs and their associated STAs)
APs coordination will facilitate the transmissions of a coordinating AP at the start of its SP to reliably serve latency-sensitive traffic
Next steps investigations will involve negotiation between APs and coordinated EDCA.

## Slide 11: SP1
Do you agree to define mechanisms that enable APs to coordinate their respective rTWT schedules and/or to ensure that one AP extends the protection of the rTWT schedule of the other AP.
  NOTE – TBD mechanisms include negotiation between 2 APs and advertisement.

## Slide 12: SP2
Do you agree that, if an AP extends the protection of the rTWT schedule of another AP, following negotiation or through other means, then:
  The AP shall ensure its TXOP ends before the start time of the corresponding OBSS rTWT SP(s)
  The AP shall advertise in the beacon frames it transmits the OBSS rTWT schedule so that its associated STAs supporting rTWT follow the baseline rTWT rules for the OBSS rTWT schedule.