## Slide 1: Smooth Roaming Follow Up: Procedure and Signalling
Date: 2023-11-10
Authors:
Name | Affiliations | Address | Phone | email
Liwen Chu Kiseon Ryu Huizhao Wang Hongyuan Zhang Rui Cao Sudhir Srinivasa Hui-Ling Lou | NXP |  |  | 

## Slide 2: Recap: Smooth Roaming[1],[2]
A roaming AP MLD includes multiple distributed AP MLDs.
  The MLD level functionalities are separated in AP MLD level and roaming AP MLD level.
  The roaming AP MLD is not visible to non-UHR non-AP MLDs.
The roaming within a roaming AP MLD from one affiliated AP MLD of the roaming AP MLD to another affiliated AP MLD of the roaming AP MLD doesn’t need the reassociation, key renegotiation.
The Link level roaming and MLD level roaming are allowed
  The multiple serving AP MLD mode through link level roaming is a transient mode and is only used during the roaming procedure for smooth roaming.
This presentation discuss the messages and procedure used for the smooth roaming within a roaming AP MLD.
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD2
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 10
MLD common MAC
5GHz
STA11
6GHz
STA12
MLD level
Roaming operation
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD2
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 10
MLD common MAC
5GHz
STA11
6GHz
STA12
Link level
Roaming operation
AP MLD21
MLD common MAC
5GHz
AP111
6GHz
AP112
AP MLD22
MLD common MAC
5GHz
AP121
6GHz
AP122
Roaming AP MLD2
Roaming AP
MLD common MAC
Non-AP MLD11
with AID 10
MLD common MAC
5GHz
STA11
6GHz
STA12

## Slide 3: Recap: 11be BTM and ML Reconfiguration for ML Setup
BTM is used for the associated AP MLD to recommend a new associated AP MLD
  BTM (BSS Transition Management) Query, BTM Request, BTM Response with the help of update Neighbor Report element.
A non-AP MLD can add or delete its setup link through ML reconfiguration
  Link Reconfiguration Request, Link Reconfiguration Response

## Slide 4: Steps for Smooth Roaming
Step 1: exchanging the information of the candidate serving AP MLD for the non-AP MLD to select the new serving AP MLD affiliated with the same roaming AP MLD as the current serving AP MLD.
  This step is optional.
Step 2: roaming from the current serving AP MLD to the new serving AP MLD.
  Through this successful step, the frame exchanges context of the non-AP MLD is established in the new serving AP MLD.

## Slide 5: Updated Basic ML Element vs New Type of ML Element
Option 1: the roaming AP MLD is announced through updating the Basic ML element.
  The Roaming AP MLD MAC Address Present subfield and AP MLD Roaming ID Present subfield are added to Presence Bitmap subfield by using any two bits of B7 to B11, e.g. B7 and B8.
    If the AP MLD MAC Address Present subfield is 1, the Roaming AP MLD MAC Address is carried in Common Info field to indicate the MAC SAP address of roaming AP MLD that the AP MLD indicated by the MLD Address of the Basic Multi-Link element is affiliated with.
    If the AP MLD Roaming ID Present subfield is 1, the AP MLD Roaming ID field indicates the AP MLD identifier of the AP MLD identified by MLD MAC Address within the Roaming AP MLD.
      Each AP MLD affiliated with a roaming AP MLD has a unique AP MLD Roaming identifier within the roaming AP MLD.
  Roam AP MLD level specific features that are not defined by its affiliated AP MLDs may also be in Common Info subfield, e.g.
    whether link level roaming is supported.
  The two new Present fields can be combined to one bit.
  The roaming AP MLD is not visible to a non-UHR non-AP MLD since the non-UHR MLD can’t decode the new added (sub)fields.

## Slide 6: Updated Basic ML Element vs New Type of ML Element
Option 2: the roaming AP MLD is announced through the new type of the ML element.
  The new type of Multi-Link element is used to announce the roaming AP MLD:
    Roaming AP MLD MAC Address,
    AP MLD Roaming ID of the Affiliated AP MLD
    Roam AP MLD level specific features that are not defined by its affiliated AP MLDs, e.g.
      whether link level roaming is supported.

## Slide 7: Updated Reconfiguration ML Element
The Roaming AP MLD MAC Address Present subfield and AP MLD Roaming ID Present subfield are added to Presence Bitmap subfield by using any two bits of B3 to B11, e.g. B3 and B4.
  If the AP MLD MAC Address Present subfield is 1, the Roaming AP MLD MAC Address is carried in Common Info field to indicate the MAC SAP address of roaming AP MLD that the AP MLD indicated by the MLD Address of the Reconfiguration Multi-Link element is affiliated with.
  If the AP MLD Roaming ID Present subfield is 1, the AP MLD Roaming ID field indicates the AP MLD identifier of the AP MLD identified by MLD MAC Address within the Roaming AP MLD.
    Each AP MLD affiliated with a roaming AP MLD has a unique AP MLD Roaming identifier within the roaming AP MLD.
The two new Present fields can be combined to one bit.

## Slide 8: Neighbor AP MLD Announcement through RNR
A new-defined TBTT Information with TBTT Information Field Type that is not 0 is used for the first AP to announce the second AP where the following are true
  the first AP and the second AP are not affiliated with the same AP MLD.
  the AP MLD with which the first AP is affiliated and the AP MLD with which the second AP MLD is affiliated are affiliated with the sane roaming AP MLD.
  The second AP MLD and the first AP MLD are one-hop neighbor (or two-hop neighbor as another example) if the two AP’s links supporting the same band work in the same channels.
    Another variant is that the first AP intends to carry the second AP’s information
The MLD Parameters field is used to carry the MLD related information of the affiliated AP MLD and affiliated roaming AP MLD.

## Slide 9: Information Exchange of Candidate Serving AP MLD
BTM Query, Request, Response are used for the information exchange of the candidate serving AP MLD affiliated with the same serving AP MLD as the current serving AP MLD.
  The Neighbor Report element can carry the Basic Multi-Link subelement for indicating a neighbor AP MLD affiliated with the roaming AP MLD.
    The Roaming AP MLD can be indicated in the Common Info field of the Basic Multi-Link element.
    Another variant is that a new type Multi-Link element is defined to indicate the affiliated roaming AP MLD.

## Slide 10: Negotiation of Roaming from One Serving AP MLD to Another Serving AP MLD
Through Link Reconfiguration Request/Response, a non-AP MLD roams from the current serving AP MLD to the new serving AP MLD, i.e. deleting the links of the current serving AP MLD and adding the links of the new serving AP MLD.
  The Reconfiguration Multi-Link element in Link Reconfiguration Request indicates the new serving AP MLD and the links being set up.
  After the reception of the Link Reconfiguration Response where the serving AP MLD switch is accepted, the future serving AP MLD’s frame exchange context with the non-AP MLD is ready. The frame exchange context in the current serving AP MLD is cancelled( not be used for frame exchanges any more) for MLD level roaming.

## Slide 11: Negotiation of Roaming from One Serving AP MLD to Another Serving AP MLD
Links for transmitting Link Reconfiguration Request/Response
  Option 1: the Link Reconfiguration Request/Response are transmitted through the current serving AP MLD to the roaming AP MLD.
  Option 2: the Link Reconfiguration Request/Response are transmitted through the future serving AP MLD to the roaming AP MLD.
  Option 3: the Link Reconfiguration Request is transmitted through the current serving AP MLD to the roaming AP MLD, and the Link Reconfiguration Response is transmitted through the current or the future serving AP MLD to the roaming AP MLD
If the AP affiliated with current serving AP MLD is used as the receiver/transmitter of the Link Reconfiguration Request/Response, all the STAs of the non-AP MLD are in power save mode with the future serving AP MLD after the serving AP MLD switch.
The Link Reconfiguration Request/Response can do the TWT negotiation, TID-to-Link mapping negotiation, BA agreement negotiation, EPCS enablement etc. with the future serving AP MLD.

## Slide 12: Summary
We propose:
  The MLD roaming includes link level roaming and MLD level roaming
    The multiple serving AP MLD mode through link level roaming is a transient mode and is only used during the roaming procedure for smooth roaming.
  A non-AP MLD has one serving AP MLD at any time when the roaming is not executed.
  The new ML element or the update Basic ML element is used to announce the roaming AP MLD.
    The new ML element is preferable.
  The updated BTM procedure is used to acquire the neighbor AP MLD’s information.
  The update MLD reconfiguration procedure is used to do the MLD roaming.

## Slide 13: Reference
[1] https://mentor.ieee.org/802.11/dcn/23/11-23-0170-00-0uhr-smooth-roaming-discussion.pptx
[2] https://mentor.ieee.org/802.11/dcn/23/11-23-0632-01-0uhr-smooth-roaming-follow-up.pptx