## Slide 1: Dynamic Power Save– follow up
Date: 2024-01-14
Authors:
January 2024
Notes: September 2012

## Slide 2: Introduction
UHR SG discussed AP power save (PS) in several contributions [1, 2, 3, 4]
  Which focus on the need for mechanisms to reduce AP power consumption and
  Discussed viable candidate features that can achieve this goal
Consequently, the UHR SG agreed [5] to defining
  “a mechanism to reduce power consumption for Access Points (APs) (including mobile APs) and improved Peer-to-Peer (P2P) operation compared to the Extremely High Throughput MAC/PHY operation.”
In addition, the UHR SG also acknowledged that
  Reducing power consumption of WLAN devices is required to prolong the battery life of untethered devices (e.g., non-AP STA, Mobile APs), reduce device cost, and lower energy bills of customers deploying non-AP and AP STAs in most scenarios (e.g., residential, enterprise, industrial, venues).
January 2024

## Slide 3: Overview
We propose to generalize the dynamic PS concept [1, 2]
  So that it is applicable at both AP and STA side
    Improving power consumption for both devices
And continue with some design details related to
  Choice of initial control frame
  Specific details that depend on the type of device
January 2024

## Slide 4: Dynamic Power Save
STA is in Listen State unless solicited to transition to Awake state
  Listen State: STA is only capable of RX PPDUs of certain configuration
    E.g., non-HT (dup) PPDUs, and mandatory data rates
  Awake State: STA is capable of RX PPDUs with highest BW/NSS
    E.g., as advertised in most recent Caps/OMN/OM Control (for both AM and PS modes)
Initial control frame (ICF) causes transition from listen to awake state
  RTS frame is one candidate since its generation is supported by both APs and STA
    Cons: PIFS-based CCA requires STA in full BW; No padding available for extra processing time
      And modifying the frame format can lead to legacy/interoperability issues
  MU RTS Trigger frame is another candidate since it does not have the above cons
    But needs to be enabled in transmission at the STA side to enable dynamic PS
  BAR frame is another candidate since its generation is supported by both APs and STA
    But padding needs to be added for extra processing time
In the following we focus on the last two candidates
<20MHz,1SS>
Non-HT (dup) PPDU
<80MHz,1SS>
<160MHz, 2SS>
Beacon
…
Beacon
ICF
ICR
Data
BA
ICF
ICR
Data
BA
Frame Exchange/TXOP
Frame Exchange/TXOP
January 2024

## Slide 5: ICF: MU RTS Trigger vs BAR frame
MU RTS Trigger frames:
  AP: TX of MU RTS Trigger frame is already supported
    Currently only allowed to be broadcast; should enable unicast as well
      STA determines from RA whether it needs to prepare response
    Has padding properties; could inherit rules from eMLSR
  Non-AP STA: Needs enablement in TX of MU RTS Trigger frame
    Enable unicast MU RTS Trigger frame; RA set to MAC address of the AP
    Required if AP advertises that is operating in dynamic PS mode
      AP advertises the amount of padding required when the AP is in dynamic PS mode
BAR frames:
  Already supported by both AP and STA
    “Mandatory” support for C-BAR and optional support for Multi-TID BAR
  Does not have padding; although can be added (see next slides)
<20MHz,1SS>
Non-HT (dup) PPDU
<80MHz,1SS>
<160MHz, 2SS>
Beacon
…
Beacon
M-RTS
CTS
Data
BA
BAR
BA
Data
BA
Frame Exchange/TXOP
Frame Exchange/TXOP
January 2024

## Slide 6: ICF: MU RTS Trigger/BAR frame
Padding: Inherited from eMLSR & design from Trigger frame
Inclusion of intra-MPDU FCS/MIC [6, 7]
  FCS/MIC field prior to padding helps verify contents well in advance
    MIC present when frame is protected [6] & FCS present when frame is not [7]
Inclusion of additional feedback
  Enables flexible delivery of control information
    Information beneficial from a dynamic PS perspective in next slides
Octets: | 2 | 2 | 6 | 6 | 2 | 0 or 2 | variable | 4
 | Frame Control | Duration | RA | TA | BAR Control | BAR Information | Padding | FCS
 | Frame Control | Duration | RA | TA | Common Info | User Info List | Padding | FCS
Octets: | 2 | 2 | 6 | 6 | 8 | Nx5 | variable | 4
MU RTS Trigger frame
BAR frame
January 2024

## Slide 7: MU RTS vs BAR frame: Comparison
Overhead Comparison (focusing on single user):
  MU RTS: Common Info + User Info + Special User Info (320 MHz)
    Most subfields of these fields are reserved/unnecessary (except BW, AID,
      At least for the purpose of dyn. PS (good to have BW, NSS though, see next slide)
    Airtime for transmitting these 2 (or 3) fields is 20 us (or 24 us) at 6 Mbps
  BAR: BAR Control + BAR Information (2 octets + NT*2)
    BAR Control needed to distinguish variants; 8 reserved bits available to use
    BAR Information needed when soliciting BlockAck Bitmaps (for set of TIDs)
      For DPS no need to solicit BlockAck bitmaps; one bit in the BAR Control can say so
    Airtime for transmitting these 2 octets (BAR Control) is 4 us at 6 Mbps;
Comparison of other functionalities:
  MU RTS Trigger solicits CTS frame, which is 14 octets long and not flexible; has CTS timeout reset property
  BAR frame solicits a C/M-BA (used to also Ack), which is at least 24 octets, and is flexible; ignores CS to ack
January 2024

## Slide 8: Dyn. Power Save Optimizations
Feedback Control in ICF/ICR allows for additional optimizations
  Advertises the BW planned to be used for that TXOP/exchange
    BW must be same or narrower to what was advertised in the ICF
      Pros: STA needs not open full BW but simply as much as advertised by ICF
  Enable advertisement of RX NSS in ICF
    RX NSS must be same or narrower to what was advertised in ICF
      Pros: STA needs not use full RX NSS but simply as much as advertised by ICF
        Remaining SSs may be turned off or used for other purposes (links, techs, etc.)
  Enable dynamic BW negotiation with ICF/ICR exchange (unicast only)
    Pros: Inherit the benefits of legacy dynamic BW negotiation of RTS/CTS
  Etc.
Note: These are beneficial from coexistence perspective as well [ref.]
January 2024

## Slide 9: Conclusions
We continued discussions on PS protocols aiming at
  Minimizing power consumption while ensuring that STAs continue to be serviced without disruptions
  Accounting for the necessary trade-offs/constraints
    Which arise due to use cases/scenarios and/or device configurations
We generalized dynamic AP PS concept to also cover the STA side
  Giving some more details on the expected behaviors,
  Pointing out certain limitations to the use of RTS/CTS, and
  Proposed using MU RTS/BAR frame to overcome these limitations
January 2024

## Slide 10: Straw Poll 1
Do you support to define a power save mode for an UHR STA wherein the STA may transition from a lower operation mode to a higher operation mode, for a duration of time (e.g., TXOP or Service Period), upon reception of a specific initial Control frame from a peer UHR STA?
  Lower operation mode (e.g., 20 MHz BW, one SS, limited data rates, etc.)
  Higher operation mode (e.g., parameters advertised in Capability/Operation elements, OM Control, etc.)
  Which is the specific Control frame is TBD
  Whether the mode can be used by a non-mobile AP is TBD
January 2024

## Slide 11: Straw Poll 2
Do you support that an UHR STA may request a peer UHR STA to initiate frame exchanges, which require the UHR STA to be in higher operation mode, with an initial control frame?
January 2024

## Slide 12: References
[1] 11-23/10r0 “Considerations for enabling AP power save”, Alfred Asterjadhi et. al.
[2] 11-23/15r0 “AP MLD power management”, Liwen Chu, et. al.
[3] 11-23/225r0 “Considering unscheduled AP power save”, Guogang Huang et. al.
[4] 11-23/244r1 “AP Power Save PAR addition proposal”, Amelia Andersdotter, et. al.
[5] 11-23/480r3 “UHR Proposed PAR”, Laurent Cariou, et. al.
[6] 11-23/312r0 “Thoughts on Secure Control frames”, Alfred Asterjadhi, et. al.
[7] 11-23/1873r0 “Post-FCS MAC Padding”, Sindhu Verma, et. al.
January 2024