## Slide 1: Multi-Link based Multi-AP Coordination for Low-Latency Traffic – Follow Up
Date: 2025-03-10
Authors:

## Slide 2: Abstract
Multi-link operation (MLO) between two multi-link devices (MLDs) are key features supported in P802.11be Extremely High Throughput (EHT) [1].
In PAR of P802.11bn, the Ultra High Reliability (UHR) capability has been defined to improve Rate-vs-Range enhancement, reduce latency, and reduce power consumption for AP, compared to P802.11be EHT MAC/PHY operation [2].
Multi-AP coordination (MAPC) framework (aka. Multi-AP operation/transmission) has been discussed as one of the key features defined in Draft 802.11bn UHR D0.1.
In this contribution, we propose propose ML-based MAPC protocol with low-latency (LL) traffic.

## Slide 3: Recap: Low-Latency Traffic in MLDs [3-7]
During multi-link setup, AP MLD may classify traffic between AP MLD and non-AP MLD into one or more categories based on the latency requirements of the traffic.
  e.g., a low latency (LL) category for LL traffic, and a non-low latency (non-LL) category for non-LL traffic.
  In operation, LL traffic may be associated with one or more TIDs associated with one or more predetermined access categories (ACs) or traffic streams.
AP MLD may negotiate with non-AP MLD a traffic identifier (TID) to link mapping to assign traffic streams to available links.
AP MLD may prioritize different links based on the category of traffic.
  e.g., A traffic stream of LL category between AP MLD and non-AP MLD may be mapped to link 2.

## Slide 4: Low-Latency Traffic in Multi-BSS
AP MLD 2 may transmit a non-LL frame (e.g., frame conveying non-LL traffic to associated STA2), via link 2, at the time T1.
Case: Non-AP MLD 1 associated with AP MLD 1 may hear the non-LL frame, via link 2, and may set its NAV at T2.
Problem:
  Non-AP MLD 1 may postpone the transmission of a LL frame (e.g., frame conveying LL traffic, as shown in the figure), via link 2, at time T3.
  As a result, delay is introduced.

## Slide 5: Multi-AP Coordination based on Link Priority – Solution 1
AP MLD 1 transmits to AP MLD 2 a notification frame indicating that link 2 is prioritized for LL traffic.
Accordingly, when a non-LL traffic arrives at AP MLD 2 for transmission, AP MLD 2 selects link 1 for the transmission of the non-LL frame.
  For example, the selection may be based on the priority of link 1 and/or the priority of link 2 specified in the notification frame.
AP MLD 2 transmits a non-LL frame, via link 1, to non-AP MLD 2.
Non-AP MLD 1 is able to transmit a LL frame, via link 2, to AP MLD 1.

## Slide 6: Multi-AP Coordination based on Link Priority – Solution 2
AP MLD 2 transmits to AP MLD 1 a request frame soliciting a response from AP MLD 1.
In response, AP MLD 1 transmits to AP MLD 2 a response frame indicating that link 2 is prioritized for LL traffic.
Accordingly, when a non-LL traffic arrives at AP MLD 2 for transmission, AP MLD 2 selects link 1 for the transmission of the non-LL frame.
  For example, the selection may be based on the priority of link 1 and/or the priority of link 2 specified in the response frame.
AP MLD 2 transmits a non-LL frame, via link 1, to non-AP MLD 2.
Non-AP MLD 1 is able to transmit a LL frame, via link 2, to AP MLD 1.

## Slide 7: Summary
In this contribution, we proposed the methods of ML-based MAPC protocol with low-latency traffic.

## Slide 8: Q&A Discussion
C: Generally, low latency streams can exist to all the links so that whichever is available free they can transmit on, and it need to make sure that one link is more likely to work for low-latency traffic. As earlier presentations show, effective reporting such as BSR thereby covers not only the low latency traffic but also other classes of traffic, too. This seems like a general solution that would address this particular use case also.
A: Mapping low latency traffic to links can be AP/STA implementation specific. For example, AP can map low latency traffic to either one or more links or all links. Both are possible and can be supported in 11be.
  The benefit of one or dedicate link mapping, in other words, mapping with priority of links, is that using dedicated link (with a high priority) for low-latency traffic so that the possibility of waiting time for delivering the low-latency traffic could be reduced as the events of transmitting/receiving non-LL traffic are much less on the LL traffic dedicated link (with a high priority).

## Slide 9: Straw Poll 1
Do you support the following text?
An AP, affiliated with one AP MLD, may exchange management frames with another AP affiliated with another AP MLD to establish a coordination agreement between the AP MLDs.
  Yes
  No
  Abstain

## Slide 10: Straw Poll 2
Do you support the following text?
An AP MLD may send/share a link priority for traffic categories to another AP MLD to protect the low-latency traffic.
  Yes
  No
  Abstain

## Slide 11: References
IEEE P802.11be Draft 5.0
IEEE P802.11bn Draft 0.1
IEEE 802.11-23/0480r3, P802.11bn Project Authorization Request
IEEE 802.11-23/0069r1, Considerations on Latency Improvement, 2023-03-27
IEEE 802.11-20/0418r4, QoS management framework in 802.11be, 2020-08-11
IEEE 802.11-19/0163r1, Low latency enhancements for R1, 2020-07-28
IEEE 802.11-20/0697r3, Supporting latency sensitive applications in 11be, 2020-05-28
IEEE 802.11-20/0408r6, Prioritized EDCA channel access over latency sensitive link(s) in MLO, 2020-03-09
IEEE 802.11-23/2204r2, TGbn November December 2023 teleconference minutes