## Slide 1: High Level Thoughts on DRU Design
Date: 2023-11-xx
Authors:
Name | Affiliations | Address | Phone | Email
Lin Yang | Qualcomm |  |  | 
Bin Tian |  |  |  | 
Youhan Kim |  |  |  | 
Qifan Chen |  |  |  | 
Notes: September 2012

## Slide 2: Introduction
Many contributions [1]-[7] have proposed Distributed tone Resource Unit (dRU) for 11bn and discussed potential tone plan, pilot location, signaling, etc.
Before discussing the detailed design options, it is better to first converge on high level directions on some topics of dRU design
In this presentation we will share our thoughts and recommendations

## Slide 3: PSD Limit and Distributed Transmission
Regulations put limitations on PSD in Sub-7GHz. E.g.,
  In 6GHz, for a non-AP STA in LPI bands, the PSD limit is -1dBm/MHz
  10dBm/MHz PSD limit in 2.4GHz bands in EU/China/Japan/Korea
Mitigation methods: spreading bandwidth for small RUs
  If spreading RU tones over 80MHz
    RU/26/52 can gain more than 11dB power
    Even RU484 can gain 2.69dB
 | Power Gain of Distributed tone Transmission over Local Transmission (dB) |  | 
Spreading BW -> | 20MHz | 40MHz | 80MHz
RU26 | 8.13 | 11.14 | 11.14
RU52 | 6.37 | 8.13 | 11.14
RU106 | 3.36 | 6.37 | 8.13
RU242 | N/A | 2.69 | 5.12
RU484 | N/A | N/A | 2.69
Assumption
  Tone distribution to max Tx power
  Assuming equal power per tone

## Slide 4: Where Should dRU Be Applied to
Focus on TB PPDU using UL OFDMA which has significant power pooling gain
  Using distributed tone plan, each STA can improve its TX power by spreading to wide bandwidth
  Power pooling gain with good spectral efficiency
  Applies to all MCS
DL OFDMA and MU-MIMO : no need to support due to lack of gain and additional complexity
SU: needs further investigation but need to consider
  Already has DUP mode
  Preamble can't be tone distributed for backward compatibility
  Un-populated tones will be wasted if spread

## Slide 5: High Level Discussion on dRU Design
Some open questions
  Spreading BW: 80MHz or higher
  Mixture of distributed RU (dRU) and regular RU (rRU)
  Supporting RU/MRU set
  Support of puncturing
  Support of STA with different BW capability in wide bandwidth OFDMA
    20MHz operating STA
    80/160MHz operating STA

## Slide 6: dRU Spreading BW
For 20/40/80MHz PPDU BW, it is reasonable for all dRUs to spread to PPDU BW
For PPDU BW>80MHz, still recommend to limit dRU spreading BW to 80MHz due to the following reasons
  Not all devices support larger than 80MHz
  Spreading over 80MHz can already harvest majority of power gains
  Need changes to segment parser and existing per 80MHz processing flow if spreading beyond 80MHz
For dRU size > RU996, if perform per 80MHz segment spreading, there is also complexity on scheduling and power allocation
  For example, for MRU996+484 in 160MHz OFDMA transmission, if RU996 and RU484 each spread over its 80MHz, then per tone power will be different
Overall to balance the complexity and gain, suggest to limit the spreading BW to 80MHz, and dRU size <RU996

## Slide 7: Mixture of dRU and rRU
For 20/40/80MHz PPDU, mixture of dRU + rRU is not preferred
  More complicated in scheduling, tone plan, signaling and AP receive processing
  dRU can spread over entire PPDU BW to max Tx power
For 160/320MHz PPDU, hybrid mode can be supported with limited flexibility to reduce scheduling and signaling complexity
  Propose per 80MHz decision: each 80MHz segment can use either dRU or rRU but no mixture
    If 80MHz segment uses dRU, then the spreading BW is 80MHz unless there is a puncturing
    If 80MHz segment uses rRU, minimal RU size is RU242

## Slide 8: Support of RU/MRU<996 Tones
dRU26 support
  dRU26 needs to be supported for 20 MHz and 40 MHz PPDU
  For 80MHz PPDU, dRU26 can be transmitted only up to 13dBm. Well using dRU52 the Tx power can be 16dBm, no much benefit to schedule dRU26 in 80MHz
Not to support of MRU52+26 and MRU106+26 in dRU
  Supporting MRU with center RU26 will further complicate the dRU tone plan design
  Marginally useful
  Only supports the most useful modes to reduce implementation/testing complexity
Prefer BW dependent dRU size support to maximize BW and power efficiency
  20MHz: RU26, RU52, RU106
  40MHz: RU26, RU52, RU106, RU242
  80MHz: RU52, RU106, RU242, RU484

## Slide 9: Supporting BW Puncture
Puncture brings another complexity to dRU design, need to balance the complexity/flexibility/gain
No puncture needs to be supported for 20/40MHz PPDU
  For 20MHz PPDUs, the distributing BW is 20MHz only
  For 40MHz PPDUs, the distributing BW is 40MHz only
For 80MHz and above, dRU and puncturing decision can be done per 80MHz segment
  If puncture occurs in 80MHz subblock, can leverage tone plan design for 20MHz and 40MHz spreading BW
    E.g., 20MHz punctured in 80MHz, one or multiple RUs spread over 20 MHz, another one or group of RUs spread over remaining 40MHz
    To avoid the need of new tone plan for 60MHz

## Slide 10: Supporting STA in wide BW OFDMA
Mainly the following two cases
  20MHz operation STA in 40, 80, 160, 320MHz
  80/160MHz operation STA in 160, 320MHz
80/160MHz operation STAs fit well with the 80MHz spreading BW limit
20MHz operation STA in wide bandwidth OFDMA need some discussion
  20MHz operation devices can only support spreading BW of 20MHz
  It is very challenge to support multiple spreading BWs in 40/80MHz
Prefer 20MHz operation STA support only in the following dRU modes
  PPDU BW of 20MHz
  In punctured 80MHz subblock where 20MHz spreading BW is used

## Slide 11: dRU Tone Plan Design Philosophy
Maximize power gain and spectral efficiency gain
  Given PSD limit (e.g., -1dBm/MHz), minimize the number of tones per 1MHz to maximize Tx power
  Spectral efficiency should not be worse than regular OFDMA transmission
    E.g, existing OFDMA mode can support 9 RU26 in 20MHz, dRU should be able to support the same
Keep dRU tone mapping simple
  Keep hierarchical OFDMA tone plan and pilot structure
  Make even distribution as much as possible to ensure channel smoothing

## Slide 12: Summary
We discussed high level questions on dRU design
  Spreading BW limit
    prefer up to 80MHz
  Mixture of dRU and rRU
    no hybrid mode for up to 80MHz, per 80MHz dRU/rRU switch
  RU/MRU
    no MRU, prefer BW dependent RU size support
  BW puncturing
    Per 80MHz dRU and puncturing decision
  STA with different BW capability in wide bandwidth OFDMA using distributed tone plan
    Prefer support 20MHz operation STA only when spreading BW of 20MHz
Briefly discussed dRU design criteria
  Max. power gain and efficiency gain
  Keep dRU tone mapping simple

## Slide 13: References
[1] 11-23-0037-00-0uhr-uhr-feature-to-overcome-psd-limitations-distributed-tone-resource-units
[2] 11-23-0281-00-0uhr-considerations-on-ru-mru-designs-for-uhr
[3] 11-23-1117-00-0uhr-dru-signaling-for-uhr
[4] 11-23-1115-00-0uhr-cfo-impact-and-pilot-design-for-dru
[5] 11-23-1447-00-0uhr-cfo-impact-and-pilot-design-for-dru-follow-up
[6] 11-23-1448-00-0uhr-further-considerations-on-dru
[7] 11-23-1511-01-0uhr-pilot-tone-allocation-and-other-considerations-of-tone-distributed-rus-for-uhr

## Slide 14: Straw Poll #1
Do you agree to introduce distributed tone RUs (dRU) transmission in 11bn?

## Slide 15: Straw Poll #2
Do you agree that 11bn UL OFDMA supports distributed tone RUs (dRU) in UHR TB PPDU?

## Slide 16: Straw Poll #3
Do you agree that the allowed spreading BWs of an dRU are 20MHz, 40MHz and 80MHz?

## Slide 17: Straw Poll #4
Do you agree the following BW dependent dRU size support to maximize BW and power efficiency?
  No MRU in distributed transmission
  20MHz: RU26, RU52, RU106
  40MHz: RU26, RU52, RU106, RU242
  80MHz: RU52, RU106, RU242, RU484

## Slide 18: Straw Poll #5
Do you support no hybrid dRU (distributed tone RU) and rRU (regular RU) mode for up to 80MHz and allowing per 80MHz dRU/rRU switch if PPDU BW >80MHz?

## Slide 19: Straw Poll #6
Do you agree that in a punctured 80MHz subblock, the only allowed spreading BWs are 20MHz and 40MHz?