## Slide 1: Non-Primary Channel Access (NPCA)
Date: 2024-1-12
Authors:

## Slide 2: NPCA discussions so far in UHR SG/TGbn
The non-primary (secondary) channel access (NPCA) was proposed in the following contributions with the problem statement, design principles, high-level concepts, different options, and simulation results
  11-23/34, “Non-primary channel utilization,” Sindhu Verma
  11-23/631, “Secondary channel usage and secondary 20MHz channel backoff,” Liwen Chu
  11-23/797, “Non-primary channel access,” Yongho Seok
  11-23/961, “UHR secondary channel access,” Minyoung Park
  11-23/962, “UHR secondary channel access evaluation,” Dibakar Das
  11-23/1112, “Thoughts on secondary channel access,” Insun Jang
  11-23/1365, “Discussions on non-primary channel access,” Sanghyun Kim
  11-23/1414, “Secondary channel usage follow up,” Liwen Chu
  11-23/1444, “Non-primary channel access evaluation – follow-up,” Dibakar Das
  11-23/1288, “Non-primary channel utilization – follow-up,” Sindhu Verma
  11-23/1911, “Secondary channel access and frame transmission,” Dongju Cha
  11-23/1913, “Secondary channel access operation,” Dongju Cha
  *11-23/1935, “Secondary channel usage follow up,” Liwen Chu
  11-23/1951, “Concurrent CCA for non-primary channel access,” Leonardo Lanante
  *11-23/2023, “Further discussion on non-primary channel access,” Sindhu Verma
  *11-23/2039, “Secondary channel usage follow up,” Liwen Chu
Although there are differences in the details of the proposals, there is a good alignment on a high-level concept to enable non-primary (secondary) channel access while the primary channel is busy

## Slide 3: Recap: Problem [11-23/961]
For any 802.11 transmission (20/40/80/160/320MHz),
  The primary 20 MHz channel must be idle to access a wideband channel (>20 MHz)
  A STA cannot transmit on any idle secondary channels if the primary channel is busy
This is not the best way to utilize < 7 GHz bands, especially for 160/320 MHz
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
time
20MHz PPDU
(interference, OBSS)
80MHz PPDU
Available
Secondary channels available
Busy
Busy
frequency
40MHz PPDU
(interference, OBSS)
(STA to AP or AP to STA)
Now STA can transmit a packet

## Slide 4: Recap: Goal [11-23/961]
If the primary channel is busy and the secondary channel(s) are available, an AP/STA transmits on the available secondary channel(s)
Busy
Primary 20MHz
Secondary 20MHz
Secondary 40MHz
time
20MHz PPDU
(interference, OBSS)
80MHz PPDU
Busy
Busy
frequency
40MHz PPDU
(interference, OBSS)
(STA to AP or AP to STA)
STA can transmit a packet on the secondary channels while the primary channel is busy
60MHz PPDU
40MHz PPDU

## Slide 5: Recap: Design considerations [11-23/961]
Need to be simple
Before using the secondary channels, an AP/STA needs to know idle/busy status of the secondary channels
No major additional receive capability on the secondary channels

## Slide 6: NPCA Primary Channel and NPCA Channel Bandwidth
To manage the complexity of the NPCA operation, we propose to limit the number of secondary channels on which a STA contends while the primary channel is busy to one
Define one NPCA primary channel
  One of the secondary channels on which channel access is performed while the primary channel is busy
Define one NPCA channel bandwidth
  Channel bandwidth on which NPCA is performed while the primary channel is busy
  Accessing the secondary channels of the NPCA primary channel follows the same PIFS rules defined in the baseline
An AP announces the following:
  Location of the NPCA primary channel
  NPCA channel bandwidth
Primary channel (P1)
NPCA primary channel (P2)
Secondary channels of the primary channel
Secondary channels of the NPCA primary channel
NPCA channel bandwidth
frequency
time

## Slide 7: When AP and STA have different views on channel idle/busy Case 1: AP side is busy, but STA side is idle
AP1
STA1
STA2
AP2
STA3
P1
P2
Secondary for P1
Secondary for P2
NAV set by AP2
AP1 and STA2 moves to P2
AP1 and STA2 can use P2 for frame exchanges
STA1 is still on P1 (NAV not set, out of range from AP2)
STA1 may transmit to AP1 on P1 but AP1 is not on P1and doesn’t respond – same as today’s behavior when AP1 is blocked by NAV
AP1 may transmit to STA1 on P2 but STA1 is not on P2 (AP1 doesn’t know if STA1 moved to P2)
On P1
On P2
On P2
On P1
OBSS1
NAV set by AP2
AP3
STA4
OBSS2
BSS
P1: primary channel
P2: NPCA primary channel

## Slide 8: Case 2: AP side is idle, but STA side is busy
P1
P2
Secondary for P1
Secondary for P2
AP1 and STA2 stay on P1
STA1 moves to P2 and stays on P2 during NAV
AP1 may transmit to STA1 on P1 but doesn’t get any response back (this is same as today’s behavior where STA1 is blocked by OBSS)
STA1 may transmit to AP1 on P2 but doesn’t get response back from AP1
AP3
On P1
STA4
On P1
NAV set by AP3
NAV
AP1
STA1
STA2
On P2
On P1
On P1
AP2
STA3
OBSS1
STA4
OBSS2
BSS

## Slide 9: Proposal to address different views of medium busy/idle
AP3
STA4
AP1
STA1
STA2
AP2
STA3
OBSS1
STA4
OBSS2
Beacon (AP3)
Beacon (AP2)
{AP3}
{AP2}
{AP2}
In a BSS, each AP/STA build a list of OBSS APs (for simplicity) that they can hear on the primary channel (see examples below) - AP1{AP2} - STA1{AP3} - STA2{AP2}
AP announces to its associated STAs the list of OBSS APs that it received (e.g., in a beacon frame) – AP1 {AP2}
Each STA compares the OBSS AP list that it received from the AP with the list of OBSS APs each STA can hear and indicate this to the AP - STA1{none} - STA2{AP2}
When a STA receives a frame from an OBSS AP that was included in the OBSS AP list received from the AP, the STA moves to P2 and may initiate TXOP to the AP; otherwise stays on P1. - STA1: doesn’t move to P2 when it receives a frame from AP3 - STA2: moves to P2 when it receives a frame from AP2; may initiate TXOP to AP1
When the AP receives a frame from an OBSS AP that it included in the OBSS AP list and the OBSS AP was indicated by a STA in c), it moves to P2 and may initiate TXOP to the STA. - AP1: moves to P2 when it receives a frame from AP2; may initiate TXOP to STA2
BSS
Frame exchanges
Frame that sets NAV

## Slide 10: Summary
The current secondary channel access mechanism is inefficient for a wideband channel (e.g., 160 or 320 MHz) and UHR needs a better secondary channel access scheme to fully utilize a wideband channel
In TGbn, there is a good alignment on a high-level concept to enable NPCA
To manage the complexity of NPCA, we propose to limit the number of the secondary channels on which a STA contends while the primary channel is busy to one

## Slide 11: SP
• Do you support to define a mode of operation that enables a STA to access the secondary channel while the primary channel is busy due to OBSS traffic and other TBD conditions?
  – The mode of operation shall not assume that the STA is capable to detect or decode a frame and obtain NAV information of the secondary channel concurrently with the primary channel.
  – A BSS shall only have a single NPCA primary channel (name TBD) on which the STA contends while the primary channel of the BSS is busy

## Slide 12: Backup Slides

## Slide 13: Recap: Proposal [11-23/961]
AP behavior (transmitter)
  Monitors medium idle/busy on the second primary channel (P2)
    ED CCA
  If the first primary channel (P1) is busy for NAV time duration and the second primary channel is idle for X (TBD) time duration
    On the second primary channel, AP does backoff and initiates TXOP with BSRP Trigger or RTS frame (a control frame) to target STA(s)
      RTS/CTS or BSRP/BSR type of control frame exchange is needed to know if the target STAs are on the second primary channel
      The TXOP ends before the NAV=0 set at the first primary channel
STA behavior (receiver)
  If the first primary channel is busy for NAV time duration
    Move to the second primary channel and wait for BSRP or RTS (a control frame) from the AP
    STA goes back to the first primary channel before NAV=0 of the first primary channel
Busy
P1 20MHz
S1.1 20MHz
OBSS frame exchanges (busy)
(both AP and STA received OBSS packet and set NAV)
Busy
Busy
frequency
P2 20MHz
S2.1 20MHz
40MHz PPDU (TX)
BSRP
BSR
BA
S2.2 20MHz
S2.3 20MHz
S1.2 20MHz
S1.3 20MHz
AP/STA decode OBSS packet or PHY preamble and sets NAV
ED CCA Access secondary channels if medium Idle for > X time duration (a value >PIFS and < maxPPDU)
Frame exchanges end before NAV =0 on P1 (to keep the medium sync on P1)
80MHz PPDU (TX)
BSRP
BSR
BA
OBSS frame exchanges
(busy)
40MHz PPDU (TX)
BSRP
BSR
BA
NAV=0
PIFS
PIFS
1st primary
2nd primary
BO
(idle)

## Slide 14: Recap: When AP and STA have different views on channel idle/busy [11-23/961]
From AP side P1 is busy (NAV set) but from STA side P1 is idle
  AP may send BSRP or RTS on P2 and available secondary channels
    STA is not monitoring P2 and does not respond to BSRP/RTS
  STA may send RTS on P1
    AP is monitoring P2 and does not respond to RTS on P1
From AP side P1 is idle but from STA side P1 is busy (NAV set)
  AP may send BSRP or RTS on P1 and available secondary channels (not including P2)
    STA is waiting on P2 and does not respond to BSRP/RTS on P1
  AP may send BSRP or RTS on P1 and available secondary channels (including P2)
    STA is waiting on P2 and may respond to BSRP/RTS on P2
  STA may send RTS on P2
    AP is monitoring P1 and does not respond to RTS on P2
For simplicity, frames on P2 while P1 is idle is ignored to avoid decoding OBSS frames on secondary channels (while decoding OBSS frames on secondary channels create blindness on the primary)
  Decode frames on P2 only when P1 is busy