## Slide 1: HT Control field expansion
Date: 2023-11-10
Authors:

## Slide 2: Background
HT Control field and A-Control subfield are useful.
  Only 5 A-Control IDs are reserved for future usage.
  Expansion with the reserved A-Control ID ONES leads to overhead and complexity.
  Overhead: A new field will be added and indicated by A-Control ID ONES.
  Complexity: HW needs to parse HT Control field. If HT Control field is HE Variant, then extract A-Control subfield and furtherly extract each Control subfield. Then parse the last Control subfield. If the A-Control ID in the last Control subfield is equal to ONES, HW needs to extract the Data field after the new added field.

## Slide 3: Another way for A-Control field expansion
Retry subfield is reserved in frames that are not non-A-MPDUs and under a block ack agreement.
  Most of exchanged frames in UHR are frames that are not non-A-MPDUs and under a block ack agreement.
  For other frames, it is possible in UHR to check whether they are retransmissions or not, regardless Retry subfield.
Retry subfield can be leveraged for A-Control field expansion.
  If Retry subfield is equal to 0, it is HT Control field.
  If Retry subfield is equal to 1, it is A-Control Expansion field.
PV | Type | … | Retry=1 | … | +HTC=1
Duration | … | A-Control Expansion
Frame Control
PV | Type | … | Retry=0 | … | +HTC=1
Duration | … | HT Control
Frame Control

## Slide 4: Conclusion
A-Control Expansion field indicated by Retry subfield is proposed.
  It is easier and no overhead, comparing to use A-Control ID ONES.
  New MPDU is as following.
2 | 2 | 6 | 0 or 6 | 0 or 6 | 0 or 2 | 0 or 6 | 0 or 2 | 0 or 4 | variable | 4
Frame Control | Duration/ID | Address 1 | Address 2 | Address 3 | Sequence Control | Address 4 | QoS Control | HT Control/ A-Control Expansion | Frame Body | FCS
B0 B1 | B2 B3 | B4 B7 | B8 | B9 | B10 | B11 | B12 | B13 | B14 | B15
Protocol Version | Type | Subtype | To DS | From DS | More Fragments | Retry/ A-Control Expansion Indicator | Power Management | More Data | Protected Frame | +HTC

## Slide 5: SP
Do you agree to define the following MPDU for transmission between 11bn STAs?
2 | 2 | 6 | 0 or 6 | 0 or 6 | 0 or 2 | 0 or 6 | 0 or 2 | 0 or 4 | variable | 4
Frame Control | Duration/ID | Address 1 | Address 2 | Address 3 | Sequence Control | Address 4 | QoS Control | HT Control/ A-Control Expansion | Frame Body | FCS
B0 B1 | B2 B3 | B4 B7 | B8 | B9 | B10 | B11 | B12 | B13 | B14 | B15
Protocol Version | Type | Subtype | To DS | From DS | More Fragments | Retry/ A-Control Expansion Indicator | Power Management | More Data | Protected Frame | +HTC