## Slide 1: R-TWT for Multi-AP
Date: 2023-11-06
Authors:

## Slide 2: Multi-AP scenarios
In previous generations, we have improved efficiency (scheduling, …) and reliability for Latency-sensitive traffic by considering mostly a single BSS
The goal of AP coordination is to extend these enhancements by considering multiple overlapping BSSs
  Simplest scenario is when all these OBSSs are from the same management domain (same ESS): typical enterprise deployment (calling this scenario a managed OBSS scenario)
  More complicated scenario, but not less useful, is when OBSSs are not part of the same management domain (calling this scenario an unmanaged OBSS scenario)
Note that we consider P2P or mobile APs also as part of this coordination
Since 11be, we have investigated several mechanisms to improve coordination between neighboring APs (mainly for managed OBSS scenario)
  Those are mainly based on one AP gaining a TxOP and sharing that TxOP with overlapping APs in time (C-TDMA), frequency (C-OFDMA) or space (C-SR) and possibly with some more advanced PHY coordination.
  At least some of those modes (if not all) will be defined in UHR
  The KPIs for these modes are very diverse: throughput, efficiency, reuse, latency, …

## Slide 3: R-TWT tool
In 11be, we have defined Restricted-TWT (r-TWT)
  Goal was primarily to increase the probability to access the medium and transmit low latency traffic
The r-TWT tool is basically doing the following:
  Forcing STAs from the BSS to stop their ongoing TxOP before the start of the r-TWT SP
  Creating a contention period at the start of the r-TWT SP and increasing the chances that the AP will gain the TxOP and schedule critical traffic during the SP.

## Slide 4: R-TWT for Multi-AP scenarios
In this contribution, we investigate how the r-TWT tool (“as is” or modified) can be useful for Multi-AP deployments
There are 2 main angles to this:
  1) Can we extend the protection (or increased probability to meet the QoS requirement of some traffic) that r-TWT tool is providing within a BSS to multiple overlapping BSSs
  2) Can the r-TWT functionality of creating a contention period at a relative precise time be useful to help also for the other Multi-AP modes (C-TDMA/FDMA/SR…) or M-AP objectives

## Slide 5: 1a) Extend r-TWT protection rules to OBSSs
An AP (AP1) is advertising an rTWT SP1 so that all EHT STAs supporting r-TWT shall end their TxOP before the start of an rTWT SP
A coordinated OBSS (AP2) could advertise an OBSS rTWT SP that overlaps in time with rTWT SP1 so that its associated STAs also respect that rule (end their TxOP before the start of the rTWT SP)
  rTWT SP advertised by AP2 would be in reference to the TSF of AP2, but be coordinated so that it overlaps in time with rTWT SP1
  Proposed in 11be but so far not accepted
  Additional rule to define would be that the OBSS (AP2) would also have to respect the rule (end the TxOP before the start of the rTWT SP)

## Slide 6: 1a) Extend r-TWT protection rules to OBSSs
Signaling to enable this in a TWT element is quite straightforward
  Just an explicit signaling that the TWT SP is for an OBSS
Ensuring no drift of OBSS rTWT SPs compared to the rTWT SP1 requires some discussion
  TSF alignment between OBSSs, TSF drift estimation and rTWT timing correction, …
Another challenge is obviously that most of/all the OBSSs (and their associated STAs) will support this and accept to extend that protection
  For managed scenarios, the APs will be coordinating through the common management entity. So no need to define anything in UHR.
  For unmanaged scenario, we will need to define in UHR the negotiation (Request/Response) between OBSSs in order to enable this advertisement. We obviously need to find the right incentives to push unmanaged APs/P2Ps to coordinate and trust each other
    If, among 2 OBSSs that negotiate, each OBSS gets a protection extension for one of its rTWT SP, it would be a Win-Win situation

## Slide 7: 1b) Multiplexing in time rTWT SPs from OBSSs
If 2 OBSSs want to establish rTWT SPs for some of their traffic, they can coordinate in order to make sure that each rTWT SP will not overlap with the rTWT SP of the neighbor
Similarly, 2 overlapping Mobile APs/P2Ps can coordinate the SPs during which they are Active/Inactive in order to be as alone as possible on the medium during operation.
This can be naturally achieved as the rTWT SPs and the Active/Inactive SPs are/will be advertised in Beacon frames and therefore can be seen by OBSSs
  We could obviously define rules/recommendations for APs to monitor the Beacon frames from OBSSs
We should also define in UHR negotiation (Request/Response) between OBSSs in order to better coordinate the time sharing between OBSSs
  Incentives here can be for better reliability, but also power save, efficiency, …

## Slide 8: 2) r-TWT to assist/enable C-TDMA/C-OFDMA/C-SR
First interest to consider is that if 2 APs are advertising r-TWTs for themselves and that are overlapping, we increase the chance that there will be an aligned contention period on the 2 APs contention domain
  If the 2 APs are operating on the same primary channel, there is a probability increase that at least one of them will get access to the channel.
  If the 2 APs are operating on the same bandwidth but with different primary channel, the probability increase to access the channel on the wider bandwidth is now considerably increased (see next slide)
  If those 2 APs also intend to apply a coordinated mechanism (C-TDMA, C-OFDMA, C-SR) during the r-TWT SP, they will then both benefit from gaining the TxOP at that time.
    Note that here, the usage of r-TWT SP as an additional tool for C-TDMA/C-FDMA/C-SR is not only for latency-sensitive traffic but also for more general M-AP KPIs like efficiency/throughput, …

## Slide 9: Illustration with a scenario of interest for enterprise
In enterprise scenarios, the fractional frequency reuse concept is a compelling target (among others):
  - Enable Spatial Reuse on entire BW to/from STAs close to the center of the BSSs (where there is less interference from neighbor OBSSs)
  - Do FDMA/OFDMA or TDMA to/from STAs close to the edge of the BSS (where there would be higher interference from neighbhor BSSs): avoid interference

## Slide 10: Illustration with a scenario of interest for enterprise
A typical scenario where we could use FFR is with 2 APs operating on the same BW but with different primary channel
  Different primary channels in order to allow frequency reuse and interference avoidance also in presence of legacy STAs
In such scenario, there are 2 contention domain on the 2 channels and the chances of doing 40 MHz channel access is very limited, which will highly limit AP coordination schemes

## Slide 11: Illustration with a scenario of interest for enterprise
If we ensure start of TxOP (and contention periods) alignment of the 2 BSSs thanks to coordinated rTWTs (advertisement by both APs of an overlapping r-TWT), we then highly increase the chances that channel access is gained on the wide BW for the group of coordinated APs.
We can then define periods of time where M-AP coordination will be possible
We can also easily define periods of time during which C-SR or more advanced coordinated PHY modes on the entire bandwidth will be used, and periods of time where operation will be limited to lower bandwidth for interference avoidance

## Slide 12: 2) r-TWT to assist/enable C-TDMA/C-OFDMA/C-SR
Second interest to consider (more exploratory at this stage) is that we could use r-TWT SPs to configure/schedule the mode of operation during the SP across multiple OBSSs
  Operating BW during the rTWT SP
    for previous FFR example: one rTWT with 20MHz operating BW for interference avoidance (each BSS on its primay channel), one rTWT for 40 MHz operating BW for M-AP reuse (both BSSs on the 40MHz channels)
  Other possible constraints to consider and analyze: limiting SP to DL or UL only, channel access restrictions for APs and STAs, role distributions (Sharing AP/Shared AP), transmit power or PSD limits…
And/or to select the members (STAs) of an rTWT SP to match the purpose of the rTWT SP above
  rTWT ID allowed to be set to 0 to cover all BSS
  To limit membership, with baseline tools or with automatic membership under conditions
    RSSI to serving AP limit, RSSI to OBSS AP, …
    ACs / TIDs / SCSs, …

## Slide 13: Example of time split with rTWT coordination for FFR

## Slide 14: Conclusion
Coordinated rTWT allows
  1) to extend the protection (i.e. increased probability to meet the QoS/latency requirement of some traffic) that r-TWT tool is providing within a BSS to multiple overlapping BSSs. Features needed:
    signaling in rTWT element for OBSS rTWT
    Solution to prevent drifts between rTWT SP
    Negotiation between APs to coordinate rTWT between unmanaged OBSSs
  2) to help other M-AP coordination techniques by increasing the chances of channel access on a wider BW and to define periods for different types of M-AP techniques. Features needed:
    Solution to prevent drifts between rTWT SP
    Feature to explore: Signaling for M-AP operating mode and members selection within rTWT

## Slide 15: SP 1
Do you agree to define a mechanism for an AP to advertise rTWT schedules of an OBSS so that the AP’s associated STAs supporting rTWT follow the rTWT rules for these schedules?

## Slide 16: SP 2
Do you agree to define a negotiation between APs for coordinating their respective rTWT schedules and/or advertising each other’s rTWT schedules?

## Slide 17: Annex

## Slide 18: Illustration of Frequency reuse 7 at 6 GHz
79
47
5935
MHz
111
15
143
175
207
UNII-5
UNII-6
UNII-7
UNII-8
P
P
P
P
P
P
P
Here, we assume that:
we keep frequency reuse 7
Distance between OBSSs is therefore much larger than BSS size
Depending on BSS size and propagation, there could be zones in the BSS where interference between OBSSs needs to be avoided, and zones where interference can be tolerated
As STAs from different OBSSs are quite far away, FDMA will likely be sufficient (compared to OFDMA) in the times where interference needs to be avoided

## Slide 19: Illustration of Frequency reuse 7 (sort of with FFR) at 6 GHz
Here, we assume that:
we keep frequency reuse 7 when operating on regular BW (for legacy or UHR with interference avoidance with OBSSs)
We allow pair of adjacent APs to use a wider bandwidth with M-AP coordination (C-SR, C-BF, JP, …)
In such scenario, the interference between neighbors is obviously larger
160
160
5935
MHz
160
160
160
160
160
UNII-5
UNII-6
UNII-7
UNII-8
P
P
P
P
P
P
P
320
P
320
P