## Slide 1: Discussion on Enhanced R-TWT for UHR
Date: 2023-11-05
Authors:

## Slide 2: Introduction
According to 11bn PAR and CSD [1, 2] , supporting the low latency traffic is one of key features for 11bn TG
IEEE 802.11 be task group also defined the several mechanisms (e.g., R-TWT, EHT SCS, etc.) for supporting the low latency traffic
In this contribution, we propose several methods to enhance R-TWT operation for better supporting low latency traffic

## Slide 3: Recap: EHT R-TWT
R-TWT procedures
  “A non-AP EHT STA with dot11RestrictedTWTOptionImplemented set to true as a TXOP holder shall ensure the TXOP ends before the start time of any active R-TWT SPs that are advertised by its associated AP that does not correspond to a nontransmitted BSSID.”
  “An R-TWT scheduling AP may schedule at most one quiet interval that overlaps with an R-TWT SP”
    To protect a start time of the R-TWT SP from legacy STAs
  “Non-AP EHT STAs may ignore overlapping quiet intervals.”

## Slide 4: EHT R-TWT’s Issues
EHT R-TWT does not consider OBSS’s R-TWT
  In EHT R-TWT, EHT STA considers active R-TWT SPs scheduled by its BSS (considering multiple BSSID set)
  OBSS transmission may still affect the active R-TWT SPs
  To minimize the impact by the OBSS, several contributions were submitted and discussed in UHR SG [3-10]
EHT R-TWT employed the traffic prioritization rather than traffic limit in the SP
  EHT R-TWT can increase more transmission opportunities, but STA can transmit a frame for a TID that is not mapped to R-TWT SP using EDCA  It may result in the delay of latency sensitive traffic
EHT STAs that does not support R-TWT can not end the TXOP before the start of any active R-TWT SPs and can still transmit frames using EDCA in active (trigger-enabled) R-TWT SPs
A member STA can also transmit a frame using EDCA, especially even in trigger-enabled R-TWT SP due to inheritance of the basic TWT rule
Overlapping quiet interval is optional (May not be scheduled)
Although overlapping quiet interval is scheduled, EHT STAs can still ignore the interval
Legacy STA (AP or non-AP) cannot understand new proposed methods

## Slide 5: Enhancing R-TWT for UHR
Consider OBSS [3-11]
  AP can obtain the R-TWT SPs of other APs by receiving frames (e.g., beacon) sent by the other APs and consider the R-TWT SPs in its scheduling
  AP can announce the received SPs to its associated STAs
  If AP or STA associated with the AP obtained the R-TWT SPs of neighbor AP, they will consider the R-TWT SPs
    The AP or STA can end the TXOP before the start of the R-TWT SPs
    The AP can schedule its own R-TWT SPs that does not overlap with the received R-TWT SPs
  AP can request R-TWT SPs to other APs (e.g., wants to get the SP fast or not receive beacon frame with the SP)
  This can reduce the contention in R-TWT SP by OBSS STAs
  However, STAs that don’t support this mechanism or R-TWT will still not consider R-TWT SPs of neighbor APs as well as their associated AP
    E.g., Still try to transmit a frame using EDCA in the R-TWT SP
  Non-member STAs in the same BSSs can still access the channel in R-TWT SP
  Member STAs can also access the channel using EDCA in a trigger-enabled R-TWT SP
  These issues were discussed in 11be TG but has not reached consensus.

## Slide 6: Enhancing R-TWT for UHR
Control in Intra-BSS (1) – Member STA in Trigger-enabled R-TWT SP
  Member STA supporting enhanced R-TWT can access the channel using EDCA in a trigger-enabled R-TWT SP after a specific period
    Note that a member STA can also transmit using EDCA in a Trigger-enabled TWT SP according to existing TWT procedure
  In a trigger-enabled R-TWT SP, AP should transmit at least one Trigger frame during the period if the channel is available
Trigger-enabled R-TWT SP
Period 1
Data
TB PPDU
BA
AP1
STA1
(Member)
STA2
(Member)
Not following a TE TWT SP rule
TF
BA
Trigger-enabled R-TWT SP
TB PPDU
TB PPDU
BA
AP1
STA1
(Member)
STA2
(Member)
Not following a TE TWT SP rule
TF
TB PPDU
TB PPDU
BA
TF

## Slide 7: Enhancing R-TWT for UHR
Control in Intra-BSS (2) – Non-member STA
  Non-member STA supporting enhanced R-TWT can also access the channel using EDCA in a R-TWT SP after a specific period
R-TWT SP
NAV
Period 1
TF
TB PPDU
BA
Beacon
(Period1)
AP1
STA1
(Member)
STA2
(Non-member)
Data

## Slide 8: Enhancing R-TWT for UHR
Control in Intra-BSS (3)
  When an AP receives an initial control frame (e.g., RTS) from non-member STA in R-TWT SP, AP may send a response frame (e.g., CTS) to control the channel access of the STA
R-TWT SP
NAV
RTS
TB PPDU
CTS
Beacon
(Period1)
TF
BA
AP1
Suspension
RTS
Period 1
STA1
(Member)
STA2
(Non-member)
Suspension time

## Slide 9: Enhancing R-TWT for UHR
Control in Intra-BSS (4)
  When AP receives data from non-member STA during non-zero NAV, the AP can also transmit response frame (e.g., BA) to control the channel access of the STA
R-TWT SP
NAV
Data
TB PPDU
Beacon
(Period1)
BA
AP1
Suspension
TF
BA
Period 1
STA1
(Member)
STA2
(Non-member)
Suspension time
Data

## Slide 10: Enhancing R-TWT for UHR
AP may not use the active R-TWT SP
  E.g., the R-TWT SP is occupied by other STAs
In that case, if the AP is affiliated with an AP MLD and another link is available for R-TWT SP, the AP can decide to allocate the R-TWT SP to another link
R-TWT SP 1
New R-TWT SP1
Beacon
(SP1)
AP 1
AP 2
AP MLD
STA 1
STA 2
Non-AP MLD
NAV
New R-TWT SP 1
Link 1
Link 2

## Slide 11: Conclusion
UHR need to improve the R-TWT for better supporting low latency traffic
Enhanced R-TWT operation can consider neighbor BSS’s R-TWT SPs
  AP can get the other AP’s R-TWT SPs by receiving the Beacon frame
  AP can transmit to the other AP a frame requesting R-TWT SPs
Enhanced R-TWT operation can control the channel access in R-TWT SP to reduce the contention in R-TWT SP
  STA supporting Enhanced R-TWT operation may try to access the channel using EDCA in (Trigger-enabled) R-TWT SP a specific time period after the start of the R-TWT SP
  When an AP receives a frame from a STA supporting Enhanced R-TWT during R-TWT SP, AP can send the STA a frame to control the channel access. The STA may suspend the channel access based on the received frame for controlling the channel access
When AP MLD knows that the AP MLD will not be able to use the active R-TWT SP on a link, the AP MLD can allocate the R-TWT SP on the other link

## Slide 12: References
[1] 11bn PAR 23/0078
[2] 11bn CSD 23/0079
[3] 11-23/250, AP coordination with R-TWT
[4] 11-23/291, R-TWT Multi-AP Coordination
[5] 11-23/297, rTWT for Multi-AP
[6] 11-23/355, Enhanced rTWT and MAP operation
[7] 11-23/771, Coordinated R-TWT Protection in Multi-BSS
[8] 11-23/860, Further thoughts on coordinated TWT
[9] 11-23/884, Announcement Procedures for Coordinated TWT
[10] 11-23/1087, Announcement for R-TWT Coordination
[11] 11-23/226, Coordination of R-TWT for Multi-AP Deployment