## Slide 1: DL MU Ext PPDUs
Date: 2024-01-09
Authors:

## Slide 2: Abstract
This submission proposes a mechanism to support OFDMA with legacy STAs

## Slide 3: Problem
Various transmissions have to be non-OFDMA PPDUs on the primary channel
  Beacons (typically 20M, though could be non-HT duplicate)
  Probe responses ( " )
  Broadcasts ( " )
  Transmissions to non-HE STAs (at the max width they support; could be < BSS width)
  etc.
These transmissions can consume a significant fraction of the beacon interval
  Typically at low rates, worsening the issue
The rest of the channel is wasted during these transmissions
Latency is increased as a result of these transmissions

## Slide 4: Solution
Introduce a special form of DL OFDMA, a “DL MU Ext PPDU”
  Transmission on the P20 (or P40 etc.) is a legacy (non-OFDMA) waveform
  Transmission on other subchannels is an OFDMA waveform
    Can also be used for TXOP Sharing Mode 2
  Can also help reduce latency for tx to UHR STAs
Use announcement frame prior to this, a “Non-HE-Primary Announcement”
  Short frame, as inexpensive as protection frame
  Ignored by legacy STAs
  UHR STAs can use this to determine where to listen for the next PPDU
    Announcement frame indicates which UHR STAs are to ignore the primary channel and look elsewhere
    Note no HE/EHT/UHR header on primary channel for DL MU Ext PPDU

## Slide 5: Example
In this example only the P20 is used for the non-HE PPDU, but can be a wider primary
In this example the HE PPDUs are shown as aligned with 20M subchannel boundaries, but can be in any RU

## Slide 6: Operation
AP identifies UHR STAs in active mode that are not interested in the transmission on the primary channel
Data broadcasts typically of interest to all STAs, so don’t use for these
Don’t use for beacons with critical update
Don’t use for short frames
  Time cost of announcement frame outweighs the spectral benefit

## Slide 7: Additional considerations
Announcement frame could indicate whether broadcast frames follow
  But the UHR STAs are in active mode so will receive anyway
Need to ensure no acks to MPDUs in DL MU Ext PPDU while DL MU Ext PPDU still being transmitted
  Could just use ack policy No Ack or Block Ack
  Could allow just one STA to legacy ack
  Could use Trigger frames in DL MU Ext PPDU to allow for UL OFDMA acks
  Could extend announcement frame to also carry trigger information, for UL OFDMA ack after the DL MU Ext PPDU
  If allowing ack, need to pad to align to end of DL MU Ext PPDU

## Slide 8: Straw poll
DL MU Ext PPDUs should be developed as a mechanism to make better use of the channel during transmissions to legacy STAs
Y
N
A

## Slide 9: Backup