## Slide 1: A-MPDU Coexistence Feedback
Date: 2025-04-15
Authors:

## Slide 2: Abstract
This submission proposes a mechanism to mitigate problems with coex during A-MPDU reception
Multi-STA BA enhanced in TGbn, to provide feedback in ICR frame
This proposal enables use of Multi-STA BA in place of BA, to provide rich A-MPDU RX feedback to the AP
This proposal enables an AP to differentiate between real channel errors and failures caused by IDC (at the non-AP STA)

## Slide 3: Problem
A STA might be unable to receive an MPDU in an A-MPDU because of coex issues
If the recipient STA does not ack MPDUs for this reason, the originating STA will typically assume a channel problem and reduce the rate for subsequent transmissions
This worsens the problem, since the consequent increased PPDU duration increases the likelihood of coex collision
In the worst case, the rate is reduced so much that even a single MPDU does not fit between consecutive coex events; as a result data flow stops and the link is dropped

## Slide 4: Solution
Enable the BlockAck frame(s) to carry new information, to help the originator distinguish between coex issues and channel issues
  Coex issues might include hidden node issues, if these can be identified
Specifically, return (feed back to the A-MPDU originator)
  The number of bad A-MPDU subframe headers / bad MPDU FCSes received
    Not caused by Coex
    Can’t be a perfect count of missed MPDUs, since if A-MPDU subframe header is corrupted resync to next header is not guaranteed
    Not counting when didn’t even try to receive, due to coex issues
  The cumulative away time during the PPDU (caused by Coex)

## Slide 5: Possible originator behaviour
If the originator had many MPDUs unacknowledged:
  If the recipient only reported a few bad MPDUs/subframes and a significant cumulative away time, the originator could surmise the recipient was just away due to coex issues for the unacked MPDUs, and use this as a hint not to change the rate
  If the recipient reported many bad MPDUs/subframes, the originator could surmise bad radio conditions, and use this as a hint to rate-adapt
  If the recipient only reported a few bad MPDUs/subframes and a zero or small cumulative away time, or there was no BA, the originator could surmise really bad radio conditions, and use this as a hint to rate-adapt

## Slide 6: AP cannot differentiate errors using only the BlockAck feedback
24/0414 in use:
In all 3 cases:
Internal (in device) Error Occurred bit is 1
Problem: AP might ignore real channel errors
Question: How can AP Link Adaptation work?

## Slide 7: AP gets rich feedback, so it can take correct action
This proposal:
Provide:
bad A-MPDU subframe headers / bad MPDU FCSes
Unavailability duration

## Slide 8: Multi-STA BlockAck
Proposed changes:
Multi-STA BA as a response frame to DL A-MPDU - from non-AP STA to AP
Additional BA information field added to provide new information/ feedback:
Bad MPDU count = bad A-MPDU subframe headers / bad MPDU FCSes
Unavailability duration = time away from DL A-MPDU RX

## Slide 9: Changes required in the TGbn D0.x
Allow Multi-STA BA as response frame to DL A-MPDU (it is already allowed as a control response frame)
Add a new “Feedback Type” value in the Multi-STA BA to allow Multi-STA BA to carry RX (DL A-MPDU) feedback information

## Slide 10: Straw poll
Do you support to define a Multi-STA BlockAck variant that a non-AP STA can use as a response frame to a DL A-MPDU, in order to provide information on bad MPDUs/subframes and cumulative away time for previous PPDU, so that the AP originator can try to distinguish coex issues from channel issues?
Y
N
A

## Slide 11: References
11-24-1247-00 icf-icr-design-for-coex
11-25-0063-00 indication-of-the-unavailability-information-for-idc
11-24-0414 Improving acknowledgment mechanisms