## Slide 1: Bluetooth SIG January 2024 Update
Date: 2024-01-16
Authors:
Notes: September 2012

## Slide 2: Abstract
This is an update on Bluetooth SIG actions and plans for sharing the 5 and 6 GHz bands with incumbents and unlicensed/license-exempt devices.
Notes: September 2012
doc.: IEEE 802.11-09/0301r1
March 2009
        Stephen McCann, RIM
Page 2

## Slide 3: Agenda
Bluetooth Sharing Goals
The Overall Bluetooth SIG Plan
Recent Actions
ETSI BRAN #120 New Work Item; BRAN #123
Bluetooth Next Steps

## Slide 4: Bluetooth Sharing Goals
The Bluetooth SIG recognizes the contribution the Wi-Fi industry has made in opening the 6 GHz band for unlicensed/license-exempt sharing to grow the technology
Today, Bluetooth technology needs to secure its future growth
  The 83.5 MHz of the 2.4 GHz band is not a sufficient hedge against congestion or sufficient to support innovation
Bluetooth and Wi-Fi successfully shared the 2.4 GHz band for many years
  Unfortunately, most of 5 GHz is not viable for Bluetooth, i.e., indoor restrictions and DFS
  5.8 GHz band available in many regulatory domains
  Narrowband technology already deployed in U-NII-3
The 6 GHz band has room for Bluetooth and Wi-Fi, and there is time to develop optimal sharing mechanisms
We will work closely with the Wi-Fi industry in IEEE 802 and Wi-Fi Alliance to enable Bluetooth sharing these band equitably

## Slide 5: The Overall Bluetooth SIG Plan
Create an industry coalition of Bluetooth companies to drive regulatory and standards changes just as Wi-Fi did
  Including companies with both Wi-Fi and Bluetooth businesses
  Collaborate with Wi-Fi industry to drive needed changes
Work with SDOs to develop optimum spectrum sharing methods and advance regulatory/standards to codify them as required
  ETSI BRAN New Work Item adopted in September 2023 (BRAN #120)
The detailed plan can best be developed working together
Now that the FCC has completed the first round of VLP decisions, we are requesting another for narrowband sharing (without geofencing)
  Chairwoman Rosenworcel said there will be a number of additional NPRMs

## Slide 6: FCC 23-86
Second Report and Order
  VLP Power Levels and Protection of Incumbents
  Bluetooth SIG:
    Support Wi-Fi conclusions on VLP power and PSD limits (14 dBm and 1 dBm/MHz); narrowband less likely to cause harmful interference
    CBP for protection of BAS and CARS not a concern for U-NII-5
Second Further Notice of Proposed Rulemaking
  Power Limits for Geofenced VLP Devices in the U-NII-5 through U-NII-8 Bands
  Bluetooth SIG:
    Currently, Bluetooth does not natively have geolocation capability, but can share in multi-radio devices via coordination with GPS
    Narrowband operation may not pose harmful interference threat without geofencing

## Slide 7: FCC 23-86 [2]
Memorandum Opinion and Order on Remand
  NAB request for dedicated 6 GHz spectrum for mobile services
  Bluetooth SIG:
    BAS and CARS only in U-NII-6 and U-NII-8, where Bluetooth has no current interest

## Slide 8: European Commission Directive on VLP Provisions
Note 1: The mean e.i.r.p. refers to the e.i.r.p. during the transmission burst which corresponds to the highest power, if power control is implemented.
Note 2: Narrowband (NB) devices are devices that operate in channel bandwidths below 20 MHz. NB devices also require a frequency hopping mechanism based on at least 15 hop channels to operate at a value of in-band power spectral density (PSD) above 1 dBm/MHz.
Note 3: The appropriateness of this limit shall be subject to review by 31 December 2024. In the absence of justified evidence, a value of -37 dBm/MHz shall apply from 1 January 2025
Techniques to access spectrum and mitigate interference that provide an appropriate level of performance to comply with the essential requirements of Directive 2014/53/EU shall be used. Where relevant techniques are described in harmonised standards or parts thereof the references of which have been published in the Official Journal of the European Union in accordance with Directive 2014/53/EU, performance at least equivalent to the performance level associated with those techniques shall be ensured.
Parameter | Technical Conditions
Permissible operation | Indoors and outdoors. Use on Unmanned Aircraft Systems (UAS) is not permitted
Category of device | The VLP device is a portable device
Frequency band | 5 945-6 425 MHz
Maximum mean e.i.r.p. for in-band emissions (note 1) | 14 dBm
Maximum mean e.i.r.p. density for in-band emissions (note 1) | 1 dBm/MHz
Narrowband usage maximum mean e.i.r.p. density for in-band emissions (note 1) (note 2) | 10 dBm/MHz
Maximum mean e.i.r.p. density for out-of-band emissions below 5 935 MHz (note 1) | - 45 dBm/MHz until 31 December 2024 (note 3)

## Slide 9: ETSI BRAN New Work Item Provisions
(1) To develop a channel access mechanism for Narrowband Frequency Hopping equipment operation
(2) To develop mechanisms enabling LPI client-to-client operations in accordance with ECC/DEC/(20)01 and EC Decision 2021/1067 on 6 GHz WAS/RLANs
(3) To consider further development of FBE and LBE parameters for channel access mechanism
(4) To consider inclusion of new channelization to support next generation technologies (bandwidths exceeding 160 MHz, e. g. 320 MHz)

## Slide 10: Recent Actions
Work on consensus response to FCC 23-86 Second FNPRM
  Referencing the EC Directive and SE45/FM57 conclusions for narrowband VLP
Continued review of sharing simulation results
Began discussion of acceptable limits

## Slide 11: Bluetooth Next Steps
Pursuing FCC FNPRM follow-on for narrowband VLP NPRMs
Participating in and contributing to the ETSI BRAN development of narrowband channel access mechanisms in 6 GHz
  ETSI BRAN #123 February 2024
Exploring enhanced sharing mechanisms for the 5725 – 5850 MHz band
Further regulatory action needed on the 5.8 GHz band globally
  China: Bluetooth type-approval requirements
  Japan: 5.8 GHz band limited by DSRC Road Tolling – can VLP share?