## Slide 1: Further Thoughts on dRU
Date: 2024-01-14
Authors:
Name | Affiliation | Address | Phone | Email
Eunsung Park | LG Electronics | 19, Yangjae-daero 11gil, Seocho-gu, Seoul 137-130, Korea |  | esung.park@lge.com
Dongguk Lim |  |  |  | dongguk.lim@lge.com
Jinyoung Chun |  |  |  | jiny.chun@lge.com
Insik Jung |  |  |  | insik0618.jung@lge.com
Jinsoo Choi |  |  |  | js.choi@lge.com
HanGyu Cho |  |  |  | hg.cho@lge.com

## Slide 2: Introduction
In [1][2], we proposed 160 MHz distribution bandwidth as well as 20 MHz, 40 MHz and 80 MHz distribution bandwidths for dRU
In [1], we also proposed to support dRUs which span a certain channel less than or equal to a bandwidth for a PPDU transmission
  This enables a hybrid PPDU where dRUs and rRUs are used at the same time in a PPDU transmission
In [2], we introduced a multiple dRU (MdRU) concept when a certain channel is punctured for a PPDU transmission
In [3], high level views on dRU including a distribution bandwidth, hybrid PPDU and MdRU were presented
In this contribution, we share our thoughts on the distribution bandwidth, hybrid PPDU and MdRU

## Slide 3: Distribution Bandwidth
We propose to support up to 160 MHz distribution bandwidth
  We expect that 160 MHz may be widely used in 11bn
    Even though 11be mandates the support of up to 80 MHz for non-AP STAs, 160 MHz has been included in the certification program since Wi-Fi 5 (R2)
    160 MHz may become more common along with hardware improvement and thus this support can be mandatory for non-AP STAs in 11bn
  In 160 MHz, various kinds of large dRUs are available with a better transmit power gain resulting in higher throughput
  Although the current PHY processing is based on 80 MHz, 160 MHz processing may be possible by just bypassing the segment parser
    When dRU is used, STAs only have to conduct PHY processing except for the segment parser/deparser
    Impacts on the implementation may be trivial
dRU |  | 26 dRU | 52 dRU | 106 dRU | 242 dRU | 484 dRU | 996 dRU
Gain (dB) | 160 MHz | 11.14 | 11.14 | 11.14 | 8.13 | 5.12 | 2.69
 | 80 MHz | 11.14 | 11.14 | 8.13 | 5.12 | 2.69 | N/A

## Slide 4: Hybrid PPDU (1/2)
We propose to support hybrid PPDU where dRUs and rRUs are used at the same time in a PPDU transmission
  By mixing dRU and rRU in a PPDU, both dRU capable and incapable STAs can be supported at the same time
  In order to enhance flexibility and support 20 MHz operating STAs, various hybrid PPDUs and diverse distribution bandwidths should be considered
    Although it can increase the signaling overhead, by reusing the current RU allocation method based on the dRU mapping rule [4], signaling overhead for dRU allocation can be minimized
    Also, to cope with puncturing cases, 20 MHz and 40 MHz distribution bandwidths are necessary, otherwise we need a 60 MHz dRU tone plan
    In addition, 20 MHz distribution bandwidth is essential, otherwise there is no supporting 20 MHz operating STAs with dRU in the hybrid PPDU
    Furthermore, *small rRUs should be available in the hybrid PPDU for 20 MHz operating STAs incapable of dRU
*Note that in a wider bandwidth TB PPDU, 20 MHz operating STAs do not support 242-tone rRU

## Slide 5: Hybrid PPDU (2/2)
Hence, we recommend the following hybrid PPDU
  40 MHz, 80 MHz, 160 MHz, and 320 MHz hybrid PPDUs are supported
  The minimum distribution bandwidth for dRUs is 20 MHz
    That means rRUs and dRUs are not mixed within 20 MHz at least
  Possible distribution bandwidths for dRUs are as follows depending on the PPDU bandwidth
    40 MHz hybrid PPDU: 20 MHz
    80 MHz hybrid PPDU: 20 MHz and 40 MHz
    160 MHz hybrid PPDU: 20 MHz*, 40 MHz* and 80 MHz
    320 MHz hybrid PPDU: 20 MHz*, 40 MHz*, 80 MHz and 160 MHz
  rRUs are disallowed within channels that dRUs span
    In order words, if a certain channel is used for dRUs and the channel width is equal to the distribution bandwidth for dRUs, no rRUs are allowed within that channel
  Small rRUs are available for 20 MHz operating STAs in a hybrid PPDU
* We are open that these distribution bandwidths are supported only when preamble puncturing is applied

## Slide 6: Multiple dRU (1/2)
We think that MdRU may not be beneficial when dRUs which are distributed in the same channel for a PPDU transmission are aggregated
However, when we combine dRUs which are distributed in different channels within a PPDU bandwidth, data rate can be increased without a loss of transmit power gain
  Especially in a punctured 80 MHz channel, if we don’t define dRUs distributed over 60 MHz channel, MdRU may be much more helpful
  In other cases, it may be better to increase the distribution bandwidth, e.g., instead of using MdRU in 40 MHz + 40 MHz, we can use one large dRU in 80 MHz
    One large dRU can be chosen which data rate and transmit power gain is similar to that of MdRU

## Slide 7: Multiple dRU (2/2)
We propose to combine two dRUs which are distributed in non-punctured 20 MHz and 40 MHz, respectively, in a punctured 80 MHz channel
  To maximize the transmit power gain, two dRUs which have a similar gain can be combined
    Power boosting gain [3]
    E.g., 52 dRU (40 MHz) + 26 dRU (20 MHz), 106 dRU (40 MHz) + 52 dRU (20 MHz), 242 dRU (40 MHz) + 106 dRU (20 MHz)
  We can achieve an increase in data rate while maintaining transmit power gain (or with a sligt decrease in transmit power gain)

## Slide 8: Summary
Up to 160 MHz distribution bandwidths have been proposed for increased transmit power gain and higher data rate
Various kinds of hybrid PPDUs have been proposed to achieve better flexibility and to support 20 MHz operating STAs
How to design MdRU which can increase data rate while maintaining transmit power gain has been proposed in a punctured 80 MHz channel

## Slide 9: Straw Poll #1
Do you agree to add the following text to the TGbn SFD?
  11bn supports 20 MHz, 40 MHz, 80 MHz and 160 MHz distribution bandwidths for dRU in 20 MHz, 40 MHz, 80 MHz and 160 MHz PPDUs, respectively
Y/N/A: //

## Slide 10: Straw Poll #2
Do you agree to add the following text to the TGbn SFD?
  Hybrid PPDU where dRUs and rRUs are used at the same time in a PPDU transmission is supported
  Detailed restrictions and configurations are TBD
Y/N/A: //

## Slide 11: Straw Poll #3
Do you agree to add the following text to the TGbn SFD?
  40 MHz, 80 MHz, 160 MHz, and 320 MHz hybrid PPDUs are supported
  Detailed restrictions and configurations are TBD
Y/N/A: //

## Slide 12: Straw Poll #4
Do you agree to add the following text to the TGbn SFD?
  The minimum distribution bandwidth for dRUs is 20 MHz in a hybrid PPDU
  rRUs and dRUs are not mixed within 20 MHz at least
Y/N/A: //

## Slide 13: Straw Poll #5
Do you agree to add the following text to the TGbn SFD?
  Possible distribution bandwidths for dRUs are as follows depending on the PPDU bandwidth
    40 MHz hybrid PPDU: 20 MHz
    80 MHz hybrid PPDU: 20 MHz and 40 MHz
    160 MHz hybrid PPDU: 20 MHz, 40 MHz and 80 MHz
    320 MHz hybrid PPDU: 20 MHz, 40 MHz, 80 MHz and 160 MHz
    In 160 MHz and 320 MHz hybrid PPDUs, 20 MHz and 40 MHz distribution bandwidths are used in a 80 MHz channel only when 20 MHz preamble puncturing is applied to that channel
  rRUs are disallowed within channels that dRUs span
    In order words, if a certain channel is used for dRUs and the channel width is equal to the distribution bandwidth, no rRUs are allowed within that channel
Y/N/A: //

## Slide 14: Straw Poll #6
Do you agree to add the following text to the TGbn SFD?
  Small rRUs are supported for 20 MHz operating STAs in a hybrid PPDU
  Exact set of supported small rRUs are TBD
Y/N/A: //

## Slide 15: Straw Poll #7
Do you agree to add the following text to the TGbn SFD?
  Multiple dRUs are defined by combining two dRUs which are distributed in non-punctured 20 MHz and 40 MHz, respectively, in a punctured 80 MHz channel
  Detailed combinations are TBD
Y/N/A: //

## Slide 16: Straw Poll #8
Do you agree to add the following text to the TGbn SFD?
  The following Multiple dRUs are supported in a punctured 80 MHz channel
    52 dRU (from non-punctured 40 MHz) + 26 dRU (from non-punctured 20 MHz)
    106 dRU (from non-punctured 40 MHz) + 52 dRU (from non-punctured 20 MHz)
    242 dRU (from non-punctured 40 MHz) + 106 dRU (from non-punctured 20 MHz)
  Detailed tone plan for dRU is TBD
  Whether to support Multiple dRUs for punctured 160 MHz is TBD
Y/N/A: //

## Slide 17: References
[1] 11-23-1919-00-00bn-dru-proposal-for-tgbn
[2] 11-23-1448-00-0uhr-further-considerations-on-dru
[3] 11-23-2020-00-00bn-high-level-perspective-on-distributed-tone-ru-for-11bn
[4] 11-23-1117-00-0uhr-dru-signaling-for-uhr