## Slide 1: DPWiFi MATLAB Validation
Date: 2024-01-18
Authors:

## Slide 2: Abstract
During last November’s plenary TWI proposed “Dynamic Polarization MIMO Multiplexing and Beamforming” as a candidate PHY for the nascent TGbn standard. TWI has since MATLAB-modelled “DPWiFi” for the Fixed Wireless Access application, and key findings are summarized herein.

## Slide 3
Why DPWiFi for TGbe?
The P802.11bn PAR states that the defining TGbn Ultra High Reliability MAC/ PHY requires one operating mode exhibiting at least 25% higher throughput than the TGbe Extremely High Throughput MAC/PHY.
In a DLOS channel, the EHT maximum Data Rate (MCS13, 320 MHz, 800 ns GI, 1 Stream) corresponds to 2.882 Gbps, while the proposed DPWiFi peak Data Rate (MCS13, 320 MHz, 800 ns GI, 32 Streams) clocks at 92.224 Gbps. So, DPWiFi DLOS operation would deliver 3200% higher throughput than TGbe.
Furthermore, the relative DLOS RvR enhancement benefits further from the Ns-dependent extended range (= 10^[(10 log Ns)/20] = 5.65 for 32 Streams) begat of the TWI candidate UHR’s innate Beamforming gain. So, DPWiFi DLOS operation would deliver 18,080% higher Rate vs Range than TGbe.

## Slide 4: Proposed DPWiFi PHY
32 IEEE802.11be concurrent, cochannel RF streams
  32x32 MIMO Dynamic Polarization Multiplexing (“DP-32”)
  32x32 MIMO Tx/Rx DLOS/ nLOS/ NLOS Beamforming/Beamsteering
  AP MU-MIMO Tx Multi-beaming
  AP, Client MU-MIMO Rx Interference Cancellation
  Client MU-MIMO Rx NLOS Multipath Recombination
  5-7 GHz UNII Operation
  4096 QAM 5/6
  320 MHz BW
  92.2 Gbps Peak Data Rate
  80 GbE P2P Throughput, 28 km Free-Space Range
  27 GbE PMP Throughput, 79 km2 Foliage-obstructed Coverage

## Slide 5
Proposed DPWiFi TRX Architecture
Post-Honolulu refinements
[HDP] DPWiFi Propagation Channel
[HDP-1] DPWiFi Rx PDMX
1

## Slide 6: DPWiFi for Fixed Wireless Access
The Fixed WiFi Access Propagation Channel
  FWA propagation channel [HDP] is an n-dimensional “Polarization Space”, with an upper bounded n >> 32
  [HDP] is non-singular, deterministic and scalar (i.e., hij = 1, i = j; hij = r, i ≠ j) r (also the “Channel Dynamic Polarization Index” or “ChDPI”) varies with [HDP] impairments
  FWA comprises DLOS, nLOS and NLOS links, all susceptible to distinct “depolarization” [HDP] impairments Channel Depolarization (“ChDp”, o) is propagation-induced angular Rx signal polarization rotation wrt the Tx-impressed baseline
    Direct Line of Sight TRXs experiencing atmospheric fog, rain, etc. encounter up to 5o [HDP] depolarization
    near Line of Sight TRXs partially obstructed by foliage, landscape or structures face up to 15o [HDP] depolarization
    Non Line of Sight TRX channels enduring reflection/diffraction by landscape, structures or vehicles depolarize [HDP] by up to 45o
  Increasing ChDp soon overwhelms a DPWiFi Rx PDMux, precluding full co-channel self-interference cancellation
    Already severe depolarization consequences magnify even further with increasing DPWiFi link MCS and MIMO order
    DPWiFi MUST incorporate channel depolarization mitigation (i.e., the receiver PDMux “RxDPI” needs track the [HDP] ChDPI)
Ergo, a 2-step Fixed Wireless Access “Adaptive DPWiFi”:
  FWA (Open Loop) Channel Sounding
    FWA AP transmits [HDP]-characterizing “Training Packets (T)” every ~1ms to all associated STAs
    Each FWA STA processes T, estimates ChDp, determines true [HDP], computes its [HDP-1] and reconfigures its Rx PDMux to match
  FWA TRX DPWiFi TRX as Honolulu-proposed, but with Rx PDMux RxDPI precisely tracking the constantly sampled ChDPI

## Slide 7: DPWiFi TRX Validation Plan
Note: See corresponding Validation Test results following

## Slide 8
DPWiFi TRX MATLAB Model
Data Source Generates
1x Training Packet/
1x Data Packet
SPC/Modulators Synthesize
1x Training Stream/
32x Symbol Streams
Tx DPAs Walsh-Polarize
1x Training Stream/
32x Symbol Streams
DPWiFi Channel MIMO-Multiplexes
1x Training Stream/
32x Symbol Streams
Rx DPAs De-correlate
32x M-M Training Streams/
32x M-M Symbol Streams
Rx DPDMux Estimates Channel DPI/
Recovers 32x Symbol Streams
Demodulators/PSC Recover 1x Data Packet
Data Sink Accepts 1x Data Packet

## Slide 9
DPWiFi TRX MATLAB Model Detail

## Slide 10: DPWiFi TRX Validation
TWI is currently executing the entire DPWiFi TRX Validation Plan of Slide 6
However, the key “Will DPWiFi work for FWA?” question has already been settled:
  Validation Plan items 1.15 and 2.15 comprise the most extreme DPWiFi-for-FWA corner case
    That is, if DPWiFi-32 320 MHz MCS13 works subjected to the full range of channel impairments, then ALL OTHER DPWiFi MIMO order, bandwidth and MCS combinations will ALSO work
    TWI HAS completed items 1.15/2.15 DP-32 320 MHz MCS13 MATLAB modeling, as summarized below
DPWiFi-32 320 MHz MCS13 TRX MATLAB Simulink Model

## Slide 11: DPWiFi TRX Modeling
1. DPWiFi TRX Simulations
1.1 DPWiFi-32 320 MHz MCS13, ChDp = 0.0o

## Slide 12: DPWiFi TRX Modeling
1.2 DPWiFi-32 320 MHz MCS13, ChDp = 1.0o

## Slide 13: DPWiFi TRX Modeling
1.3 DPWiFi-32 320 MHz MCS13, ChDp = 1.1o

## Slide 14: DPWiFi TRX Modeling
1.4 DPWiFi-32 320MHz MCS13, ChDp = 5.0o

## Slide 15: DPWiFi TRX Modeling
1.5 DPWiFi-32 320 MHz MCS13, ChDp = 15.0o

## Slide 16: DPWiFi TRX Modeling
1.6 DPWiFi-32 320 MHz MCS13, ChDp = 45.0o

## Slide 17
DPWiFi TRX Modeling- Salient Observations
DPWiFi TRX Modeling- Analysis 3.1 DPWiFi is tremendously sensitive to propagation channel depolarization, as even slight fog could crash an FWA link 3.2 Adaptive DPWiFi, however, comprehensively mitigates any amount of channel depolarization
4. DPWiFi TRX Modeling- Conclusions Adaptive DPWiFi (henceforth just “DPWiFi”) represents both an extraordinarily powerful and robust TGbn Fixed Wireless Access solution
DPWiFi TRX Modeling Observations, Analysis and Conclusions
DPWiFi TRX Performance in Impaired Propagation Channels DPWiFi-32 320 MHz MCS13 vs Channel Depolarization |  |  |  |  |  | 
Channel Impairment Depolarization Angle | None 0.0o | Heavy Mist 1.0o | Slight Fog 1.1o | Heavy Rain 5.0o | Rain + Foliage 15.0o | Orthogonal Reflection 45.0o
Channel DP Index | 0.5016 | 0.5087 | 0.5095 | 0.5417 | 0.6124 | 0.7071
Uncompensated TRX BER | 0.000 | 0.000 | 0.003 | 0.195 | 0.315 | 0.376
Compensated TRX BER | 0.000 | 0.000 | 0.000 | 0.000 | 0.000 | 0.000

## Slide 18
DPWiFi MATLAB Validation Summary
Granted that comprehensive modeling results are still pending, the fully completed corner-case MATLAB simulations (results presented herein) nevertheless conclusively validate TWI’s unprecedented and extraordinary DPWiFi performance claims. DPWiFi thereby fully merits enthusiastic, unqualified endorsement for adoption as a TGbn PHY.

## Slide 19: References
1. 23/1606r1 Dynamic Polarization Multiplexing and Beamforming WLANs Carlos A Rios (Terabit Wireless Internet), 13-Sep-2023
23/1756r3 MIMO Dynamic Polarization and Beamforming: Proposed IEEE802.11bn PHY Carlos A Rios (Terabit Wireless Internet), 16-Nov-2023