## Slide 1: Relay Operation Follow-up
Date: 2023-12-08
Authors:

## Slide 2: Introduction
A potential relay architecture is proposed in [1], i.e. the relay AP is advertised as an affiliated AP of the AP MLD.
Under this relay architecture, the non-AP MLD can use the link reconfiguration to flexibly add or remove the relay link with its mobility.
In this presentation, we shows some updates since the last presentation.
  Support the legacy client’s association

## Slide 3: Recap Non-colocated AP MLD for seamless roaming
Considering the Link ID space (4 bits in length) is not enough, the following non-colocated AP MLD architecture for the seamless roaming is proposed.
  Each link can be identified with colocated MLD MAC address (or a newly defined colocated ID) plus link ID.
    The EHT non-AP MLD only can associate with the colocated AP MLD.
    The UHR non-AP MLD can associate with either the colocated AP MLD or the non-colocated AP MLD, which depends on whether the UHR non-AP MLD has the need of roaming.

## Slide 4: Relay architecture
Each relay device consists of a relay STA (or named backhaul STA) and a relay AP.
  Case 1. The relay AP can share a common radio with the relay STA and operates on the same channel.
    In this case, the TXS mechanism may be used to improve the channel access.
    Note. Based on the current 11be draft, the non-AP MLD is not allowed to simultaneously establish link 1 and link 2.
  Case 2. The relay AP and the relay STA may use different radios and are deployed on different channels.
architecture
MLD upper MAC
AP 0
(2.4 GHz)
AP 1
(5 GHz)
Relay function
Relay device
Relay STA
Relay AP
(AP 2)
architecture
MLD upper MAC
Non-AP MLD
STA 0
STA 1
(Direct) link 0
(Direct) link 1
(Relay) link 2
AP MLD
Backhaul link
STA 2

## Slide 5: Relay architecture (Cont.)
In this scenario, the relay AP is advertised as an affiliated AP. From this point of view, the architecture is also a kind of non-colocated AP MLD.
Compared with the previous non-colocated AP MLD architecture (for the enterprise scenario), there are two following main differences
  No need to advertise the existence of another (non-collocated) AP MLD which is build on the top of the current colocated AP MLD. Because 15 links are enough for this relay scenario.
  The interface between the MLD upper MAC sublayer and the MLD lower MAC sublayer is wireless.

## Slide 6: Relay architecture (Cont.)
The benefit of this proposed two-level non-colocated AP MLD architecture is it can be transparent to the EHT non-AP MLD. Thus the EHT non-AP MLD can associate with this (non-colocated) AP MLD.
  At most support 15 links.
MLD upper MAC
AP 0
(2.4 GHz)
AP 1
(5 GHz)
AP MLD
AP 2
(2.4 GHz)
AP 3
(5 GHz)
Relay/Backhaul STA
AP 4
(2.4 GHz)
AP 5
(5 GHz)
Relay/Backhaul STA
Note. The pre-EHT STA still associates with the affiliated AP. So the affiliated AP has the full legacy AP function which is not in shown in this figure.
Level 2: (non-colocated) AP MLD
Level 1: Affiliated AP

## Slide 7: Discovery of relay AP
First, the relay STA initiates the association with the AP MLD.
  Meanwhile, the profile of the relay AP is included within a newly defined element of the Association Request frame, e.g.
    Operating class, channel number
    BSSID, Beacon interval, TSF, DTIM info
    Indicates whether the STA is power constrained or not
    …
After the relay STA successfully associates with AP MLD, then the AP MLD will start advertising the existence of AP 2 (i.e. relay AP) affiliated with the AP MLD through the RNR element in the Beacon frame and the Basic Multi-link element in the Probe Response frame.
  Which exactly follows the current 11be draft.

## Slide 8: Relay link setup procedure
Assuming that the non-AP MLD has established link 0 and/or link 1 with the AP MLD, the relay link setup procedure is shown as the right figure.
  Step 0. The AP MLD sends a Beacon Request to inform the non-AP MLD to do the measurement on the RSSI of the relay AP.
  Step 1. The AP MLD sends a Link Reconfiguration Notify frame to recommend the non-AP MLD to establish the relay link based on the received Beacon Report.
  Step 2. The non-AP MLD exchanges Link Reconfiguration Request/Response frames with the AP MLD through one of direct links to establish the relay link.
Non-AP MLD
AP MLD
Relay AP
Beacon Request
Beacon Report
Link Reconfiguration Notify
Link Reconfiguration Request
Link Reconfiguration Response
Link Reconfiguration
UL transmission
(switch to awake state)
Non-colocated AP MLD

## Slide 9: Summary
The proposed relay architecture can be used for the coverage expansion and the seamless roaming for the home scenario.
  Which can be transparent to the EHT non-AP MLD.
For this proposed relay architecture, we have discussed the following operation details, including
  Discovery of relay AP
  Relay link setup procedure

## Slide 10: References
[1] Guogang Huang et al., IEEE 802.11-23/1899r0 Relay operation for 11bn
[2] Guogang Huang et al., IEEE 802.11-23/231r0 Thoughts on Seamless Roaming Under the Non-collocated AP MLD Architecture
[3] Duncan et al., IEEE 802.11-23/1910r3 Seamless Roaming for UHR
[4] Liwen et al., IEEE 802.11-23/1937r0 Seamless Roaming Follow-up: Procedure and Signalling